## Slide 1
Example Exercise introduction to Renewable energy systems

## Slide 2
Exercise: Case study – Your country: PV, Wind & Biomass
Objective: Size an energy mix that delivers 1.0 TWh/a of electricity and 200 GWhth/a of heat; estimate simple costs and CO2 abatement.
What to submit (1 page):
Sizing results
Simple cost metrics (€/kWh)
CO2 abatement
2 barriers & 2 opportunities for your country.
*CO2 abatement: Actions, strategies, and technologies used to reduce or prevent the release of carbon dioxide (CO2) and other greenhouse gases into the atmosphere.

## Slide 3
Exercise: Case study – PV, Wind & Biomass
Data given
Units: 1 kWh=3.6 MJ; 1 y=8760 h
Targets:
  Electricity 1.0 TWh/a
  Heat 200 GWhth/a
Baseline Emission factors (EF):
  Electricity Grid electricity (oil‑shale/coal dominated) 1.0 kgCO2/kWh_e
  Heat Gas 0.20 kgCO2/kWh_th
  Biomass stack CO2≈0 (biogenic)
PV:
  FLH=1,000 h/a
  PR=0.80 → 800 kWh/kWp·a
  Capex 900 €/kWp
  O&M 1.5%/a
  Life 25
  CRF25=0.078
Wind (onshore, 2 MW class):
  CF=0.35
  Capex 1400 €/kW
  O&M 50000 €/turbine·a
  Life 20 y
  CRF20=0.087
Biomass (chips, 20% moisture):
  LHV=14 MJ/kg≈3.89 kWh/kg
  Boiler η=0.85
  CHP split: 25% elect / 55% heat / 80% total.
  Fuel cost 25 €/MWh_fuel
  Capex: CHP 2500 €/kWe or Boiler 500 €/kWth
  O&M 4%/a
  Life 20 y
  CRF20=0.087
Abbreviations
EF Emission Factor (kg CO₂ per kWh of energy delivered)
EEE Energy (kWh or MWh/GWh/TWh per year)
PPP Power/Capacity (kW, MW)
FLH Full-Load Hours (h/a)
PR Performance Ratio (unitless, PV losses)
CF Capacity Factor (unitless, wind)
LHV Lower Heating Value (MJ/kg or kWh/kg, biomass fuel)
O&M Operation & Maintenance (€/a or % of capex per year)
Capex Capital expenditure (€, €/kW, €/kWp)
CRF Capital Recovery Factor (used to annualize capex)
t CO2 / kt / Mt tonnes / kilotonnes / megatonnes of CO2

## Slide 4
Exercise: Case study – PV, Wind & Biomass
STEP by STEP
Electricity mix (choose A or B) A: 60% wind / 40% PV; B: 40% wind / 60% PV. a) Set energy targets:
E_wind_target = share_wind * 1.0 TWh (convert to kWh)
E_PV_target = share_PV * 1.0 TWh (convert to kWh)
b) PV capacity from its annual yield.
Y_pv: 800 kWh/kWpa
P_dc (kWp) = E_PV_target (kWh) / Y_pv (kWh/kWp·a). MWp = kWp/1,000
c) Wind capacity and number of turbines required
Y_wind (kWh/kWa)​=CF*tyear(h)​
P_w (kW) = E_wind_target (kWh) / Y_wind (kWh/kWa)
#turbines = P_w / 2,000 (kW).
Y_wind: Wind turbine specific yield
CF: 0.35 is the capacity factor, the fraction of time the turbine effectively produces power at full capacity. A 35% capacity factor is realistic for a good onshore site.
tyear: 8760 h Number of hours in one year (365 × 24).
Y_pv: Wind turbine specific yield
How is this obtained?
Solar insolation (annual global horizontal irradiance, adjusted for tilt, location, and weather).
PV system efficiency and performance ratio (losses due to inverter, wiring, temperature, etc.).
For Estonia or similar northern climates, that works out to about 800 kWh per installed kWp per year.

## Slide 5
Exercise: Case study – PV, Wind & Biomass
STEP by STEP
2) District heat with biomass (choose Boiler or CHP): target 200 GWhth/a. Boiler path (heat only): a) Fuel energy:
E_fuel = E_heat (GWth/a) / η_boiler, (convert to kWh)
b) Biomass mass (t/a):
mass = (E_fuel (kWh) / LHV (kWh/kg)) / 1,000 (kg/t) c) Boiler size (kW_th):
from peak/operating hours (use 4,500 h/a).
Pth = E_heat (kWth/a)/Operaitng hours (h) CHP path (25% electricity / 55% heat): a) Heat: E_h = 200 = Share of heat × E_fuel. b) Electricity: E_e = Share of electricity × E_fuel
kW_e ≈ E_e / 8,000 (h/a), assuming operation of 8000 hours per year c) A biomass CHP needs flue-gas cleanup, ash disposal or reuse must be considered. In cost/LCOE calculations, you can credit the heat (e.g. assume heat is worth 35 €/MWhth) to reduce the “effective cost” of electricity.

## Slide 6
Exercise: Case study – PV, Wind & Biomass
STEP by STEP
3) Simple costs, Annualized Capex = Capex × CRF. PV:
Capex = P_dc(kWp) × 900 (€/kWp)
O&M = 1.5% Capex
LCOE_PV ≈ (AnnCapex + O&M)/E_PV Wind:
Capex = P_w(kW) × 1400 (€/kW)
O&M = 50000 × #turbines
LCOE_wind ≈ (AnnCapex + O&M)/E_wind Biomass heat (boiler):
Capex = P_th (kWth) × 500 (€/kWth)
O&M = 4% Capex
Fuel = E_fuel(MWh) × 25 €/MWh
Cost_heat ≈ (AnnCapex + O&M + Fuel)/E_heat. Biomass CHP:
Capex = kW_e × 2,500 (€/kWe)
O&M = 4% Capex
Fuel = as above
LCOE_e with heat credit: ((AnnCapex + O&M + Fuel) − (35 €/MWh_th × E_h)) / E_e
LCOE = Levelized Cost of Electricity (€/kWh) It tells the average cost of producing 1 kWh of electricity over the whole lifetime of a plant, including investment, maintenance, and fuel.

## Slide 7
Exercise: Case study – PV, Wind & Biomass
STEP by STEP
4) CO2 abatement. calculate how much CO2 emissions are avoided (abated) if Estonia uses renewables (PV, wind, biomass) instead of fossil baselines.
Electricity:
Abated CO2_e​=(EF_baseline​−EF_renewable​)×(E_PV​+E_wind​)
PV and wind have ≈ 0 direct CO₂ emission
Abated CO2_e = (1.0 − ~0) kg/kWh × (E_PV + E_wind) → convert to MtCO2/a Heat:
Biomass:biogenic CO2 = 0 (because trees reabsorb CO₂ during growth). But: upstream impacts (logging, transport, soil carbon, NOₓ/PM emissions).
Abated CO2_th​= (EF_gas,th​−EF_biomass​)×E_heat​
Abated CO2_th​= 0.20 kg/kWh_th × 200 GWh → convert to MtCO2/a

## Slide 8
Exercise: Case study – PV, Wind & Biomass
Report (max 1 page)
Mix selection: A (60% wind / 40% PV) or B (40% wind / 60% PV)
Electricity split (GWh/a): Wind = … ; PV = …
PV: Capacity … MWp ; Annual energy … GWh/a
Wind: … # turbines (2 MW each, … MW total) ; Annual energy … GWh/a
Biomass (Boiler/CHP): • Fuel required … t/a • Plant size … MWth / MWe • Annual output: Heat … GWhth/a [Electricity … GWhe/a if CHP]
Costs: • PV LCOE … €/MWh • Wind LCOE … €/MWh • Biomass cost … €/MWhth (boiler) / €/MWh (CHP) • Weighted electricity mix LCOE … €/MWh
CO₂ abatement: • Electricity … tCO₂/a • Heat … tCO₂/a • Total … tCO₂/a
Barriers (your country):
Opportunities (your country):