## Slide 1
SOLAR energy
14.02.2025
Mais Baqain Ph.D.;
Mais.Baqain@taltech.ee
Prof Alar Konist, Ph.D.

## Slide 2
Content:
Introduction: PV Technology, history and how PV cells work
Doping of Silicon : positive (p) and negative (n) layers
Equivalent circuit of the solar cell and characteristic curve
PV Systems: off-grid and on-grid

## Slide 3
Photovoltaic Technology
Photovoltaic (PV) is the technology of converting light directly to electrical energy (photo = light, voltaic = electricity).
Commonly known as “solar cells.”
The simplest systems power the small calculators we use every day. More complicated systems will provide a large portion of the electricity in the near future.
PV represents one of the most promising means of maintaining our energy intensive standard of living while not contributing to global warming and pollution.
[The energy report
100% renewable energy by 2050]
Notes: Photovoltaics (PV) is the conversion of light into electricity using semiconducting materials
Photovoltaic converters are semiconductor devices that convert part of the incident solar radiation directly into electrical energy.
Massively growing tech. In 2019, worldwide installed PV capacity increased to more than 635 gigawatts (GW) covering approximately two percent of global electricity demand.[10] After hydro and wind powers, PV is the third renewable energy source in terms of global capacity.

## Slide 4
History
1839 – photovoltaic effect first recognized 1883 – first solar cell created
1946 – modern pn junction solar cell
1954 – doped silicon first used in solar cells 1958 – first spacecraft to use solar panels 1970 – GaAs solar cells created
1989 – first dual junction cell created
1993 – first dual junction cells for spacecraft 1995 – 30% efficiency barrier broken
2004 – terrestrial solar cell production exceeds 1 GW 2009 – 40% efficiency barrier broken
[ NREL Feb. 2010]
Notes: A brief history of photovoltaics is presented by Wolf (1981).
An early public demonstration of solar cells occurred in 1955 in Georgia, where a small panel of experimental silicon cells provided energy to charge a battery and power telephone equipment.
Since then, tremendous progress has been made in the development of cell technology and applications. Early hand-made cells were 5% efficient, were 1 or 2 cm2 in area, and had outputs of a few milliwatts. In recent years laboratory cells have been reported with efficiencies of over 30%, modules (groups of cells) are being manufactured with areas of many square meters, and the cells produced in the world in 2011 had an aggregate peak generating capacity of over 70 GW with the cumulative installed capacity of over 185 GW.

## Slide 5
Application of solar energy
Link
1954 Bell Labs
1958 Vanguard 1
1963 Sharp 242W PV station
1966 1kW stationNASA
80s consumer small appliances

## Slide 6
How PV elements work
PV cells use a physical phenomenon called the photoelectric effect to produce electricity. This was first described by Heinrich Hartz
1887 This effect was described in detail1905 a. Albert Einstein Nobel Prize.
Simply put, they are materials that produce electricity when exposed to light. Some electrons (so-called photoelectrons) are detached from their atoms by light. If we attach an electrically conductive material to the plus and minus sides of the photovoltaic material, we create a circuit and can control the electricity generated.
The first PV element was manufactured Bell Labs more than 50 years ago. The first real use of PV panels in the aerospace industry was to provide power to satellites.
[EPEA]
Notes: materials that produce electricity when exposed to light. Some electrons (so-called photoelectrons) are detached from their atoms by light. If we attach an electrically conductive material to the plus and minus sides of the photovoltaic material, we create a circuit and can control the electricity generated.

## Slide 7
How PV elements work
When Light Strikes Silicon
When light shines on a crystal of pure silicon, particles called "electrons" are ejected from silicon atoms and move about the crystal somewhat randomly.
The place the electron came from is called a "hole'. It takes energy from the light to eject the electron from its normal resting place,
Energy is released when the electron returns to an atom that is missing an electron, and recombines with a hole.

## Slide 8
fuel of solar PV cells
Solar Cell
Electrical power once a Load is connected
(Type: DC)
Sun Rays
Power (P) [W] = Voltage (V) [V] x Current (I) [A]
[W/m2]
voltage
current
Incident Solar Irradiance (Instantaneous Power Density)
200
1000
+
-
Solar Radiation
intermittent
Solar cells are rated at 1000 W/m2
V
I
[SIT-winter workshop, lecture slides “Photovoltaics”, Dr. Firas Alawneh]

## Slide 9
Photon Energy
Notes: Photon energy is the energy carried by a single photon. The amount of energy is directly proportional to the photon's electromagnetic frequency and thus, equivalently, is inversely proportional to the wavelength. The higher the photon's frequency, the higher its energy. Equivalently, the longer the photon's wavelength, the lower its energy.

## Slide 10
fuel of solar PV cells
PV is the direct conversion of sunlight to electricity

## Slide 11
Semiconductors
Solar cells are fabricated using semiconductors.
Semiconductors are made from crystal and can act as conductors or insulators in different circumstances, according to the amount of energy that is given to the material.
Silicon is the most common semiconductor crystal.
Silicon
Notes: Semiconductors are materials which have a conductivity between conductors (generally metals) and nonconductors or insulators (such as most ceramics). Semiconductors can be pure elements, such as silicon or germanium, or compounds such as gallium arsenide or cadmium selenide.

## Slide 12
Silicon Chemical Properties
Melting Point: 1410 ºC
Boiling Point: 2355 ºC
Notes: Silicon is a chemical element with the symbol Si and atomic number 14. It is a hard, brittle crystalline solid with a blue-grey metallic color, and is a tetravalent metalloid with four electrons available for covalent chemical bonding in its valence and semiconductor
Its melting and boiling points of 1414 °C the second highest among all the metalloids and nonmetals,.

## Slide 13
Energy Bands for Materials
Conduction Band
Valence Band
Conduction Band
Valence Band
Metal Semiconductor
Eg
Conduction Band
Valence Band
Insulator
Eg
E
Photon
E = hc/λ
e -
Element | Eg (eV)
Silicon | 1.14
Germanium | 0.67
Tin | 0.1
Copper | 0
All at 20ºC
The semiconductors in general lies between metal and insulator properties, it needs a small energy related to insulator to be in conduction band.
[GJU, lecture slides “Photovoltaics”, Dr. Mohammad Al-addous]
Notes: Energy band theory explains the interaction of electrons between the outermost shell and the innermost shell. Based on the energy band theory, there are three different energy bands: Valence band. Forbidden energy gap. Conduction band.
the electronic band structure (or simply band structure) of a solid describes the range of energy levels that electrons may have within it, as well as the ranges of energy that they may not have (called band gaps or forbidden bands).

## Slide 14
From sand to silicon solar cells
[GJU, lecture slides “Photovoltaics”, Dr. Mohammad Al-addous]
Notes: Silicon is the eighth most common element in the universe by mass, but very rarely occurs as the pure element in the Earth's crust.

## Slide 15
PV CELLS MANUFACTURING
Virtually all mono-crystalline and poly-crystalline silicon wafer manufacturers apply the described technology as a standard technology. Cells manufactured as mono-crystalline silicon wafers based on the Czochralski process allow achievement of efficiencies from 14 to 18 %, while the efficiencies of poly Crystalline wafers stretch from approximately 13 to 15.5 %. Thus, the described process sequence is a compromise between a simple and cost-efficient process design and wafer materials on the one hand, and minimised efficiency losses due to simplicity, on the other.
[Renewable Energy Technology, and Environment Martin Kaltschmitt, 2007]

## Slide 16
Mono-crystalline vs. Poly-crystalline Silicon
There are two types of crystalline silicon depending on its purity and crystals orientation obtained during the crystal growth process:
Poly-crystalline: Non-uniform crystals orientation
Mono-crystalline: Uniform crystals orientation (purer and more expensive and efficient) The mono-crystalline silicon ingots are prepared by the exacting Czochralski (CZ) crystal growth process (crystal pulling). While the poly-crystalline silicon ingots are prepared by a simpler casting (or, more generally, directional solidification).
CZ Crystallization Method
Mono
c-Si
Si liquid
seed
Simple Crystallization
Insulation
Electric Heaters
Poly c-Si
Si liquid
CZ process is a method of crystal growth used to obtain single crystals of semiconductors.
Notes: The mono-crystalline silicon ingots are prepared by the crystal growth process (crystal pulling).
Silicon (Si) is first melted and then allowed to freeze into a crystalline state in a controlled manner. The advantage of this method is that it is fast and highly controllable.
The almost perfect crystal structure yields the highest light-to-electricity conversion efficiency for silicon.

## Slide 17
How to distinguish between polycrystalline and monocrystalline silicon solar cells by visual inspection?
Link
Non-uniform appearance
uniform appearance

## Slide 18
Creation of a depletion layer
[Renewable Energy Technology, and Environment Martin Kaltschmitt, 2007]

## Slide 19
Photosensitivity?
e-+
e-+
e-+
e-+
Notes: electrons freed and energized by photons will wander for a short time and then recombine with a wandering hole. The energy originally transferred to the electron from the photon is simply lost as heat. The key to producing usable output current is to sweep the freed electrons out of the material before they recombine with holes.

## Slide 20
P-N junction
[Renewable Energy Technology, and Environment Martin Kaltschmitt, 2007]

## Slide 21
The response of the silicon due to the incident Photons
e-
e-
e+
e+
e-
e-
e+
e+
Conclusion: we have to reengineer the material, so that
we can separate t (e⁻) freo- m thee+ eh- oles(e⁺) to
e+
prevent the recombination inside the material.

## Slide 22
Solar Cell Parts
(n+) & (p+) diffusions (heavily doped siliconc to behave as a conductor) used to connect the layers with the metal to decrease the series resistance.
The top metal grid
N layer
P layer
Bottom metal
[GJU, lecture slides “Photovoltaics”, Dr. Mohammad Al-addous]

## Slide 23
Structure of solar cell
[Renewable Energy Technology, and Environment Martin Kaltschmitt, 2007]
P-N Junction
https://www.youtube.com/watch?v=ar7xDMR4P_U

## Slide 24
What is Doping?
Answer: Adding foreign atoms to the silicon crystal to produce negative or positive free charge carries (electrons or holes).
Answer: As mentioned before, electrons freed and energized by photons will wander for a short time and then recombine with a wandering hole. The energy originally transferred to the electron from the photon is simply lost as heat. The key to producing usable output current is to sweep the freed electrons out of the material before they recombine with holes.
Why Doping?

## Slide 25
The P-type silicon
The silicon atom creates four covalent bonds with other neighboring atoms in the pure silicon crystal.
When the crystal is doped with Boron atoms, the silicon will make three covalent bonds with it with the forth bond missing, which represents a hole (e+), so this type of semiconductor is called P-type.
This hole is waiting for a free electron to fill its location to create the forth bond, so the impurity atoms then is referred to it as acceptor atoms.

## Slide 26
The N-type silicon
Silicon is doped with Phosphorus which has five electrons in its outer orbit. So one electron (e-) will be free. This type of semiconductor is called N-type.
Phosphorous atoms (P) can donate this electron to another bond that needs it, so it is referred to as donor atoms.

## Slide 27
Doping in 3D view
P-type
N-type

## Slide 28
Photovoltaic Effect: p-n junction operation and its parts
e+e-
e+e-
e-
e-
e+
e+
Depletion region
Built-in electric field
e- e+
E
e+e-
e+ e-
The p-n junction
Voltage Difference
Conclusion: The goal of doping is to create the depletion region to create the electric field that separates the electrons from the holes to produce the potential difference.
Notes: A p-n junction is an interface or a boundary between two semiconductor material types,
where the mobile charge carriers have been diffused away, or have been forced away by an electric field. The only elements left in the depletion region are ionized donor or acceptor impurities.

## Slide 29
Solar Cell Operation
e-
e-
e-
e+
e+
e+

## Slide 30
Silicon Solar Cell Packaging
Notes: Busbars- These front and rear contact strips are the busbars which conduct the electric DC power generated by the cell.
Perpendicular to the busbars are the super-thin and metallic grid fingers , which are connected by the busbar. These fingers collect the generated DC current and deliver them to the busbars.
basic structure of a photovoltaic cell consisting of p-conducting base material and an n-conducting layer on the topside. The entire cell rear side is covered with a metallic contact while the irradiated side is equipped with a finger-type contact system to minimise shading losses. Also full cover, transparent conductive layers are used. To reduce reflection losses the cell surface may additionally be provided with an anti-reflecting coating. A silicon solar cell with such construction usually has a blue colour

## Slide 32
Element, panel, chain?
A standard PV element consists of a glass or plastic coating, a non-reflective layer, a top contact plate,
from the lower contact plate and the semiconductor layers.
If we join some number of PV elements together we get a PV panel and if we join together PV panels we get a PV circuit.
The PV system (installation, station) consists of PV panels (circuits) and a DC / AC converter (inverter). In addition, it is possible to upgrade the systems with either recording or network connection.
[EPEA]

## Slide 33
Classification of various Cell Technologies
Depending upon the type of absorbing material used, manufacturing technique process adopted, and type of junction formed etc., the solar cell technologies can be broadly classified as following.
Wafer based crystalline silicon solar cells
Thin-film solar cells, which includes, Copper Indium Gallium Diselenide (CIGS), Cadmium Telluride, Amorphous silicon (a-Si) etc.
Emerging technologies such as thin-film silicon, dye sensitized solar cells; polymer organic solar cells etc.
Note: MS stands for Market Share.

## Slide 34
Multi-junction PV Cells
Multi-junction (MJ) solar cells are solar cells with multiple p–n junctions made of different semiconductor materials. Each material's p-n junction will produce electric current in response to different wavelengths of light. The use of multiple semi conducting materials allows the absorbance of a broader range of wavelengths, improving the cell's sunlight to electrical energy conversion efficiency.
Notes: will produce electric current in response to different wavelengths of light

## Slide 35
Quantum Efficiency
The "quantum efficiency" (Q.E.) is the ratio of the number of carriers collected by the solar cell to the number of photons of a given energy incident on the solar cell.
Notes: QE is dimensionless, but it is closely related to the responsivity, which is expressed in amps per watt. Since the energy of a photon is inversely proportional to its wavelength, QE is often measured over a range of different wavelengths to characterize a device's efficiency at each photon energy level. For typical semiconductor photodetectors, QE drops to zero for photons whose energy is below the band gap

## Slide 36
EFFICIENCIES OF SOLAR CELLS
[Renewable Energy Technology, and Environment Martin Kaltschmitt, 2007]

## Slide 37
Notes: Gallium arsenide (GaAs) is a III-V direct band gap semiconductor with a zinc blende crystal structure.

## Slide 38
Equivalent circuit of the solar cell and characteristic curve

## Slide 39
Equivalent Circuit for Solar Cell
Standard Solar cell
Notes: A simple equivalent circuit model for a PV cell consists of a real diode in parallel with an ideal current source. The ideal current source delivers current in proportion to the solar flux to which it is exposed.
The photocurrent IPh is assumed to be proportional to the photon flow incident on the cell
A diode vacuum tube or thermionic diode is a vacuum tube with two electrodes, a heated cathode and a plate, in which electrons can flow in only one direction,

## Slide 40
Equivalent Circuit of a Solar Cell
I = IL − ID − ISH
where I = output current (amperes)
IL = photo-generated current (amperes)
ID = diode current (amperes)
ISH = shunt current (amperes).
where
I0 = reverse saturation current (amperes) – increases at high temperatures
n = diode ideality factor (1 for an ideal diode)
q = elementary charge
k = Boltzmann's constant
T = absolute temperature
Real Solar cell
Notes: A diode vacuum tube or thermionic diode is a vacuum tube with two electrodes, a heated cathode and a plate, in which electrons can flow in only one direction,
a shunt is a device that creates a low-resistance path for electric current, to allow it to pass around another point in the circuit.[1] The origin of the term is in the verb 'to shunt' meaning to turn away or follow a different path.

## Slide 41
I -V and P-V curves for PV module.
The current axis (where V = 0) is the short-circuit current Isc, and the intersection with the voltage axis (where I = 0) is the open-circuit voltage Voc. For this module the current decreases slowly to about 15 V and then decreases rapidly to the open-circuit conditions at about 21.4 V. For comparison, a single 1-cm2 silicon cell at a solar radiation level of 1000 W/m2 has an open-circuit voltage of about 0.6 V and a short-circuit current of about 20 to 30 mA.
The maximum power that can be obtained corresponds to the rectangle of maximum area under the I -V curve. At the maximum power point the power is Pmp, the current is Imp, and the voltage is Vmp. Ideally, cells would always operate at the maximum power point, but practically cells operate at a point on the I -V curve that matches the I -V characteristic of the load

## Slide 42
Open-circuit voltage (Voc) : max. voltage (I=0)
Short-circuit current (Isc or Iph): max. current (V=0)
Maximum power voltage (Vmp): Knee voltage (Max. power voltage)
Maximum power current (Imp): Knee current (Max. power current)
Maximum power (Pmp) : Pmp = Vmp * Imp
Maximum Power Efficiency (ηmax) : Knee efficiency
Fill factor ( FF ) : squareness factor
Electrical Properties of solar cells
Notes: The "fill factor", more commonly known by its abbreviation "FF", is a parameter which, in conjunction with Voc and Isc, determines the maximum power from a solar cell.

## Slide 43
IV-Curve of a typical (100mmx100mm) silicon solar cell
Notes: The "fill factor", more commonly known by its abbreviation "FF", is a parameter which, in conjunction with Voc and Isc, determines the maximum power from a solar cell.

## Slide 44
Global Solar Radiation Effect on Solar Cell

## Slide 45
Cell Temperature Effect on Solar Cell
Notes: The parameter most affected by an increase in temperature is the open-circuit voltage (Voc). Accordingly, the power of the solar cell at the Maximum Power Point (MPP) decreases by increasing the cell’s temperature.

## Slide 46
[Renewable Energy Technology, and Environment Martin Kaltschmitt, 2007]

## Slide 47
Temperature Effect on Silicon Wafer-based Solar Cells
Hot
Cold
STC

## Slide 48
Standard Test Conditions (STC Conditions)
• In-plane Global Solar Irradiance (G): 1000 W/m2
• Cell Temperature (T): 25 ºC
• Air Mass (AM): 1.5 (solar spectrum)
θ = 48.2º means AM1.5
(approximation)
cos (48.2º) = 2 / 3
Notes: STC stands for “Standard Test Conditions” and are the industry standard for the conditions under which a solar panel are tested. By using a fixed set of conditions, all solar panels can be more accurately compared and rated against each other

## Slide 49
Efficiency of Solar Cell at MPP
The efficiency of the solar cell is the ratio of electrical power output to the incident radiant power :
Input Power = G [W/m2] x Area [m2]
Output Power = Vmp [V] x Imp [A]
G “Global Solar Irradiance”
Area
+
-
V
I
Resistor
Solar Cell
Notes: The MPP voltage can drift depending on wide range of variables including the irradiance intensity, device temperature, and device degradation.

## Slide 50
Efficiency of PV elements in conclusion
The efficiency of a PV cell shows how much of the light it emits is efficiently converted into electricity. With today's technologies, the efficiency is somewhere between 6 & 44%. PV panels for ordinary household use have an efficiency of 15-20%.
When manufacturers measure the efficiency of the panels they produce, this shall be done under agreed standard conditions (STC), which correspond to the clear for a summer day with air temperature + 25 ° C.
rather, the price / power (€ / W) ratio when making a purchase decision, as the panel price increases exponentially as efficiency increases. Today, the best W / € ratio ensures 270-275W polycrystalline panel.
Notes: Solar cell efficiencies are only 6% for amorphous silicon-based solar cells.
an efficiency of 44.0% has been achieved with experimental multiple-junction concentrated photovoltaics.

## Slide 51
Typical Temperature Coefficients for Silicon Wafer-based Cells
Pmpp (T) = Pmpp (25 °C) [ 1 + γPmpp ×(T – 25 °C) ]
Vmpp (T) = Vmpp (25 °C) [ 1 + βVmpp × (T – 25 °C) ]
Impp (T) = Impp (25 °C) [ 1 + αImpp × (T – 25 °C) ]
Voc (T) = Voc (25 °C) [ 1 + βVoc × (T – 25 °C) ]
Isc (T) = Isc (25 °C) [ 1 + αIsc × (T – 25 °C) ]

## Slide 52
Commercial PV Modules – The datasheet of the PV module
Manufacturer’s name and Model number
Cell technology and shape.
Number of cells.
Lamination material.
Frame material and outer dimensions.
Front glass material.
Back sheet material.
Junction box.
Cables and connectors.
Number of bypass diodes.
Practical Exercise: compare between a wafer-based and a thin-film PV module
Electrical Data @ STC and NOCT : Voc, Isc, Vmp, Imp, Pmax, STC efficiency and fill factor.
Maximum system voltage.
Fuse rating current.
Operating temperature range.
Temperature coefficients for voltage, current and power.
Power tolerance.
Power warranty.
Manufacturing or workmanship warranty.
Manufacturing standards.
Quality certificates.
Notes: NOCT normal operating cell Temperature
You can read datasheet without saving it for different manufacturer and compare it to different pv cell types

## Slide 53
The world's largest PV power plants in 2017
PV station | Power (MWp) | Location | Year of completion
Tengger Desert Solar Park | 1 547 | China | 2016
Datong Solar Power Top Runner Base Phase I, total plan 3 X 1000 MW | 1,000 | China | 2016 (Phase I)
Kurnool Ultra Mega Solar Park | 1,000 | India | 2017
Longyangxia Dam Solar Park | 850 | China | 2015
Kamuthi Solar Power Project | 648 | India | 2016
Solar Star (I and II) | 579 | USA | 2015
Topaz Solar Farm | 550 | USA | 2014
Copper Mountain Solar Facility | 550 | USA | 2015
Desert Sunlight Solar Farm | 550 | USA | 2015
Huanghe Hydropower Golmud Solar Park | 500 | China | 2015
Bhadla Solar Park | 480 | India | 2016
Mesquite Solar project | 400 | USA | 2013
Quaid-e-Azam Solar Park | 400 | Pakistan | 2015
Longyangxia Dam Solar Park (850 MW)
[EPEA]
Notes: The following is a list of photovoltaic power stations that are larger than 250 megawatts (MW) in current net capacity.[1] Most are individual photovoltaic power stations, but some are groups of co-located plants owned by different independent power producers
In 2016, the largest photovoltaic power station in the world was the 850 MW Longyangxia Dam Solar Park, in Gonghe County, Qinghai, China. This was passed in 2019 with the completion of the Pavagada Solar Park in Karnataka, India, with a capacity of 2050 MW.

## Slide 54
The world's largest PV power plants, updated
1. China, Gonghe 2,200 MWAC
China recaptures the number one position this year with the 2,200 MWAC solar power plant commissioned last September by Huanghe Hydro­power Developments. It covers over 5,000 hectares of semi-desert in Gonghe County of the Hainan Prefecture in Qinghai, China.
2. Sweihan Power Project 938 MW
his 938 MWAC plant in Abu Dhabi in the UAE became the world’s largest single solar power station when commis­sioned in June 2019 – a position it held for 15 months.

## Slide 55
4. Copper Mountain Solar Facility 816 MW (-)
The USA’s highest entry this time is at #4 (it’s highest at #6 in the previous list, Solar Star, is now down to #10). One of the U.S.’ earliest utility-scale solar plants, phase one of the Copper Mountain project was first connected by Sempra Energy back in 2010. When the southernmost phase five was commissioned this March, it took the total capacity of the plant to 816 MW.
3. Yanchi Solar Park 820 MW
2019’s number one is third in today’s list – the so-called Yanchi Solar Park just south of Gaoshawo in Ninxia’s Yanchi district. Despite the name, it is not a ‘solar park’, as we would define it. The project was developed by China Minsheng New Energy and has been operational since 2016. Its 1 GWP solar arrays give it an output of about 820 MWAC.

## Slide 56
Distribution of PV installations
The share of households is declining but will still dominate
With the development of storage technologies, the share of off-grid and hybrid systems is increasing
[IEA Technology Roadmap Solar Photovoltaic Energy 2010]

## Slide 57
PV installation
FOR SLICING
FOR FLAT ROOF
INTEGRATED
TO THE FACADE
ON THE GROUND
https://www.greenrhinoenergy.com/solar/technologies/pv_mounting.php

## Slide 58
PV panels and snow?
Canadian Northern Alberta Institute of Technology Survey 2012-2015

## Slide 59
The value of energy storage
Cost-effective storage solves a fundamental problem in the use of solar energy - a different cycle of production and consumption. With the help of the recording, the production of the day can be shifted to cover the consumption peaks in the evening and in the morning.
Notes: The Balance of System (BoS) comprises of junction boxes, HV, LV and DC electrical works, transformers, switch gears, AC and DC cables, security systems etc. The Other costs include costs for installation, all kinds of approvals, land registry & planning, grid integration, engineering and technical analysis, plant validation, financial & legal services, etc.

## Slide 60
Cost of home battery storage
Cost of electricity produced and stored
=
Cost of production (LCOE)
+
cost of storage (LCOS)
Production cost 8 ... 10 € c / kWh Recording cost ~ 10 ... 12 € c / kWh
A total of 18 ... 22 € c / kWh
vs.
Electricity from the network:
EE; LT, CZ, HU: 11 ... 12 € c / kWh
In 2022 EE 20…52 c / kWh
EU avg 21 € c / kWh (2015)

## Slide 61
The price of battery storage is falling ...
Is the decrease comparable to the decrease in PV prices?

## Slide 62
Is a solar power plant a black box?
The solar power plant is:
cash flow production technology
fixing energy costs for 30 years
investment for 30 years
A solar power plant is not a black box!
100% energy produced
Electricity to the general grid 60-80%
Local consumption 20-40%
Electricity from the mains
Savings cash flow + sales cash flow

## Slide 63
PV CAPEX and LCOE
Doubling global production reduces the cost of systems by 25-30%
Today in Estonia "turnkey" price:
For the business range 0.8 - 1.0 € / W
For the private consumer range 1.1 - 1.6 € / W
The price depends on the conditions of the specific installation
  Network connection
  Tech. complexity
Based on the price of the system, the cost of production (LCOE) today ranges 0.06 - 0.1 € / kWh
Fixed price for 25 ... 30 years!
SourceFraunhofer Institute 2013

## Slide 64
PV power plant operating costs
OPERATING COSTS 0.5 - 1% of the investment per year
(cleaning, maintenance, insurance)
DEGRADATION: ~ 0.5% decrease in productivity
Hiding or covering 2% of the surface of the PV panel can reduce the production capacity of the panel (and the whole chain) by up to 70%
Due to dirt on the surface of the PV panel reduced productivity!

## Slide 65
General profitability parameters Useful life of the installation
For equipment
Solar panels - 25-30 years (80% of original productivity retained)
(Wind generator - 15-20 years. Needs more maintenance - mechanics!)
Inverter - 20-25 years.
Other materials - cables and contacts UV resistant
OTHER:
IS THE ROOF LIFE OF 30 YEARS?
HOW LONG IS THE EXPECTED RETURN? WILL I ALWAYS LIVE IN THIS HOUSE FOR 30 YEARS?

## Slide 66
PV System Components
Notes: A charge controller or charge regulator is basically a voltage and/or current regulator to keep batteries from overcharging. It regulates the voltage and current coming from the solar panels going to the battery. ... Most batteries need around 14 to 14.5 volts to get fully charged.
Inverter It converts the variable direct current (DC) output of a photovoltaic (PV) solar panel into alternating 240V current (AC). This AC electricity then can be fed into your home to operate your appliances.

## Slide 67
off-grid and on-grid PV Systems
Standalone “off-grid”
Grid-connected “on-grid”
Without storage
With storage
Hybrid Systems
directly connected to the public grid
connected to public grid via house grid
Motors
“e.g. pumps”
DC Systems
AC Systems
with wind turbine
with diesel generator
with public grid backup

## Slide 68
PV Array
DC Load
DC/DC Power Conditioning Unit
Off-grid / Without battery storage / Power-conditioned DC system

## Slide 69
DC Submersible Water Pumping System
PV Array
DC/DC Pump Controller
DC Submersible Pump
Variable Voltage
(Proportional to Solar Intensity)
Off-grid / Without battery storage / Power-conditioned DC system

## Slide 70
Off-grid / Without battery storage / Power-conditioned AC system
PV Array
AC Load
DC/AC Power Conditioning Unit

## Slide 71
AC Submersible Water Pumping System
PV Array
DC/AC Pump Controller
AC Submersible Pump
Variable Voltage & Frequency
(Proportional to Solar Intensity)
Off-grid / Without battery storage / Power-conditioned AC system

## Slide 72
PV Array
DC Load
Charge
&
Load Controller
Battery
Off-grid / With battery storage / DC system

## Slide 73
PV Array
DC Load
Charge
Controller
Battery
Load
Controller
Charge & Load Controller
CCP*
*Common Connection Point (CCP)
Off-grid / With battery storage / DC system

## Slide 74
Solar Home Systems & DC Industrial Systems
PV Array
DC Load
Battery Bank
Charge & Load Controller
Off-grid / With battery storage / DC system

## Slide 75
PV Array
Charge
Controller
Battery
DC/AC Inverter
AC Load
CCP*
*Common Connection Point (CCP)
Off-grid / With battery storage / AC system

## Slide 76
Solar Home Systems & AC Industrial Applications
PV Array
AC Load
Battery Bank
Charge Controller
DC/AC Inverter
With fixed voltage & frequency
Off-grid / With battery storage / AC system

## Slide 77
On-grid PV Systems
The grid is the network of cables by which electricity is transported from power stations to houses, buildings & other places.
A grid connected PV system is linked to this grid or electrical network. This means that it can deliver the electricity it produces into the electricity network and therefore no battery or other storage is needed.

## Slide 78
On-grid PV Systems

## Slide 79
Grid connected PV systems
Net metering
The difference between production-consumption is measured
Feed-in tariff
The total production of energy is measured

## Slide 80
For more info
For nanoproducers (below 0,79 kW)
https://www.elektrilevi.ee/en/nanotootjale
Connection for small producers (under 500 kW)
https://www.elektrilevi.ee/en/vaiketootjale
For electricity generator (from 500 kW)
https://www.elektrilevi.ee/elektritootjale
For large application projects
https://elering.ee/en/handbooks#accordion0

## Slide 81
THANK YOU
Mais.Baqain@taltech.ee