## Slide 1: Basics of microscopic traffic modelling: using PTV Vissim in traffic simulations
Konrad Biszko
Gdańsk University of Technology
Sustainability and Quality Assurance for Academic Governance and Redesign Engineering Studies

## Slide 2: Chapter 1 - theory
Konrad Biszko
Gdańsk University of Technology
Sustainability and Quality Assurance for Academic Governance and Redesign Engineering Studies

## Slide 3: Properties of traffic models
Quality | Microscopic | Macroscopic
Scale | Individual vehicles | Aggregated traffic stream
Precision | Relatively big, description of individual user behaviour | Relatively small, based on average values
Calculated simulation state | Simulation timestep, typically 0.1s | Typically whole day or single hour
Frequency of calculations | Calculations conducted every timestep | Calculation procedure conducted once for simulation state
Scale of network | Relatively small (single intersection, a slice of network) | Relatively big (whole city, region, country)

## Slide 4: Example – microscopic vs macroscopic
Microscopic
Macroscopic

## Slide 5: Car following model in Vissim
Vissim uses Wiedemann 74 and Wiedemann 99 car following models.
It is a „Psycho-Physical” model, taking into account the physical aspects of vehicle movement and also drivers' psychological aspects related to perception

## Slide 6: Wiedemann 74 car following model
If there is no vehicle in front of you, you move in free-flow traffic and are able to freely choose the speed.
If there is a vehicle in front, you try to maintain the desired distance:

## Slide 7: Wiedemann 74 parameters

## Slide 8: Example of car following in practice
http://w99demo.com/

## Slide 9: PTV Vissim: Start Page
Save, load, create new files, settings. It is recommended to save the file often.
Main „toolbox”
Starting page
Information about updates
Different views

## Slide 10: PTV Vissim: Network editor
Scale of the current view
Switch to „Network Editor”
You use the „toolbox” in Network Editor

## Slide 11: PTV Vissim – Manual
Click on „Help”
Click on „PTV Vissim Manual”
It (most likely) contains all the information you need if you get stuck or need details related to the software's functionality

## Slide 12: Chapter 2 – Developing traffic network
Konrad Biszko
Gdańsk University of Technology
Sustainability and Quality Assurance for Academic Governance and Redesign Engineering Studies

## Slide 13: Ch.2 Part 1 – creating basic road network
Konrad Biszko
Gdańsk University of Technology
Sustainability and Quality Assurance for Academic Governance and Redesign Engineering Studies

## Slide 14: User preferences - language
Select Edit and User Preferences
Set the language to English!
(The software is made by a German company, and not everything might be fully translated to languages other than English, so by default some errors or functions might appear in German)

## Slide 15: User preferences – right click behaviour
In the same User Preferences window select Network Editor
Select the option that you prefer, you can change it later
There are two options available for adding objects into the model

## Slide 16: Vissim map background
Click the globe icon to switch the background map

## Slide 17: Vissim with map background active
Initial view of a new Vissim file is usually zoomed out, which is easier to see by looking at the map

## Slide 18: Finding the proper scale
Judging by the value displayed at the scale we can draw a conclusion, that it is impossible to work with road network when zoomed out to this extent.

## Slide 19: Locating test site pt. 1
By clicking at the blue pin we can search for a location we want to use as the base for our model. It is also possible to manually zoom in to the location using the scroll wheel.

## Slide 20: Locating test site pt. 2
After finding our location we see that the view has been zoomed in significantly. This is better, but still is too far to start drawing a road network at microscopic level.

## Slide 21: Zooming in
Using the scroll wheel we zoomed in. We can use the background as a reference, or use the value on the scale. Feel free to zoom in and out when working with Vissim software, so the view suits your needs.
Hold the middle mouse button to move the view around without changing the zoom level.

## Slide 22: Preparing the canvas
We will not reproduce any particular road section at this time. We will turn off the map by clicking on the globe icon.
Select „Links” by clicking on it (it might also be the first thing already selected by default).
We will add the first link. Make sure to use right-click or ctrl+right-click depending on the options set in user preferences.
The next slide presents the process of adding a link.

## Slide 23: Drawing links
Click RMB and drag to add a new link.
Links are always one-way road segments, and the traffic direction will be set in accordance with the direction you are drawing the link.
After releasing the RMB, a new window with parameters will appear.

## Slide 24: Links – properties pt. 1
You can type in the width of the link
By right-clicking add more lanes to the left or right
A window with properties is opened automatically, but you can also double-click the link to reopen that window. You can always come back to this window and change the properties.

## Slide 25: Links – properties pt. 2
The small arrows point in the direction of traffic flow
You can click and drag these handles to add and delete lanes
You can extend and move one end of the link by clicking on the yellow dot.

## Slide 26: Next steps: adding more links
We will now add a second link to our model and connect the links by drawing a special link – a „connector”.
Make sure the links are added in the same direction.

## Slide 27: Creating connectors between links
Adding connectors is done the same way as other links, but we start drawing on the first link and finish on the second

## Slide 28: Connector properties
The width of the connector is calculated automatically depending on the width of connected links

## Slide 29: Connectors in the model, pt. 1
Connectors are the same objects as links, but since they are „special”, in a way they connect two other links, Vissim automatically assigns a new number starting from 10000 instead of 1 (as for normal links)
You can see small arrows pointing in the direction of traffic flow.

## Slide 30: Connectors in the model, pt. 2
After clicking the connector you will see 3 handles at each side.
You can use these handles to change the layout of lanes on the link.
The best way is to see what exactly the behaviour of each handle is to experiment with possible options.

## Slide 31: Dynamic modification of connectors
This video presents some of the possibilities in our case.
Apart from the handles, you can also use the yellow dots to attach the connector to a different lane (or to a completely different link)
As with other links, this can be modified at a later stage if necessary.

## Slide 32: Wireframe view pt. 1
By default, connectors are not distinguishable from regular links. The best way to deal with that is to turn on the „Wireframe” view.
You can toggle it with the wireframe icon or by pressing ctrl+A

## Slide 33: Wireframe view pt. 2
Links and connectors have different colours in the wireframe view.
By hovering over the link or clicking it you will still see the full frame of the link. The functionality of the software remains unchanged, only the view is different.

## Slide 34: Next step: adding a link in the opposite direction
We will add a link in the opposite direction

## Slide 35: Adding pedestrian crossing
We will add pedestrian crossing by drawing a new link that crosses the previously created links

## Slide 36: Selecting parameters for pedestrian link
Let's assume the total width of pedestrian crossing at 4m. Rememeber that we need to draw the links in two directions, so for the first pedestrian link we will set the width as half of that, so 2m.
We need to change the behaviour on the lane, since pedestrians act differently than vehicles
We select „Footpath”

## Slide 37: Generating a link in an opposite direction
After adding the pedestrian link we need to open the context menu (ctrl+RMB; depending on the option selected in user preferences)
Afterwards we select the option „generate opposite direction” and press ok

## Slide 38: Link in an opposite direction
New link in an opposite direction is automatically added

## Slide 39: Conflict areas pt. 1
Without any changes to the behaviour, vehicles and pedestrians will simply pass through each other.
From the toolbox we select Conflict Areas. New objects will automatically appear in the model.
Yellow fields will appear in the place where links inersect. It means that the links intersect, but there is no interaction, simulated objects will pass through each other.

## Slide 40: Conflict areas pt. 2
After clicking one of the fields, directions of traffic flow together wth labels „A” and „B” will appear.
In the left bottom corner of Vissim you will see the details of selected conflict

## Slide 41: Setting right of way pt. 1
Right clicking changes the behaviour on the selected conflict area. The flow displayed in green has the right of way. You can keep right clicking in order to cycle through possible options.
The parameters of the conflict area are dynamically updated in the Quick View window

## Slide 42: Setting right of way pt. 2
You can also edit the behaviour and other parameters directly from the Quick View window

## Slide 43: Conflicts – displaying a list
Right click on „Conflict Areas” in the toolbox, and then select the option „Show List”.
Remember this option for showing the list – you can do it for every object in the toolbox

## Slide 44: Setting conflicts from the list view
A new window containing a list is displayed at the bottom of the screen. You can click on objects in the list to highlight them in Network Editor. You can also modify them directly from the list.
This comes especially useful, when the intersection has complex geometry with many conflicts located on top of each other. It might be hard to click on them in Network Editor or to even see them, but by using the list you immediately see which conflicts have not yet been modified.

## Slide 45: Final setting of conflicts
We want the vehicles to give way to pedestrians, so for every conflict we select the option that gives the right of way to pedestrian links.

## Slide 46: Conflict status: „Undetermined”
Vissim also allows us to set the conflict as „Undetermined” (both flows are red). It means that there is an interaction between simulated vehicles/pedestrians and the first one to arrive at the conflict area is given right of way.
This is different from the default option „Passive” (both flows are yellow), as it will not cause any interacion at all.

## Slide 47: Drawing link geometry pt. 1
The video presents additional possibilities regarding drawing links. During drawing the link, use LMB to add new intermediate points.

## Slide 48: Drawing link geometry pt. 2
You can also add new intermediate points to an already created link by using RMB (depending on the options set in user preferences). These points can be moved to change the geometry of a link.

## Slide 49: Drawing link geometry pt. 3
You can click on the link (not on the yellow point in the link) to move it.
You can also add intermediate points by using the link properties (opened by clicking twice on a link).
This also applies to connectors, and Vissim tries to help you by automatically adjusting the curvature based on the number of assigned intermediate points.

## Slide 50: Task 1:
Create a road network for a three-way intersection. Create pedestrian crossings on two adjacent intersection entries.

## Slide 51: Example solution

## Slide 52: Example solution

## Slide 53: Example solution

## Slide 54: Ch.2 Part 2 – Traffic lights and fixed traffic light programs
Konrad Biszko
Gdańsk University of Technology
Sustainability and Quality Assurance for Academic Governance and Redesign Engineering Studies

## Slide 55: Signal controllers pt. 1
To add a new signal controller we need to first display the Signal Controllers list.
Select „Signal Control” and then „Singal Controllers”

## Slide 56: Signal controllers pt. 2
A new list will be opened at the bottom of the screen. Click on the green + sign to add a new signal controller.
Notice that the old list has not been replaced, you can cycle through opened lists.

## Slide 57: Signal controllers pt. 3
A new window will appear on the screen. Usually, you will be using the fixed time signal controller when working with Vissim (but modelling control logic is also possible)
Click on the „Edit controller data”

## Slide 58: Signal controllers pt. 4
A new window related to the signal controller will appear

## Slide 59: Signal groups pt. 1
From the list located on the left side select „Signal Groups”
Click green + sign to add new signal groups

## Slide 60: Signal groups pt. 2
Typically we need at least 1 signal group for each intersection entry (or more, if lanes for turning left and right are required to be separated from the „main” traffic stream) and 1 signal group for every pedestrian crossing.
We will add 3 signal groups and type in the names: N for north entry, S for south entry and Pedestrians E&W for pedestrian crossing.
Names do not change functionality of the software – use names that are clear and useful to you.

## Slide 61: Signal groups pt. 3
If added signal groups are hidden press on the + next to the „Signal Groups”
Select the first added signal group
Select the default sequence for this signal group. Initially every new group is assigned „red, red+yellow, green and yellow” that is usually the sequence for vehicle signals in Europe
After selecting the correct sequence you can modify the minimum times for each signal.

## Slide 62: Signal groups pt. 4
For the pedestrian signal group we can use „Red, green, flashing green” sequence.

## Slide 63: Intergreen matrix pt. 1
Switch to the Intergreen Matrix tab from the list and click the + sign to add a new matrix.

## Slide 64: Intergreen matrix pt. 2
Select added matrix from the list. Values should be put for the signal groups that cannot be given green signal at the same time.
In this case, pedestrians and vehicles cannot be given green light together.
While there are rules for calculating minimal intergreen times, for the purpose of this course we will focus on preparing the model and skip the calculations. We will type in some sample values.

## Slide 65: Stages
Switch to the Stages tab and press the + sign to add new stages.
For our model we need two stages: one for vehicles and one for pedestrians.

## Slide 66: Stage assignment, pt. 1
In the stage assignment tab we decide which signal groups belong to every stage. By default every group is red signal.

## Slide 67: Stage assignment, pt. 2
Double-click on the fields (initially red crosses) to switch the state of signal for each stage.
We want both vehicle signal groups in one stage, and the pedestrian crossing in the other stage.

## Slide 68: Selecting intergreen matrix
Select the default intergreen matrix for the stage assignment.

## Slide 69: Example of errors visible with matrix selected
When the intergreen matrix is selected and you allow for green light for conflicting signal groups for a stage (on the picture – every signal group has green light in the first stage), Vissim will warn you that the intergreen has been violated.
You should correct situations like this one before proceeding, usually by changing the signal group assignment to stages.

## Slide 70: Stage sequence pt. 1
Go to the stage sequence tab. Added stages will appear in the window.

## Slide 71: Stage sequence pt. 2
Double click on the stages in the upper part of the window to add them to the bottom sequence. For this excercise, add both stages once.
We can adjust the cycle time as appriopriate and click on „Create stage based program”

## Slide 72: Signal programs – stage based pt. 1
We can still change the cycle time if necessary.
The intergreen matrix we selected in the stage assignment tab is automatically selected
Click on the white sections of the program and drag them to manually change the time of stages.

## Slide 73: Signal programs – stage based pt. 2
The video presents adjusting the time of stages.

## Slide 74: Stage sequence pt. 3
Go back to the Stage Sequence tab. We will not change the sequence, but this time click on the „Create signal group based program”

## Slide 75: Stage sequence pt. 4
Cycle time can be changed as previously
No intergreen is selected, select it manually
You can type in the values of green time to adjust it.
Notice there are no white sections like with the stage-based program. You drag every signal group individually.

## Slide 76: Signal programs – group based
The video presents operations on the signal program.
You can shorten or extend the time by draging the Edge of a signal, or click in the middle of a signal and move it. You can also type in the values in the table on the right.
Select the intergreen matrix. Vissim will display if intergreen is violated (in orange) or if you have time without any signal that could be utilized (in green).

## Slide 77: Signal programs – manual pt. 1
You can also omit stage-related tabs and go directly to the signal programs tab. By clicking on the + sign add a new traffic program and select it from the list.

## Slide 78: Signal programs – manual pt. 2
A new program was created with default values, without intergreen Times defined. Select intergreen matrix from the list.

## Slide 79: Signal programs – manual pt. 3
Firstly let's change the cycle time to 120s. The program will extend the times.
Select the appropriate intergreen matrix
With matrix selected, the conflicts are highlighted like with previous signal programs.

## Slide 80: Signal programs – manual pt. 3
Modify the program so it allows for longer green light for the road traffic stream.
Make sure there are no orange bars indicating intergreen violation.

## Slide 81: Interstages pt. 1
Interstages are created automatically after creating stages and the first stage-based program.

## Slide 82: Interstages pt. 2
Select one of the interstages. You can modify it similarly to regular programs. After modification create a new stage-based program to see the interstages changed.
If you want to go back to default values or you made some changes e.g. to intergreen matrix click on „Recalculate” to automatically generate default interstages.

## Slide 83: Saving a signal controller
Select the option with the green arrow and the door to save the signal controller and go back to the main Vissim window. You can keep clicking this icon during your work to make saves regularly and then go back to this window.

## Slide 84: Finalizing work with a signal controller
After saving the changes click on the „OK” button. If you click the X in the upper right corner or cancel, the changes might not get saved and you will lose all your work.

## Slide 85: Signal controller in the simulation pt. 1
Added signal controller can be always accessed and modified from the list by double-clicking.

## Slide 86: Signal controller in the simulation pt. 2
We created 3 traffic programs during our work with the signal controller. We can switch the active program using the list by typing in the number.
If you want to run the simulation with the traffic lights for selected controller turned off, just type in a program number that has not been created. E.g. type in 99, so Vissim knows that a non-existant program has been selected and all the signals will be turned off, so the intersection will act as if there are no traffic lights at all.

## Slide 87: Adding signal heads pt. 1
A signal controller has been created, but traffic lights are yet to be inserted into the model.
Select „Signal Heads” from the toolbox.

## Slide 88: Adding signal heads pt. 2
Click RMB on the link to add a new signal head. While in real life signal heads are next to or above the road, in the simulation these objects are inserted in the location of the stop line or other place where vehicles are supposed to stop.

## Slide 89: Adding signal heads pt. 3
After inserting a signal head a new window with options regarding this particular signal head will appear.

## Slide 90: Adding signal heads pt. 4
Select signal group for this signal head.
On previous slides we added the signal head on south entry to the intersection, so we will select „S”

## Slide 91: Signal head after insertion
You can click on the signal head to display the direction of flow.

## Slide 92: All signal heads in the model
We need to add a signal head for every lane separately.
The picture displays an example location of signal heads.

## Slide 93: Task 2:
Create a signal controller and a traffic light program for previously created 3-way intersection. Prepare three signal plans with cycle times: 60, 90, 120

## Slide 94: Example solution

## Slide 95: Example solution

## Slide 96: Example solution

## Slide 97: Example solution

## Slide 98: Example solution

## Slide 99: Example solution

## Slide 100: Example solution

## Slide 101: Example solution

## Slide 102: Example solution

## Slide 103: Chapter 3 – Traffic flow
Konrad Biszko
Gdańsk University of Technology
Sustainability and Quality Assurance for Academic Governance and Redesign Engineering Studies

## Slide 104: Ch.3 Part 1 – Vehicle types, Inputs and Routing
Konrad Biszko
Gdańsk University of Technology
Sustainability and Quality Assurance for Academic Governance and Redesign Engineering Studies

## Slide 105: Vehicle compositions pt. 1
To add a new vehicle composition select Traffic and Vehicle composition to display a new list.

## Slide 106: Vehicle compositions pt. 2
A new list will appear at the bottom of the screen.

## Slide 107: Vehicle compositions pt. 3
Click the plus sign to add a new composition
Rename the composition to Pedestrians
In the right part of the window modify the „VehType” to „Man”

## Slide 108: Vehicle compositions pt. 4
Use the plus sign to add a new veh type to the composition
For the newly added type select „Woman”
These values represent the distribution of types in the composition. Here we have:
1+1 = 2 this is 100% of composition
½ = 50% of pedestrians of type „Male”
½ = 50% of pedestrians of type „Female”

## Slide 109: Vehicle compositions pt. 5
Let's click on the first vehicle composition to see what is inside
In here the total sum is:
0,930 + 0,050 + 0,020 = 1
Cars:
0,930/1 = 93% in traffic stream
Light commercial vehicles (LGV):
0,050/1 = 5% in traffic stream
Heavy commercial vehicles (HGV):
0,020/1 = 2% in traffic stream

## Slide 110: Vehicle inputs pt. 1
In order to add traffic flow to the model we need to place vehicle inputs on links, where vehicles and pedestrians will be entering the networks.
Select „Vehicle Inputs” from the toolbox

## Slide 111: Vehicle inputs pt. 2
Click RMB on the link to add vehicle input. The place where you click does not matter as long as it is on the correct link, the vehicle input will automatically shift to the beginning of the link

## Slide 112: Vehicle inputs pt. 3
Add 4 inputs at every entry to the network
Parameters of Vehicle Inputs can be modified in the list view

## Slide 113: Vehicle inputs pt. 4
For the purpose of this excercise type in the volume as presented in the table. The volumes are always given in 1-hour intervals. If the simulation lasts for e.g. 2 hours, Vissim will recalculate the values accordingly on its own.

## Slide 114: Adding additional time intervals pt. 1
In real world, the road network is not entirely empty. Therefore, if we want to simulate a certain period of time, we might want to add some vehicle and pedestrian traffic acting as a warm-up period before the actual simulation that is meant to be analysed.
Select „Base Data” and then „Time Intervals”

## Slide 115: Adding additional time intervals pt. 2
Time intervals can be defined for many different objects independently.
We need to open the list of objects and select „Vehicle inputs”

## Slide 116: Time interval for a warm-up period
Press the + sign to add a new time interval
The first interval should start at 0. The end of the first interval will be set automatically, depending on the start of the second interval.
For this excercise we will set the warm-up period at 15 minutes, which equals to 900 seconds. The second interval ends at time „MAX” which means the value for the second interval will remain the same until the end of the simulation.

## Slide 117: Changing the volume across different periods
We need to modify the list view in order to display added time interval. Click on the wrench icon to open a new window that allows for modifying the list

## Slide 118: Selecting attributes to be displayed pt. 1
On the list find the volume. Notice that the „0-900” is already added. We only need to add „900-MAX”
Click the green arrow to add selected values to the list

## Slide 119: Selecting attributes to be displayed pt. 2
New positions are added at the end of the list. Click on them and then use the arrow, to shift the „Volume (900-MAX)” so it is next to the „Volume (0-900)”.
This is how it looks like initially
This is after moving it up

## Slide 120: Selecting attributes to be displayed pt. 3
By default, every time interval will have the same value. As we want to modify the value for the warm-up period, we need to add one more option to the list.
Find the „Continued” option in the window and add it to the list.

## Slide 121: New appearance of the list
As long as the „Continuous” is enabled for a time interval, you cannot change the values. Untick all the boxes for „Cont(900-MAX)” column.

## Slide 122: Changing flow volumes for warm-up pt. 1
After unticking the Continuous column, the volumes can be modified separately.

## Slide 123: Changing flow volumes for warm-up pt. 2
The warm-up period is the first period in the simulation, so we will modify the volume for 0-900 interval.
One of common ways to deal with the warm-up period is to use 80% of the volume from the analysed period.
Important! The value for volume is always added in hourly values. Even if the warm-up period is 15 minutes, in the table you still have to put the value for 1 hour of simulation. Vissim software re-calculated the values on its own.

## Slide 124: Changing simulation parameters
We will now adjust the parameters of the simulation.
Select „Simulation” and Parameters

## Slide 125: Simulation time with warm-up period
By default the simulation period is 3600 seconds, meaning 1 hour. This is the typical time for conducting a microscpic simulation, as we usually analyse 1 hour of peak traffic during the day (or 1 hour of morning peak and 1 hour of afternoon peak)
We added a warm-up period to our simulation, so we need to extend the total simulation time by that period: 900+3600=4500

## Slide 126: Next step: extending the network
You can click on the icons on the left side of the toolbox to turn on and off the display of objects.
We will extend our network by adding two separate one-way links

## Slide 127: Network extension
This is the view in the wireframe. Notice that there are two new links connected with two separate connectors.

## Slide 128: Adding Vehicle Routes pt. 1
We want to decide on the number of vehicles that will drive onto our newly added links.
In order to do that we will use Vehicle Routes – select them in the toolbox.

## Slide 129: Adding Vehicle Routes pt. 2
The video presents the process of adding vehicle routes. Right click in the place the route is supposed to begin. After that, click in the place where the route is supposed to end. A route will have one beginning, but typically many endings. To finish adding routes click away from the roads.
Typically, the beginning of a route should be placed relatively early, so the vehicles have a lot of time for decision. Usually the route should end after the intersection (or turn, or divergance of roads).
If we use static routes to guide the vehicles, they will usually cover most of the links in the model.

## Slide 130: View of added routes
Open the list of routes (unless it opened automatically after adding the first route).
In the left list there are all route beginnings.
After clicking on one of the beginnings, all route endings are being displayed in the right list.
Click on it to display the course of a route.

## Slide 131: List with routes and assigned flow volumes
We will type 70 for the route going straight, and 30 for the route turning. Vissim always recalculates values to 100%, so this equals to 70% and 30%, regardless of the number of vehicles that will actually pass through the route.
It is up to you if you put in the absolute values like e.g. 263 and 748 vehicles, percentage values like 30% and 70%, or fractions like 0,45 and 0,55. (The values DO NOT NEED to add to a sum of 1 or 100)

## Slide 132: Modyfing the routes: complex cases
After selecting a route, you can add intermediate points by right clicking (depending on set user preferences) to a route.
You can grab these points to change the course of the route. If you only put one intermediate point, you can accidentally shift the entire route even if you only want to make some small adjustments.
Typically it is best to insert at least 3 intermediate points: 1 before and 1 after the place you want to change, and one in the middle. The first and last point will act as an anchor, so the route before and after will not change, and only the middle part will be modified.
The points that you add to a route reset after clicking away or selecting a dfferent route, but the adjusted course of the route remains.

## Slide 133: Running the simulation
Press the blue arrow to start the simulation.
Use + and – on your keyboard to slow down and speed up the simulation.
Press the quick mode button to speed up the simulation to the maximum possible value limited by the resources Vissim can use on the machine the simulation is being run on. You will not see the vehicles, but the calculations will be performed at maximum capacity in the background.

## Slide 134: Simulation conclusion - warnings
After the simulation has concluded Vissim might show some warnings.
Sometimes they indicate user error, but some of the messages are simply the result of the situation the model is representing.
In this case, the error message means that 116 vehicles could not enter the network from the South input. The reason for that is limited network capacity, it is not possible for this many vehicles to pass through the network when entering from South.
In some cases this could be due to user errors, but in this case it simply means that the network is not suitable for such big traffic flow volume and congestion might arise.
If there are more messages their content will be hidden. Click „Show” to open new windows with the list of all warnings.

## Slide 135: Error and warning messages
This is a window with all warnings and errors. Warnings are messages and do not stop the simulation from running. Errors might shut down the simulation, not allow it to start or stop you from taking certain actions.
Errors usually occur due to user mistake. Two most common situations when errors are being displayed:
Mistakes in the model that do not allow the simulation to start (at the begining of the simulation)
Trying to change something when the simulation is running, which in most cases is impossible (at the end of simulation)

## Slide 136: Task 3
Generate traffic inputs with volumes between 200 and 1000 for each intersection entry. For pedestrians use values between 50 and 500 per input.
Generate routes for vehicles

## Slide 137: Example solution

## Slide 138: Example solution

## Slide 139: Example solution

## Slide 140: Example solution

## Slide 141: Ch.3 Part 2 – Driver Behaviour parameters
Konrad Biszko
Gdańsk University of Technology
Sustainability and Quality Assurance for Academic Governance and Redesign Engineering Studies

## Slide 142: Driving Behaviours – opening the list
Driver behaviour parameters can be modified.
Select „Base Data” and then „Driving Behaviors”.
A new list will open at the bottom of the screen.

## Slide 143: Default Driver Behaviours
There are a few behaviours present in the model by default. For now, double click behaviour on the list to open a new window with driver behaviour properties.

## Slide 144: Default Behaviour – Urban - Following
This is the view of the window after opening driver behaviour „Urban”
By default the behaviour opens at tab „Following”

## Slide 145: Default Behaviour – Urban – Car Following
In the tab Car Following we can inspect the Car Following model and its parameters. Two most commonly used models are Wiedemann 74 (typically for city and relatively low-speed traffic) and Wiedemann 99 (typically for high-speed roads)

## Slide 146: Default Behaviour – Right-side rule - Following
If we take a peek at the Wiedemann 99 model, we will see that the number of parameters is much higher.
Generally speaking, select the model more suitable for your needs and modify the parameters based on available data if necessary.

## Slide 147: Default Behaviour – Urban – Lane Change
The next tab contains parameters related to Lane Change behavior

## Slide 148: Default Behaviour – Urban – Lateral
The tab „Lateral” is about the position of a vehicle on the lane. It can be used to model the situation where there is e.g. 1 lane on the road, but there are multiple vehicles (like motorcycles) next to each other.

## Slide 149: Default Behaviour – Urban – Signal control
Th enext tab describes the behaviour of vehicles when interacting with traffic lights.

## Slide 150: Adding new driver behaviour: aggressive
Go back to the list of behaviours and using the + icon add a new behaviour. We will lower the safety distance that vehicles are trying to maintain, so we will call it „Urban Aggressive”. We will be using the Wiedemann 74 model.
Reduce the Average standstill distance by 1
Reduce additive and multiplicative part of safety distance by 0,5

## Slide 151: Link Behaviour types – list view
Driver behaviours need to be assigned to link behaviour types.
Select Base Data and Link Behavior Types.
A new list will appear.

## Slide 152: Adding new link behaviour type pt. 1
Add a new Link Behavior with the + icon

## Slide 153: Adding new link behaviour type pt. 2
Rename the Link Behaviour to „Urban Agressive” and from the list select Driver Behavior with the same name.

## Slide 154: Changing behaviour type – Quick View (Links)
To change behaviour of a link you can click on it and make the change in the quick view menu

## Slide 155: Changing behaviour type – link properties
Alternatively, you can click twice on a link and select the behaviour in link parameters

## Slide 156: Task 4
Create two new driver behaviours:
Aggressive: adjust the standstill distance and W74 parameters, so the values are lower than the default values
Calm: adjust the standstill distance and W74 parameters, so the values are higher than the default values

## Slide 157: Example solution

## Slide 158: Example solution

## Slide 159: Example solution

## Slide 160: Example solution

## Slide 161: Chapter 4 – Collecting data from simulation
Konrad Biszko
Gdańsk University of Technology
Sustainability and Quality Assurance for Academic Governance and Redesign Engineering Studies

## Slide 162: Ch.4 Part 1 – Data Collection
Konrad Biszko
Gdańsk University of Technology
Sustainability and Quality Assurance for Academic Governance and Redesign Engineering Studies

## Slide 163: Vehicle Travel Times pt. 1
While watching the simulation can provide much information, it is usually better to have some data to back up the observations.
We will start by adding an object measuring Vehicle Travel Times – find it in the toolbox.

## Slide 164: Vehicle Travel Times pt. 2
Click RMB once to add the beginning of travel time measurement
Click RMB for the second time to add an ending

## Slide 165: Vehicle Travel Times pt. 3
Show the list of the Vehicle Travel Times by clicking RMB on the toolbox

## Slide 166: Vehicle Travel Times pt. 4
Add second Travel Time Measurement in the opposite direction. Try to maintain relatively similar distance of both measurements.

## Slide 167: Queue Counters pt. 1
Next item will measure the Queue. Find Queue Counters in the toolbox and select it
Click RMB to place the queue counter. Usually you place that object in the location where the vehicles stop. In this case it will allign with the signal head, as it also serves as a stop line.

## Slide 168: Queue Counters pt. 1
Similarly to travel times, add second queue counter and open the list to inspect the objects in your model.

## Slide 169: Configurating data collection pt. 1
By default Vissm does not save any data. We need to tell Vissim which data we want to save, for how long and how often.
Select Evaluation and then Configuration

## Slide 170: Configurating data collection pt. 2
Most of the selection of the data to be gathered is done in „Result Attributes” tab
Tick the box to save the data
Select when to start gathering the data, for how long to gather it and what the intervals should be for saving the data into the table.
You can save the data for diferent classes separately, for all classes by default
The data can be saved for objects that are listed
Some items have additional parameters that can be modified

## Slide 171: Configurating data collection pt. 3
We will select the items that we added and on top of that we will select the data for the entire network. (Vehicle network performance).
We start gathering the data from 900s (from 0 to 900 is a warm-up period) and it will last for 1 hour, so up to 4500s
We want to get the data from one full hour, so for interval we type in 3600

## Slide 172: Configurating data collection pt. 4
In the result management windows you can choose to save results of all simulations you will run using your model, or you can select to save the data only from a single simulation run. You generally pick the option based on your needs.
Press OK to close the window and save the changes.

## Slide 173: Viewing the results pt. 1
Select Evaluation, then Result Lists and then, one by one select the results that you want to open. In this case we want:
Simulation runs
Network Performance (vehicles)
Queue Results
Vehicle Travel time results

## Slide 174: Viewing the results pt. 2
All of opened lists can be selected at the bottom of the screen. If you have too many tabs to select from, feel free to close them, you can always reopen them later.
Initially all the lists will be empty. After running the simulation the results will appear. You can use quick mode if you do not need to watch the simulation.

## Slide 175: Simulation Runs Data pt. 1
Simulation runs list is empty, if no simulations with results have yet been conducted.

## Slide 176: Simulation Runs Data pt. 2
After running the simulation the information about that run will be saved. If you do not want to store the data (including other results) of this particular run, you can click on it and delete it.

## Slide 177: Queue Results
Queue results by default show the average and maximum number of vehicles on each Queue measurement. Hover over the name of parameter in the table or check the Manual for more details.

## Slide 178: Travel Time Results
Travel times display the amount of vehicles that passed through those measurement objects, the time and distance it took.

## Slide 179: Vehicle Network Performance Results
Vehicle network performance contains many metrics related to the entire network.

## Slide 180: Adjusting results list
Some of the metrics are not on the list by default, so feel free to use the Wrench icon and modify the list, so it meets your needs.

## Slide 181: Task 5
Collect the data for your model:
Collect the data (Travel Times, Queue Results) for driver behaviours: urban (default), aggressive, calm for every proposed traffic light program (60, 90, 120) and for scenario without traffic lights (in the Signal Controllers list set the ProgNo to a value that you did not assign to any traffic light program e.g. „99” to temporarily disable the traffic lights)
Use an external tool (e.g. Excel, Calc, Google Sheets) to store the results for each run
Compare the results

## Slide 182: Example Solution

## Slide 184: Example Solution

## Slide 185: Example Solution

## Slide 186: Example Solution

## Slide 187: Example Solution

## Slide 188: Example Solution

## Slide 189: Example Solution

## Slide 190: Ch.4 Part 2 – Video Recording of simulation
Konrad Biszko
Gdańsk University of Technology
Sustainability and Quality Assurance for Academic Governance and Redesign Engineering Studies

## Slide 191: Switching to a 3d view pt. 1
Press ctrl+d on keyboard or click the „2D/3D” icon to switch between the views.
Use the scroll wheel to zoom in and out.
Hold the middle mouse button to move around the model.
Hold alt+middle mouse button to rotate the view.

## Slide 192: Switching to a 3d view pt. 2
If upon switching to a 3d view you cannot see your model, the easiest way to find it is to open the list of links, right click on any of them and select „Zoom”. It might take a couple of seconds for Vissim to properly zoom to your network or you might want to repeat the „Zoom” a couple of times.
In the video it required two „Zooms” and a couple of seconds to properly zoom to the model.

## Slide 193: Adding camera positions pt. 1
Click on the camera icon to open the list of camera positions.
Click Add to save your current view on the list.
We will add 4 different camera views, every one with different rotation and/or zoom. This is the first one, feel free to experiment.

## Slide 194: Adding camera positions pt. 2
The second camera position could be made from perspective of the other direction

## Slide 195: Adding camera positions pt. 3
Another camera position might be a side view

## Slide 196: Adding camera positions pt. 4
Final camera position can be a zoomed-out top-down view for the entire model.

## Slide 197: Presentation tab pt. 1
Select presentation and camera positions to display the list of camera positions that were previously added.

## Slide 198: Presentation tab pt. 2
Select presentation and storyboards to display a new list.
Using the + sign add a new storyboard to the model

## Slide 199: Storyboards
On the left side there are general properties of the storyboard. You might modify them, especially in terms of the column „filename” to assign a name to the video that will be recorded and to select the location the video will be saved in.
On the right side there are different keyframes that will be included in the recording. Press + icon to add new keyframes, you can double click on them to open a window of properties or modify them in the list view.

## Slide 200: Adding keyframe pt. 1
This is the window with properties of a frame. We want to select the time when this keyframe should start being displayed in our recording and the time the view will stay at selected camera position.

## Slide 201: Adding keyframe pt. 2
We want to start during simulation, after warm-up period
We want to start during simulation, after warm-up period
For the purpose of a short presentation, a few seconds of dwell time is enough.
Select the camera position for this keyframe

## Slide 202: Proposed set of keyframes
We saved 4 camera positions, so we will add 4 keyframes, one for every camera position. We will start the first keyframe at 1200, and next keyframes will start in 20s increments. For every keyframe we will set the dwell time at 10s. This means that between every keyframe there will be 10s for camera transition.

## Slide 203: Presentation tab pt. 3
In order to save the video with the next simulation run select Presentation and „Record Videos”. You can also turn on other settings, but this is optional.

## Slide 204: Video preview during simulation run
Run the simulation, you can turn on the „Quick Mode” if you do not need to watch the entire simulation and only want to make the recording. Vissim will automatically slow down to save the video within the time specified in keyframes. By default Vissim displays a preview of the video even if the simulation is run in the quick mode. Keep in mind, the preview might differ from the final video saved, if the model is big, the preview will be displayed slower than the recording due to time required for calculations in between the frames. Video compression might also change the final outcome.

## Slide 205: Recorded video
This is the video that was recorded using the steps in this presentation. Enjoy!

## Slide 206: Extra task
The vehicles are causing congestion due to the short time for changing the lane. Try modifying the network so the drivers have an opportunity to start changing their lane sooner and in return the congestion is smaller.

## Slide 207: Task 6
Record the video of the three-way intersection prepared in previous tasks. Prepare the video for at least two different scenarios (e.g. traffic lights 120s and no traffic lights). Draw conclusions based on your observations.

## Slide 208: Example solution