## Slide 1: Course C.03.06.01 Traffic assessment
Marek Pszczola

## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Factors affecting design process
Traffic
Climatic conditions
Conditions of subbase (type of soil, water level)
Type of materials that can be used
Number of layers and their thickness

## Slide 5: Traffic conditions and their influence on road and motorway pavements

## Slide 6: Influence of vehicles on road pavements
Type of vehicle,
Overall weight,
Axle configuration and number of axles,
Load of wheel and wheel numbers,
Tyre pressure,
Type of tyre,
Type of suspension (pl. zawieszenie),
Speed of vehicle.

## Slide 7: Type of vehicle
Cars (up to 3,5 t) should be omitted from the design process. They have a minor influence on pavement stresses and strains, and as a consequence on the fatigue life of pavement

## Slide 8: Type of vehicle
In the design process, only vehicles with a total weight over 3,5 t are taken into consideration:
Heavy Goods Vehicles (HGV),
HGV with trailers,
HGV with semitrailers
Buses

## Slide 9: Configuration and load of the axle
Depands on axle configuration there are:
  single axle,
  dual axle (tandem)
  triple axle (tridem).
In Poland there is limitation in axle load:
Single axle: 100 kN (115 kN),
Dual axle: 145 kN – 160 kN (depands on configuration).
In the European Union in general single axle load limitation is 115 kN but there are many exceptions based on domestic regulations: for example in Spain, France Netherland the limitation is 130 kN per axle

## Slide 10: Configuration and load of the axle
. Depending on axle configuration, there are:
  single axle,
  dual axle (tandem)
  triple axle (tridem).
In Poland, there is a limitation on axle load:
  Single axle: 100 kN (115 kN),
  Dual axle: 145 kN – 160 kN (depends on configuration).
  In the European Union, in general, single axle load limitation is 115 kN but there are many exceptions based on domestic regulations: for example in Spain, France Netherland the limitation is 130 kN per axle

## Slide 11: Wheels configuration
Dual wheels
Single wheels

## Slide 12: HGV with semitrailer

## Slide 13: Special vehicles

## Slide 14: The heaviest vehicle in the UE
44 t
Fj = 1,82 osi 115 kN
Fj = 3,18 osi 100 kN
Fj = 7,76 osi 80 kN

## Slide 15: In comparison the vehicles in USA

## Slide 16: Vehicles in USA

## Slide 17: Weight of vehicle
In the USA, the weight of a vehicle can be compensated for by an increased number of axles and wheels. As a consequence of that, the pavements can be built
not as thick as in Europe
In Europe, higher loads per axle and single wheels are allowed, so pavements have to be thicker (more durable)

## Slide 18: Load equivalency factor
There is a ratio between total number of axle load that was measured during traffic assessment (real number of vehicles) and number standard axle loads (for example 100 kN)
The exponent in that equetion can be 4 (as presented above for flexible pavements and can be equal to 10 or 12 in case of rigid pavements)

## Slide 19: Average Daily Traffic
The equivalency factors for different types of vehicles:
Heavy Goods Vehicles (HGV)
Heavy Goods Vehicles with trailer and semitrailer
Buses

## Slide 20: Methods for traffic prediction
Back calculation method – based on results of traffic measurement during whole period of road in service
General Traffic Measurements – in Poland every 5 years – last one was conducted in 2010 (www.gddkia.gov.pl)

## Slide 21: Total traffic calculations
Back calculation method – based on results of traffic measurement during whole period of road in service
General Traffic Measurements – in Poland every 5 years – last one was conducted in 2010 (www.gddkia.gov.pl)

## Slide 22: Total traffic calculations
Method 1 – traffic addition in the design period of time:
where:
Ntotal - total traffic in standard axle loads of 100 kN in the design period of time (20 years)
f1 - lane distribution factor
ADT100i – average daily traffic in each year of design period of time in standard axles of 100 kN (all lanes)
Ti – numer of years in the design period of time.

## Slide 23: Lane distribution factor

## Slide 24: Total traffic calculations
Method 2 – when the Average Daily Traffic (ADT) is known in the middle point of design period:
where:
ADT100middle- average daily traffic in the middle point of design period of time in standard axles of 100 kN (all lanes)

## Slide 25: Design traffic
Design traffic= Traffic at the beginning x growth factor

## Slide 26: Total traffic calculations
Method 3 – geometrical increase of traffic when the Average Daily Traffic (ADT) is known at the beginning point of design period:
where:
ADT1000 - average daily traffic at the beginning point of the design period in standard axles of 100 kN (all lanes)
p [%] – annual increase of traffic
t design– design period

## Slide 27: Total traffic calculations

## Slide 28: Total traffic distribution
Traffic | L [axle load 100 kN] | Ntotal [axle load 100 kN] | Ntotal [axle load 115 kN]
KR1 | ≤ 12 | ≤ 90 000 | ≤ 51 500
KR2 | 13 ÷ 70 | 90 001 ÷ 510 000 | 51 501 ÷ 291 600
KR3 | 71 ÷ 335 | 510 001 ÷ 2 500 000 | 291 601 ÷ 1 429 400
KR4 | 336 ÷ 1000 | 2 500 001 ÷ 7 300 000 | 1 429 401 ÷ 4 173 800
KR5 | 1001 ÷ 2000 | 7 300 001 ÷ 14 600 000 | 4 173 801 ÷ 8 347 600
KR6 | ≥ 2001 | ≥ 14 600 001 | ≥ 8 347 601

## Slide 29: An example – back calculated traffic
Year | 1990 | 1995 | 2000 | 2005 | 2010
Average daily traffic [number of vehicles/lane/day] | 1500 | 1830 | 2220 | 2700 | 3290
Contribution of Heavy Goods Vehicles | 9,5% | 9,2% | 8,9% | 8,8% | 8,6%
Contribution of Heavy Goods Vehicles with trailers | 8,5% | 8,1% | 7,9% | 7,8% | 7,7%
Contribusion of buses | 3,3% | 3,0% | 2,7% | 2,2% | 2,0%
Number of Heavy Goods Vehicles | 142 | 168 | 198 | 238 | 283
Number of Heavy Goods Vehicles with trailers | 127 | 148 | 175 | 211 | 253
Number of buses | 49 | 55 | 60 | 59 | 66
Notes: 29

## Slide 30: An example – back calculated traffic - cd
Year | 1990 | 1995 | 2000 | 2005 | 2010
ADT 100HGT – HGT (r1=0,109) | 15,5 | 18,4 | 21,5 | 25,9 | 30,8
AVT 100HGT+T – HGT with trailers (r2=1,95) | 248,6 | 289,0 | 342,0 | 410,7 | 494,0
AVT 100bus – BUSES (r2=0,594) | 29,4 | 32,6 | 35,6 | 35,3 | 39,1
AVTYEAR=Ʃ(AVTHGV, HGV+T, BUS) axle100 kN/day/lane | 294 | 340 | 399 | 472 | 564
AVT (20 years) | 410 axle load 100 kN/day/lane |  |  |  | 
Total traffic (20 years) | 2,99 milionów axle loads 100 kN/lane (KR4) |  |  |  | 
Notes: 30

## Slide 31: An example – Method 3
Important data:
  National road (2 lanes each direction) – lane distribution factor f1=0,45,
  Data from site measurement in 2005
Type of vehicles | Number of vehicles (2 lanes each direction in 2005 [number of vehicles per day] | Equivalent factors | Number of design axles 100 kN/day In 2005 (ADT1000)
HGV | 896 | r1 = 0,109 | 98
HGV with trailers | 1584 | r2 = 1,950 | 3089
Buses | 1152 | r3 = 0,594 | 684
Sum: |  | ADT1000: | 3871

## Slide 32: An example – Method 3
Important data:
  The beginning year – 2005,
  Design period: 20 years
  Growth factor per year: 2%
The equation:

## Slide 33: An example – Method 3
So:
Finally:
Ntotal=15,45 mln axle load 100 kN/design lane
And:
Ntotal=8,83 mln axle load 115 kN/design lane