## Slide 1: Traffic Engineering
Exercise 4.3: Traffic Signal Design Phasing and Timing

## Slide 2: Exercise-1
Given:
Cycle length = 80 s
Green = 35 s
Yellow + all-red = 5 s
Start-up lost time = 2 s
Clearance lost time = 3 s
Saturation headway = 2.2 s/veh
Calculate:
Compute saturation flow rate
Compute effective green time
Compute lane capacity

## Slide 3: Exercise-2
A signalized intersection approach has three lanes with no exclusive left- or right-turning lanes. The approach has a 40-second green out of a 75-second cycle. The yellow plus all-red intervals for the phase total 4.0 seconds. If the start-up lost time is 2.3 s/phase, the clearance lost time is 1.1 s/phase, and the saturation headway is 2.48 s/veh under prevailing conditions, what is the capacity of the intersection approach?