## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Estimating design traffic for a regional road
Exercise 2
Mixed exercise | Estimated duration: 90 minutes
Topic: Traffic assessment, heavy vehicles, standard axle loads
Local context: Yaoundé–Bafoussam regional corridor, Cameroon
PowerPoint-ready classroom exercise
AfroTrans — Road Construction | Exercise 2
MSc Road Transportation Systems Engineering

## Slide 5: Slide 2. Learning objectives
Traffic assessment, heavy vehicles, standard axle loads | Yaoundé–Bafoussam regional corridor, Cameroon
• Identify vehicle classes relevant for pavement design.
• Convert heavy vehicles into equivalent standard axles.
• Estimate design traffic using simple growth assumptions.
• Classify pavement traffic demand at a basic level.
AfroTrans — Road Construction | Exercise 2
MSc Road Transportation Systems Engineering

## Slide 6: Slide 3. Background / case study
Traffic assessment, heavy vehicles, standard axle loads | Yaoundé–Bafoussam regional corridor, Cameroon
• A two-lane regional road in Cameroon carries passenger cars, buses, heavy goods vehicles and trucks with trailers.
• Passenger cars are omitted from structural pavement design because their effect on pavement fatigue is minor.
• Assumed data for educational purposes.
AfroTrans — Road Construction | Exercise 2
MSc Road Transportation Systems Engineering

## Slide 7: Slide 4. Student task
Traffic assessment, heavy vehicles, standard axle loads | Yaoundé–Bafoussam regional corridor, Cameroon
1. Calculate ADT100 at the beginning of the design period.
2. Apply the lane distribution factor.
3. Estimate total standard axle loads over 20 years.
4. Select an approximate traffic category.
5. Discuss why overloaded trucks may change the design decision.
AfroTrans — Road Construction | Exercise 2
MSc Road Transportation Systems Engineering

## Slide 8: Slide 5. Data / materials
Traffic assessment, heavy vehicles, standard axle loads | Yaoundé–Bafoussam regional corridor, Cameroon
• Design period: 20 years; annual traffic growth ignored for this simplified exercise.
• Lane distribution factor: 0.50; use 365 days/year.
Vehicle type | Vehicles/day | Equivalency factor
───────────────────┼──────────────────┼─────────────────────
HGV | 260 | 0.109
HGV with trailer | 180 | 1.950
Bus | 120 | 0.594
Category | Total standard axles
───────────┼───────────────────────
Low | < 1.0 million
Medium | 1.0–5.0 million
High | > 5.0 million
AfroTrans — Road Construction | Exercise 2
MSc Road Transportation Systems Engineering

## Slide 9: Slide 6. Work organisation
Traffic assessment, heavy vehicles, standard axle loads | Yaoundé–Bafoussam regional corridor, Cameroon
• 20 min — individual calculation of ADT100.
• 20 min — pair check and correction.
• 20 min — group discussion on overloaded trucks.
• 20 min — short group reporting.
• 10 min — teacher summary.
AfroTrans — Road Construction | Exercise 2
MSc Road Transportation Systems Engineering

## Slide 10: Slide 7. Expected answer / solution
Traffic assessment, heavy vehicles, standard axle loads | Yaoundé–Bafoussam regional corridor, Cameroon
• HGV: 260 × 0.109 = 28.3 standard axles/day.
• HGV with trailer: 180 × 1.950 = 351.0 standard axles/day.
• Bus: 120 × 0.594 = 71.3 standard axles/day.
• Total ADT100 = 450.6; design lane = 450.6 × 0.50 = 225.3 standard axles/day/lane.
• 20-year total = 225.3 × 365 × 20 = 1,644,690 standard axles → medium traffic.
• Overloaded trucks would increase equivalent axle loads and may require stronger pavement design.
AfroTrans — Road Construction | Exercise 2
MSc Road Transportation Systems Engineering

## Slide 11: Slide 8. Teacher notes
Traffic assessment, heavy vehicles, standard axle loads | Yaoundé–Bafoussam regional corridor, Cameroon
• Observe whether students omit passenger cars correctly and understand axle equivalency.
• Typical mistakes: using all vehicles, forgetting the lane distribution factor, treating buses and trucks as equal.
• Extension: how would 3% annual traffic growth affect the result?
AfroTrans — Road Construction | Exercise 2
MSc Road Transportation Systems Engineering