## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Blending two aggregate stockpiles
Exercise 6
Individual exercise with group discussion | Estimated duration: 90 minutes
Topic: Aggregate gradation, stockpile blending, job mix formula
Local context: Asphalt mixture for an urban road in Douala, Cameroon
PowerPoint-ready classroom exercise
AfroTrans — Road Construction | Exercise 6
MSc Road Transportation Systems Engineering

## Slide 5: Slide 2. Learning objectives
Aggregate gradation, stockpile blending, job mix formula | Asphalt mixture for an urban road in Douala, Cameroon
• Calculate combined aggregate gradation.
• Compare gradation with specification limits.
• Understand the role of stockpile blending.
• Identify whether a blend is acceptable.
AfroTrans — Road Construction | Exercise 6
MSc Road Transportation Systems Engineering

## Slide 6: Slide 3. Background / case study
Aggregate gradation, stockpile blending, job mix formula | Asphalt mixture for an urban road in Douala, Cameroon
• An asphalt plant in Douala has two aggregate stockpiles.
• The contractor proposes a blend: 60% crushed stone and 40% sand.
• Students must check whether the blend fits a simplified gradation envelope.
• Assumed data for educational purposes.
AfroTrans — Road Construction | Exercise 6
MSc Road Transportation Systems Engineering

## Slide 7: Slide 4. Student task
Aggregate gradation, stockpile blending, job mix formula | Asphalt mixture for an urban road in Douala, Cameroon
1. Calculate percent passing for the combined blend.
2. Compare results with specification limits.
3. Mark each sieve as pass/fail.
4. Decide whether the blend can be accepted.
5. Suggest one correction if the blend fails.
AfroTrans — Road Construction | Exercise 6
MSc Road Transportation Systems Engineering

## Slide 8: Slide 5. Data / materials
Aggregate gradation, stockpile blending, job mix formula | Asphalt mixture for an urban road in Douala, Cameroon
• Formula: p = A × a + B × b, where A and B are percent passing for each stockpile and a and b are decimal fractions in the blend.
• Blend: 60% crushed stone, 40% sand.
Sieve | Crushed stone passing | Sand passing | Lower limit | Upper limit
───────────┼───────────────────────────┼──────────────────┼─────────────────┼──────────────
12.5 mm | 100 | 100 | 90 | 100
9.5 mm | 82 | 100 | 70 | 95
4.75 mm | 45 | 98 | 40 | 70
2.36 mm | 20 | 90 | 25 | 55
0.075 mm | 3 | 8 | 3 | 8
AfroTrans — Road Construction | Exercise 6
MSc Road Transportation Systems Engineering

## Slide 9: Slide 6. Work organisation
Aggregate gradation, stockpile blending, job mix formula | Asphalt mixture for an urban road in Douala, Cameroon
• 30 min — individual calculations.
• 25 min — compare in pairs.
• 25 min — group interpretation.
• 5 min — class answer check.
• 5 min — teacher conclusion.
AfroTrans — Road Construction | Exercise 6
MSc Road Transportation Systems Engineering

## Slide 10: Slide 7. Expected answer / solution
Aggregate gradation, stockpile blending, job mix formula | Asphalt mixture for an urban road in Douala, Cameroon
• 12.5 mm: 100×0.6 + 100×0.4 = 100 → pass.
• 9.5 mm: 82×0.6 + 100×0.4 = 89.2 → pass.
• 4.75 mm: 45×0.6 + 98×0.4 = 66.2 → pass.
• 2.36 mm: 20×0.6 + 90×0.4 = 48.0 → pass.
• 0.075 mm: 3×0.6 + 8×0.4 = 5.0 → pass.
• Decision: blend is acceptable under simplified limits.
AfroTrans — Road Construction | Exercise 6
MSc Road Transportation Systems Engineering

## Slide 11: Slide 8. Teacher notes
Aggregate gradation, stockpile blending, job mix formula | Asphalt mixture for an urban road in Douala, Cameroon
• Observe whether students use decimal fractions correctly and check every sieve.
• Typical mistakes: using 60 instead of 0.60; checking only one sieve; assuming gradation is acceptable based on visual appearance.
• Extension: what risks appear if too much natural sand is used?
AfroTrans — Road Construction | Exercise 6
MSc Road Transportation Systems Engineering