## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Earthworks volume for a rural road section
Exercise 1
Individual exercise | Estimated duration: 90 minutes
Topic: Earthworks, cut/fill calculation, road construction planning
Local context: Rural feeder road near Goma, DR Congo
PowerPoint-ready classroom exercise
AfroTrans — Road Construction | Exercise 1
MSc Road Transportation Systems Engineering

## Slide 5: Slide 2. Learning objectives
Earthworks, cut/fill calculation, road construction planning | Rural feeder road near Goma, DR Congo
• Calculate earthwork volume using cross-section areas.
• Distinguish between cut and fill sections.
• Interpret whether soil must be imported or removed.
• Explain why balancing earthworks reduces construction cost.
AfroTrans — Road Construction | Exercise 1
MSc Road Transportation Systems Engineering

## Slide 6: Slide 3. Background / case study
Earthworks, cut/fill calculation, road construction planning | Rural feeder road near Goma, DR Congo
• A rural feeder road near Goma is being improved to provide access to a local agricultural market.
• The design team has measured cross-section areas at three points.
• The contractor must estimate the earthworks volume before planning excavation, transport and compaction.
• Assumed data for educational purposes.
AfroTrans — Road Construction | Exercise 1
MSc Road Transportation Systems Engineering

## Slide 7: Slide 4. Student task
Earthworks, cut/fill calculation, road construction planning | Rural feeder road near Goma, DR Congo
1. Calculate the earthwork volume between cross-sections A–B and B–C.
2. Determine whether each section is mainly cut or fill.
3. Calculate the total volume of cut and fill.
4. Decide whether the project has surplus soil or soil deficit.
5. Propose one practical measure to reduce soil transport distance.
AfroTrans — Road Construction | Exercise 1
MSc Road Transportation Systems Engineering

## Slide 8: Slide 5. Data / materials
Earthworks, cut/fill calculation, road construction planning | Rural feeder road near Goma, DR Congo
• Use formula: V = 1/2 × (F1 + F2) × L
• Assumption: cut material is suitable for embankment construction; no shrinkage or bulking factor is considered.
Section | Length L | Area at start F1 | Area at end F2 | Type
──────────┼──────────────┼──────────────────────┼────────────────────┼───────
A–B | 40 m | 12 m² | 18 m² | Cut
B–C | 40 m | 8 m² | 14 m² | Fill
AfroTrans — Road Construction | Exercise 1
MSc Road Transportation Systems Engineering

## Slide 9: Slide 6. Work organisation
Earthworks, cut/fill calculation, road construction planning | Rural feeder road near Goma, DR Congo
• 20 min — individual calculation.
• 20 min — compare results in pairs.
• 20 min — discuss soil balance in small groups.
• 20 min — selected students present results.
• 10 min — teacher summary.
AfroTrans — Road Construction | Exercise 1
MSc Road Transportation Systems Engineering

## Slide 10: Slide 7. Expected answer / solution
Earthworks, cut/fill calculation, road construction planning | Rural feeder road near Goma, DR Congo
• Section A–B: V = 1/2 × (12 + 18) × 40 = 600 m³ cut.
• Section B–C: V = 1/2 × (8 + 14) × 40 = 440 m³ fill.
• Soil balance: cut = 600 m³, fill = 440 m³, surplus = 160 m³.
• Interpretation: if suitable, surplus material can be used for nearby shoulders, embankment widening or local access improvements.
AfroTrans — Road Construction | Exercise 1
MSc Road Transportation Systems Engineering

## Slide 11: Slide 8. Teacher notes
Earthworks, cut/fill calculation, road construction planning | Rural feeder road near Goma, DR Congo
• Observe correct use of the cross-section formula and correct distinction between cut and fill.
• Typical mistakes: adding areas without multiplying by length; mixing cut and fill volumes; ignoring material suitability.
• Key discussion: what happens if cut material is unsuitable? How do rainfall and soil moisture affect earthworks in tropical regions?
AfroTrans — Road Construction | Exercise 1
MSc Road Transportation Systems Engineering

## Slide 12: Questions?
Have you reviewed the syllabuses we sent you?
Have you selected from them which subjects you would like to include in the programs of study you are creating?