## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Aggregate source selection
Exercise 5
Group exercise | Estimated duration: 90 minutes
Topic: Aggregates, rock origin, processing, transport cost
Local context: Road construction near a river and a quarry in DR Congo
PowerPoint-ready classroom exercise
AfroTrans — Road Construction | Exercise 5
MSc Road Transportation Systems Engineering

## Slide 5: Slide 2. Learning objectives
Aggregates, rock origin, processing, transport cost | Road construction near a river and a quarry in DR Congo
• Compare aggregate sources for road construction.
• Consider durability, shape, processing and transport.
• Select suitable aggregates for asphalt and base layers.
• Justify material choice under local constraints.
AfroTrans — Road Construction | Exercise 5
MSc Road Transportation Systems Engineering

## Slide 6: Slide 3. Background / case study
Aggregates, rock origin, processing, transport cost | Road construction near a river and a quarry in DR Congo
• A road contractor has access to two local aggregate sources: river gravel from a nearby river and crushed basalt from a quarry farther away.
• The road will carry medium heavy truck traffic and must perform well during rainy seasons.
• Assumed data for educational purposes.
AfroTrans — Road Construction | Exercise 5
MSc Road Transportation Systems Engineering

## Slide 7: Slide 4. Student task
Aggregates, rock origin, processing, transport cost | Road construction near a river and a quarry in DR Congo
1. Compare the two aggregate sources.
2. Decide which material is better for asphalt mixture.
3. Decide which material may be used for subbase or base.
4. Identify additional processing needed.
5. Prepare a short procurement recommendation.
AfroTrans — Road Construction | Exercise 5
MSc Road Transportation Systems Engineering

## Slide 8: Slide 5. Data / materials
Aggregates, rock origin, processing, transport cost | Road construction near a river and a quarry in DR Congo
• Assumption: river material may contain clay and organic contamination after flooding.
Parameter | River gravel | Crushed basalt
──────────────────────┼────────────────────────────────┼──────────────────
Distance to site | 8 km | 45 km
Particle shape | Rounded | Angular
Expected durability | Medium | High
Processing needed | Washing; possible crushing | Sizing; washing
Transport cost | Low | High
Availability | Seasonal | Stable
AfroTrans — Road Construction | Exercise 5
MSc Road Transportation Systems Engineering

## Slide 9: Slide 6. Work organisation
Aggregates, rock origin, processing, transport cost | Road construction near a river and a quarry in DR Congo
• 15 min — group comparison table.
• 15 min — decision for asphalt mixture.
• 25 min — decision for base/subbase.
• 25 min — group recommendation.
• 10 min — teacher summary.
AfroTrans — Road Construction | Exercise 5
MSc Road Transportation Systems Engineering

## Slide 10: Slide 7. Expected answer / solution
Aggregates, rock origin, processing, transport cost | Road construction near a river and a quarry in DR Congo
• Crushed basalt is preferred for asphalt mixtures because angular particles improve interlock.
• River gravel may be acceptable for lower layers if cleaned, tested and possibly crushed.
• River gravel is cheaper but quality risk is higher.
• Final decision requires gradation, clay content, abrasion and soundness tests.
• Procurement recommendation: use basalt for asphalt wearing/base asphalt layers; use processed river gravel for selected subbase only after quality control.
AfroTrans — Road Construction | Exercise 5
MSc Road Transportation Systems Engineering

## Slide 11: Slide 8. Teacher notes
Aggregates, rock origin, processing, transport cost | Road construction near a river and a quarry in DR Congo
• Observe whether students consider both transport cost and performance.
• Typical mistakes: selecting only the cheapest material; ignoring particle shape; forgetting contamination risk.
• Discussion: when is local material use justified? How can laboratory testing reduce construction risk?
AfroTrans — Road Construction | Exercise 5
MSc Road Transportation Systems Engineering