## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Pavement edge failure diagnosis
Exercise 4
Mixed exercise | Estimated duration: 45 minutes
Topic: Pavement edge construction, compaction, premature failures
Local context: Rural road carrying trucks to an agricultural area in Cameroon
PowerPoint-ready classroom exercise
AfroTrans — Road Construction | Exercise 4
MSc Road Transportation Systems Engineering

## Slide 5: Slide 2. Learning objectives
Pavement edge construction, compaction, premature failures | Rural road carrying trucks to an agricultural area in Cameroon
• Identify causes of pavement edge failure.
• Connect construction details with long-term performance.
• Propose corrective construction measures.
• Discuss quality control during base and asphalt layer construction.
AfroTrans — Road Construction | Exercise 4
MSc Road Transportation Systems Engineering

## Slide 6: Slide 3. Background / case study
Pavement edge construction, compaction, premature failures | Rural road carrying trucks to an agricultural area in Cameroon
• A newly paved rural road began to show edge cracking after two rainy seasons.
• Field observations: trucks often drive close to the edge; shoulder is weak and poorly compacted; base course was placed irregularly; drainage ditch is partially blocked.
• Assumed data for educational purposes.
AfroTrans — Road Construction | Exercise 4
MSc Road Transportation Systems Engineering

## Slide 7: Slide 4. Student task
Pavement edge construction, compaction, premature failures | Rural road carrying trucks to an agricultural area in Cameroon
1. Identify at least four probable causes of edge failure.
2. Rank them from most to least important.
3. Propose three preventive measures during construction.
4. Propose two maintenance actions after opening the road.
5. Prepare a short group explanation.
AfroTrans — Road Construction | Exercise 4
MSc Road Transportation Systems Engineering

## Slide 8: Slide 5. Data / materials
Pavement edge construction, compaction, premature failures | Rural road carrying trucks to an agricultural area in Cameroon
• Field notes for the diagnosis exercise.
Parameter | Observation
──────────────────┼─────────────────────────────────────────────────────
Pavement width | 6.0 m
Shoulder width | 0.5 m
Base course | Crushed aggregate
Asphalt edge | Not vertically supported
Water near edge | Standing water visible
Traffic | Heavy trucks to banana and cocoa collection points
AfroTrans — Road Construction | Exercise 4
MSc Road Transportation Systems Engineering

## Slide 9: Slide 6. Work organisation
Pavement edge construction, compaction, premature failures | Rural road carrying trucks to an agricultural area in Cameroon
• 15 min — individual cause identification.
• 30 min — group ranking and solution table.
• 25 min — group presentation.
• 10 min — class discussion.
• 10 min — teacher conclusion.
AfroTrans — Road Construction | Exercise 4
MSc Road Transportation Systems Engineering

## Slide 10: Slide 7. Expected answer / solution
Pavement edge construction, compaction, premature failures | Rural road carrying trucks to an agricultural area in Cameroon
• Probable causes: weak/poorly compacted shoulder; water infiltration and blocked drainage; insufficient compaction near pavement edge; inadequate construction detail of base/asphalt edge; heavy wheel loads close to road edge.
• Preventive measures: extend and compact base layers correctly; provide stable shoulder support; ensure drainage continuity; control compaction at edge; avoid placing aggregate on organic soil or grass.
• Maintenance actions: restore drainage, strengthen shoulder and seal edge cracks.
AfroTrans — Road Construction | Exercise 4
MSc Road Transportation Systems Engineering

## Slide 11: Slide 8. Teacher notes
Pavement edge construction, compaction, premature failures | Rural road carrying trucks to an agricultural area in Cameroon
• Observe whether students connect structural, drainage and traffic factors.
• Typical mistakes: treating cracking only as an asphalt problem; ignoring shoulder support; ignoring water.
• Extension: how could road width or lane marking reduce edge loading?
AfroTrans — Road Construction | Exercise 4
MSc Road Transportation Systems Engineering