## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Inspection of asphalt production and paving operations
Exercise 10
Mixed exercise | Estimated duration: 90 minutes
Topic: Asphalt plant production, HMA delivery, paving inspection, defects
Local context: Asphalt paving of an urban arterial road in Kinshasa, DR Congo
PowerPoint-ready classroom exercise
AfroTrans — Road Construction | Exercise 10
MSc Road Transportation Systems Engineering

## Slide 5: Slide 2. Learning objectives
Asphalt plant production, HMA delivery, paving inspection, defects | Asphalt paving of an urban arterial road in Kinshasa, DR Congo
• Identify key inspection items during asphalt paving.
• Connect visible defects with possible construction causes.
• Understand the need to balance plant, trucking, paving and compaction.
• Propose corrective actions during field works.
AfroTrans — Road Construction | Exercise 10
MSc Road Transportation Systems Engineering

## Slide 6: Slide 3. Background / case study
Asphalt plant production, HMA delivery, paving inspection, defects | Asphalt paving of an urban arterial road in Kinshasa, DR Congo
• During paving works, the site engineer observes: uneven mat texture, visible steam from the mix, segregation near the edge, paver stops caused by irregular truck delivery and insufficient tack coat in some areas.
• Assumed data for educational purposes.
AfroTrans — Road Construction | Exercise 10
MSc Road Transportation Systems Engineering

## Slide 7: Slide 4. Student task
Asphalt plant production, HMA delivery, paving inspection, defects | Asphalt paving of an urban arterial road in Kinshasa, DR Congo
1. Classify each observation as material, equipment, logistics or workmanship issue.
2. Identify likely causes.
3. Propose immediate corrective actions.
4. Decide whether paving may continue or should stop.
5. Prepare an inspection checklist.
AfroTrans — Road Construction | Exercise 10
MSc Road Transportation Systems Engineering

## Slide 8: Slide 5. Data / materials
Asphalt plant production, HMA delivery, paving inspection, defects | Asphalt paving of an urban arterial road in Kinshasa, DR Congo
• Inspection items: uniformity, temperature, appearance, geometrics, placing procedures and joints.
Observation | Inspection focus
───────────────────────────────────────┼─────────────────────────────────
A. Steam visible from HMA | Temperature / moisture
B. Segregation behind paver | Uniformity / material handling
C. Paver stops every 10–15 minutes | Logistics / production balance
D. Tack coat missing on 20 m section | Surface preparation
E. Mat thickness varies by 20 mm | Geometrics / screed control
F. Longitudinal joint appears open | Joint construction
AfroTrans — Road Construction | Exercise 10
MSc Road Transportation Systems Engineering

## Slide 9: Slide 6. Work organisation
Asphalt plant production, HMA delivery, paving inspection, defects | Asphalt paving of an urban arterial road in Kinshasa, DR Congo
• 15 min — individual classification.
• 25 min — group cause/action table.
• 25 min — prepare checklist.
• 15 min — group reporting.
• 10 min — teacher conclusion.
AfroTrans — Road Construction | Exercise 10
MSc Road Transportation Systems Engineering

## Slide 10: Slide 7. Expected answer / solution
Asphalt plant production, HMA delivery, paving inspection, defects | Asphalt paving of an urban arterial road in Kinshasa, DR Congo
• A: possible moisture in aggregate or mix; check plant drying and weather.
• B: material handling, paver feed or truck loading/unloading problem.
• C: imbalance between plant, trucking and paving; improve delivery coordination.
• D: stop paving and apply tack coat correctly.
• E: check screed control, head of material and paver speed.
• F: poor joint construction or compaction.
• Decision: continue only after correcting tack coat, delivery balance and paver settings; defective sections may require removal or corrective treatment.
AfroTrans — Road Construction | Exercise 10
MSc Road Transportation Systems Engineering

## Slide 11: Slide 8. Teacher notes
Asphalt plant production, HMA delivery, paving inspection, defects | Asphalt paving of an urban arterial road in Kinshasa, DR Congo
• Observe whether students propose actions during construction, not only after failure.
• Typical mistakes: treating all defects as material defects; ignoring paver logistics; continuing paving despite missing tack coat.
• Extension: how does traffic congestion in Kinshasa affect HMA delivery temperature?
AfroTrans — Road Construction | Exercise 10
MSc Road Transportation Systems Engineering