## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Cross-section for an urban access road
Exercise 3
Group exercise | Estimated duration: 90 minutes
Topic: Cross-section drawings, drainage, sidewalks, shoulders
Local context: Urban road serving a school and market in Butembo, DR Congo
PowerPoint-ready classroom exercise
AfroTrans — Road Construction | Exercise 3
MSc Road Transportation Systems Engineering

## Slide 5: Slide 2. Learning objectives
Cross-section drawings, drainage, sidewalks, shoulders | Urban road serving a school and market in Butembo, DR Congo
• Identify basic elements of a road cross-section.
• Adapt cross-section elements to local road function.
• Include pedestrians, drainage and pavement edge details.
• Justify design choices under limited space conditions.
AfroTrans — Road Construction | Exercise 3
MSc Road Transportation Systems Engineering

## Slide 6: Slide 3. Background / case study
Cross-section drawings, drainage, sidewalks, shoulders | Urban road serving a school and market in Butembo, DR Congo
• A 600 m urban access road connects a school, a local market, a health centre and residential plots.
• The road has many pedestrians, motorcycles and minibuses.
• Drainage problems occur during heavy rainfall.
• Assumed data for educational purposes.
AfroTrans — Road Construction | Exercise 3
MSc Road Transportation Systems Engineering

## Slide 7: Slide 4. Student task
Cross-section drawings, drainage, sidewalks, shoulders | Urban road serving a school and market in Butembo, DR Congo
1. Prepare a simple cross-section concept.
2. Select lane width, sidewalk width and drainage solution.
3. Add pavement edge protection.
4. Mark key dimensions.
5. Explain three design decisions.
AfroTrans — Road Construction | Exercise 3
MSc Road Transportation Systems Engineering

## Slide 8: Slide 5. Data / materials
Cross-section drawings, drainage, sidewalks, shoulders | Urban road serving a school and market in Butembo, DR Congo
• Available corridor width: 12.0 m.
• Minimum required elements: two traffic lanes, at least one sidewalk, drainage element, pavement edge support and safe walking space near school.
Element | Suggested value
──────────────────────────────────┼──────────────────
Lane width | 3.0–3.25 m
Sidewalk width | 1.5–2.0 m
Drainage ditch or covered drain | 0.5–1.0 m
Shoulders or edge strips | 0.25–0.50 m
AfroTrans — Road Construction | Exercise 3
MSc Road Transportation Systems Engineering

## Slide 9: Slide 6. Work organisation
Cross-section drawings, drainage, sidewalks, shoulders | Urban road serving a school and market in Butembo, DR Congo
• 15 min — individual sketch.
• 35 min — group cross-section drawing.
• 20 min — group prepares design justification.
• 10 min — two groups present.
• 10 min — teacher feedback.
AfroTrans — Road Construction | Exercise 3
MSc Road Transportation Systems Engineering

## Slide 10: Slide 7. Expected answer / solution
Cross-section drawings, drainage, sidewalks, shoulders | Urban road serving a school and market in Butembo, DR Congo
• Example solution: 2 × 3.0 m traffic lanes = 6.0 m.
• 1 × 2.0 m sidewalk near the school side.
• 1 × 0.75 m covered drain.
• 2 × 0.50 m edge strips.
• Remaining space for local adjustment / verge.
• Justification: sidewalk protects pedestrians; drainage reduces water damage; edge strips improve pavement edge support under traffic loads.
AfroTrans — Road Construction | Exercise 3
MSc Road Transportation Systems Engineering

## Slide 11: Slide 8. Teacher notes
Cross-section drawings, drainage, sidewalks, shoulders | Urban road serving a school and market in Butembo, DR Congo
• Observe whether groups include drainage, pedestrians and pavement edge support.
• Typical mistakes: using full width only for cars; forgetting drainage; no transition between pavement and shoulder.
• Discussion: should the sidewalk be on one or both sides? What changes if motorcycles dominate traffic?
AfroTrans — Road Construction | Exercise 3
MSc Road Transportation Systems Engineering