## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Interpreting Marshall mix design results
Exercise 9
Individual exercise | Estimated duration: 120 minutes
Topic: Asphalt mixture design, Marshall method, stability, flow, air voids
Local context: Asphalt mix for a medium-traffic road in Cameroon
PowerPoint-ready classroom exercise
AfroTrans — Road Construction | Exercise 9
MSc Road Transportation Systems Engineering

## Slide 5: Slide 2. Learning objectives
Asphalt mixture design, Marshall method, stability, flow, air voids | Asphalt mix for a medium-traffic road in Cameroon
• Interpret simple Marshall test results.
• Compare stability, flow and air voids with criteria.
• Select a preliminary binder content.
• Explain the trade-off between durability and stability.
AfroTrans — Road Construction | Exercise 9
MSc Road Transportation Systems Engineering

## Slide 6: Slide 3. Background / case study
Asphalt mixture design, Marshall method, stability, flow, air voids | Asphalt mix for a medium-traffic road in Cameroon
• A laboratory has prepared asphalt mixture specimens with different binder contents.
• The road will serve a regional market and carry medium truck traffic.
• Students must select a preliminary optimum binder content.
• Assumed data for educational purposes.
AfroTrans — Road Construction | Exercise 9
MSc Road Transportation Systems Engineering

## Slide 7: Slide 4. Student task
Asphalt mixture design, Marshall method, stability, flow, air voids | Asphalt mix for a medium-traffic road in Cameroon
1. Check which binder contents meet all criteria.
2. Select the best binder content.
3. Explain why very low or very high binder content is risky.
4. Prepare one technical statement for the contractor.
AfroTrans — Road Construction | Exercise 9
MSc Road Transportation Systems Engineering

## Slide 8: Slide 5. Data / materials
Asphalt mixture design, Marshall method, stability, flow, air voids | Asphalt mix for a medium-traffic road in Cameroon
• Medium traffic criteria: stability ≥ 5,338 N; flow 8–16 units; air voids 3–5%.
Binder content | Stability | Flow | Air voids
─────────────────┼───────────────┼──────────┼────────────
4.5% | 5,800 N | 9 | 5.8%
5.0% | 6,200 N | 11 | 4.6%
5.5% | 6,000 N | 14 | 3.7%
6.0% | 5,300 N | 17 | 2.8%
AfroTrans — Road Construction | Exercise 9
MSc Road Transportation Systems Engineering

## Slide 9: Slide 6. Work organisation
Asphalt mixture design, Marshall method, stability, flow, air voids | Asphalt mix for a medium-traffic road in Cameroon
• 20 min — individual pass/fail table.
• 30 min — pair comparison.
• 35 min — class discussion on optimum binder content.
• 25 min — technical statement writing.
• 10 min — teacher summary.
AfroTrans — Road Construction | Exercise 9
MSc Road Transportation Systems Engineering

## Slide 10: Slide 7. Expected answer / solution
Asphalt mixture design, Marshall method, stability, flow, air voids | Asphalt mix for a medium-traffic road in Cameroon
• 4.5%: fail — air voids too high.
• 5.0%: pass.
• 5.5%: pass.
• 6.0%: fail — stability slightly too low, flow too high and air voids too low.
• Preliminary selection: 5.0% or 5.5% acceptable. 5.5% may improve durability due to lower air voids, but should be checked against rutting risk.
• Final choice should consider VMA, density and project specification.
• Technical statement: the mix should not be approved at 4.5% or 6.0%; binder content around 5.0–5.5% should be further verified.
AfroTrans — Road Construction | Exercise 9
MSc Road Transportation Systems Engineering

## Slide 11: Slide 8. Teacher notes
Asphalt mixture design, Marshall method, stability, flow, air voids | Asphalt mix for a medium-traffic road in Cameroon
• Observe whether students check all criteria, not only stability.
• Typical mistakes: choosing maximum stability only; ignoring flow; accepting too-low air voids.
• Extension: what additional test would help evaluate rutting resistance?
AfroTrans — Road Construction | Exercise 9
MSc Road Transportation Systems Engineering