## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Selecting asphalt binder product for field use
Exercise 8
Group exercise | Estimated duration: 90 minutes
Topic: Asphalt binders, asphalt cement, cutbacks, emulsions, tack/prime coats
Local context: Staged road rehabilitation in DR Congo
PowerPoint-ready classroom exercise
AfroTrans — Road Construction | Exercise 8
MSc Road Transportation Systems Engineering

## Slide 5: Slide 2. Learning objectives
Asphalt binders, asphalt cement, cutbacks, emulsions, tack/prime coats | Staged road rehabilitation in DR Congo
• Distinguish asphalt cement, cutback and emulsion.
• Select binder product for different construction operations.
• Explain asphalt vs tar terminology.
• Assess environmental and safety implications.
AfroTrans — Road Construction | Exercise 8
MSc Road Transportation Systems Engineering

## Slide 6: Slide 3. Background / case study
Asphalt binders, asphalt cement, cutbacks, emulsions, tack/prime coats | Staged road rehabilitation in DR Congo
• A contractor is rehabilitating a paved road section near Butembo.
• Three operations are planned: bonding a new asphalt layer to an existing pavement; treating an unbound granular base before paving; producing hot mix asphalt at a plant.
• Students must select suitable binder products.
• Assumed data for educational purposes.
AfroTrans — Road Construction | Exercise 8
MSc Road Transportation Systems Engineering

## Slide 7: Slide 4. Student task
Asphalt binders, asphalt cement, cutbacks, emulsions, tack/prime coats | Staged road rehabilitation in DR Congo
1. Match each field operation with a binder product.
2. Explain why the product is appropriate.
3. Identify one construction risk for each operation.
4. Discuss why “asphalt” and “tar” should not be used as identical terms.
AfroTrans — Road Construction | Exercise 8
MSc Road Transportation Systems Engineering

## Slide 8: Slide 5. Data / materials
Asphalt binders, asphalt cement, cutbacks, emulsions, tack/prime coats | Staged road rehabilitation in DR Congo
• Constraints: hot climate, limited safety equipment, traffic must reopen quickly and environmental protection is required.
Operations | Available products
───────────────────────────────────────────┼─────────────────────────
A. Tack coat between asphalt layers | 1. Asphalt cement
B. Prime coat on granular base | 2. Asphalt emulsion
C. Binder for hot mix asphalt production | 3. Slow-curing cutback
| 4. Coal tar product
AfroTrans — Road Construction | Exercise 8
MSc Road Transportation Systems Engineering

## Slide 9: Slide 6. Work organisation
Asphalt binders, asphalt cement, cutbacks, emulsions, tack/prime coats | Staged road rehabilitation in DR Congo
• 10 min — group matching.
• 30 min — prepare justification.
• 20 min — risk identification.
• 20 min — class discussion.
• 10 min — teacher summary.
AfroTrans — Road Construction | Exercise 8
MSc Road Transportation Systems Engineering

## Slide 10: Slide 7. Expected answer / solution
Asphalt binders, asphalt cement, cutbacks, emulsions, tack/prime coats | Staged road rehabilitation in DR Congo
• Recommended matching: A. Tack coat — asphalt emulsion.
• B. Prime coat — slow-curing cutback or suitable emulsion, depending on local specifications.
• C. HMA binder — asphalt cement.
• Coal tar is not recommended as a standard road asphalt binder; it has different origin and chemical behaviour.
• Main risks: excessive tack coat can cause slippage or bleeding; insufficient prime penetration reduces bonding; wrong asphalt cement grade may affect rutting or cracking resistance.
AfroTrans — Road Construction | Exercise 8
MSc Road Transportation Systems Engineering

## Slide 11: Slide 8. Teacher notes
Asphalt binders, asphalt cement, cutbacks, emulsions, tack/prime coats | Staged road rehabilitation in DR Congo
• Observe whether students understand function, not only product names.
• Typical mistakes: selecting asphalt cement for tack coat without considering application; treating tar and asphalt as synonyms; ignoring curing time.
• Extension: how would heavy rainfall change timing of prime or tack coat application?
AfroTrans — Road Construction | Exercise 8
MSc Road Transportation Systems Engineering