## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Project 03. Treatment selection
• Exercise type: Mixed exercise
• Estimated duration: 90 minutes
• Course topic: asphalt pavement maintenance and rehabilitation treatments

## Slide 5: Learning objectives
• Match surface treatments with pavement needs.
• Distinguish preventive treatment from structural rehabilitation.
• Recognise when pre-overlay repair is necessary.
• Explain treatment choice using technical and budget arguments.

## Slide 6: Background / case study
• A paved interurban road near Douala carries trucks and buses.
• The surface is ageing but some sections have more severe structural distress.
• The agency considers fog seal, chip seal, micro-surfacing, HMA overlay or local repair.
• Students choose treatment packages for four short sections.

## Slide 7: Student task
• 1. Diagnose the main treatment objective for each section.
• 2. Select one treatment option.
• 3. Identify whether pre-treatment is required.
• 4. Justify why cheaper surface treatment may or may not be sufficient.

## Slide 8: Data / materials
• Assumed section descriptions:
• A: oxidised surface, no structural distress, minor hairline cracks.
• B: low friction and polished aggregate, no rutting.
• C: medium rutting and isolated potholes at bus stops.
• D: reflection cracks over old concrete slabs.
• Available treatments: fog seal, chip seal, slurry seal, micro-surfacing/rut fill, crack sealing, HMA overlay, slab repair.

## Slide 9: Work organisation
• Individual work: 25 min — first treatment choice.
• Group work: 40 min — agree on treatment table.
• Short presentation: 15 min — one section per group.
• Teacher synthesis: 10 min — preventive versus rehabilitative logic.

## Slide 10: Expected answer / solution
• A: fog seal or light seal treatment; objective: slow ageing and seal minor cracking.
• B: chip seal or suitable surface treatment; objective: improve friction and texture.
• C: local pothole repair plus rut fill/micro-surfacing; if structural failure is present, detailed diagnostics before overlay.
• D: crack sealing/pre-overlay treatment, stress-relieving interlayer or HMA overlay with reflection-crack control.
• Key rule: do not place thin surface treatment over unresolved structural or drainage failure.

## Slide 11: Teacher notes
• Observe whether students separate symptom treatment from cause treatment.
• Typical mistake: selecting overlay for every problem.
• Key discussion point: the cheapest treatment is not always cost-effective if applied too late or on wrong distress.
• Extension: add unit costs and ask for a budget-optimised package.