## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Project 01. PMS data collection plan
• Exercise type: Mixed exercise
• Estimated duration: 90 minutes
• Course topic: Pavement Management System and input data collection

## Slide 5: Learning objectives
• Identify necessary and additional data for pavement management.
• Prepare a simple field inspection plan for a road section.
• Select low-cost data collection methods suitable for limited equipment resources.
• Explain why periodic updating is required.

## Slide 6: Background / case study
• A 4.0 km rural road connects villages with a weekly market near Dschang.
• The first 1.5 km is paved asphalt; the remaining 2.5 km is gravel/laterite.
• During the rainy season, drainage problems and potholes reduce accessibility.
• The municipality wants a simple first inventory for future maintenance planning.

## Slide 7: Student task
• 1. List the minimum data needed before inspection.
• 2. Define inspection sections and marking rules.
• 3. Select field observations and simple measurements.
• 4. Propose how data should be recorded and updated.
• 5. Prepare a one-page inspection plan for the municipality.

## Slide 8: Data / materials
• Assumed data for educational purposes:
• Road length: 4.0 km; traffic: 250 vehicles/day; motorcycles are frequent.
• Available tools: smartphone, measuring tape, GPS app, paper forms, camera.
• Required outputs: section ID, surface type, main distress, drainage status, photos, maintenance urgency.
• Suggested section length: 200 m for paved part, 500 m for unpaved part.

## Slide 9: Work organisation
• Individual work: 20 min — identify necessary data.
• Group work: 35 min — prepare the inspection plan.
• Class discussion: 25 min — compare plans.
• Reporting: 10 min — each group states one key improvement.

## Slide 10: Expected answer / solution
• Minimum data: location, length, surface type, width, traffic function, photos, damage type, drainage condition.
• Sections should be clearly marked by chainage or GPS points.
• Use simple rating: good / fair / poor / critical.
• Update after each rainy season and after major maintenance works.
• Prioritise sections with drainage failure, potholes, rutting and access to public services.

## Slide 11: Teacher notes
• Observe whether students distinguish necessary from additional data.
• Typical mistake: collecting too much data without a clear purpose.
• Key discussion point: data quality versus available resources.
• Extension: ask students how the plan changes if a drone or falling weight deflectometer is available.