## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Laboratory 03. Drainage and rainfall diagnosis
• Exercise type: Mixed exercise
• Estimated duration: 120 minutes
• Course topic: drainage and tropical-climate maintenance

## Slide 5: Learning objectives
• Explain how water accelerates paved and unpaved road deterioration.
• Identify visible indicators of poor drainage.
• Select immediate and medium-term drainage interventions.
• Relate drainage failure to safety and accessibility.

## Slide 6: Background / case study
• A 2.2 km road links a school, clinic and market in a hilly area.
• During intense rainfall, water flows along the road surface and across shoulders.
• Motorcycle crashes increase near muddy sections.
• The local authority has funds only for minor drainage work this month.

## Slide 7: Student task
• 1. Identify likely water-related defects on paved and unpaved sections.
• 2. Draw a simple cross-section showing desired drainage paths.
• 3. Prioritise three immediate actions before the next storm.
• 4. Propose two medium-term interventions for the annual maintenance plan.

## Slide 8: Data / materials
• Assumed observations:
• Paved section: edge cracking, potholes near blocked side ditch, low skid resistance in rain.
• Unpaved section: rutting, potholes, slippery fines, erosion channels.
• Available resources: labour crew, hand tools, one small truck, local gravel, no laboratory tests.
• Budget: enough for ditch cleaning, spot gravel, small culvert cleaning and vegetation removal.

## Slide 9: Work organisation
• Individual work: 30 min — identify mechanisms.
• Group work: 40 min — cross-section and priority actions.
• Discussion: 40 min — defend priorities.
• Teacher synthesis: 10 min — connect to PMS and maintenance planning.

## Slide 10: Expected answer / solution
• Immediate actions: clear ditches and culverts; restore crossfall/crown; remove vegetation; fill dangerous potholes with compacted suitable material.
• Medium-term actions: improve side drains, add/repair culverts, regrade unpaved section, add laterite/gravel wearing course, stabilise shoulders.
• Key principle: remove water from the pavement and prevent water from entering pavement layers.
• Safety link: wet surface, mud, rutting and potholes increase motorcycle and pedestrian risk.

## Slide 11: Teacher notes
• Observe whether students prioritise drainage before surface repairs.
• Typical mistake: filling potholes without correcting the water source.
• Key discussion point: “drainage, drainage, drainage” as a flexible-pavement requirement.
• Extension: ask students to design a simple inspection checklist for culverts.