## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Exercise 5. Pavement condition classification
• Exercise type: Individual calculation + group interpretation
• Estimated duration: 120 minutes
• Course topic: condition values, classes and levels

## Slide 5: Learning objectives
• Use a simple 0-100 condition value scale.
• Assign pavement condition classes A-D.
• Determine desired, warning and critical levels.
• Identify dominant parameters for maintenance planning.

## Slide 6: Background / case study
• A municipal road section in Kinshasa is inspected before the rainy season.
• The road is important for buses and access to a health centre.
• The authority wants a transparent classification method for decision-making.
• Students receive simplified condition values.

## Slide 7: Student task
• 1. Assign class A, B, C or D to each parameter.
• 2. Assign condition level: desired, warning or critical.
• 3. Identify the dominant parameter.
• 4. Recommend whether routine maintenance, detailed diagnostics or urgent rehabilitation is needed.

## Slide 8: Data / materials
• Assumed data for educational purposes:
• Class thresholds: A = 80-100; B = 60-79; C = 40-59; D = 0-39.
• Levels: A-B = desired; C = warning; D = critical.
• Parameters: cracks = 55; rut depth condition = 35; friction = 62; longitudinal evenness = 48; drainage = 30.
• Priority order: drainage, rutting, friction, cracks, evenness.

## Slide 9: Work organisation
• Individual work: 30 min — classify parameters.
• Pair check: 30 min — compare results.
• Group work: 30 min — agree on dominant parameter and recommendation.
• Discussion: 30 min — compare decision logic.

## Slide 10: Expected answer / solution
• Cracks: 55 = C / warning.
• Rutting: 35 = D / critical.
• Friction: 62 = B / desired.
• Evenness: 48 = C / warning.
• Drainage: 30 = D / critical.
• Dominant parameter: drainage, because it is critical and has highest priority.
• Decision: urgent drainage correction and detailed diagnostic before structural rehabilitation.

## Slide 11: Teacher notes
• Observe whether students confuse condition value with physical measurement.
• Typical mistake: selecting lowest value only, ignoring priority rules.
• Key discussion point: dominant parameter guides action, not only reporting.
• Extension: ask students how the result changes if drainage improves to 65.