## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Laboratory 02. Unpaved road classification
• Exercise type: Group exercise
• Estimated duration: 90 minutes
• Course topic: unpaved local roads

## Slide 5: Learning objectives
• Classify unpaved roads by viability and level of service.
• Identify the role of platform, foundation and wearing course.
• Match local materials with their road function.
• Explain why road type affects maintenance requirements.

## Slide 6: Background / case study
• A district authority manages three rural links:
• Road A: seasonal agricultural track used mainly by tractors.
• Road B: village access road used daily by motorcycles and small cars.
• Road C: untreated natural track through hilly terrain.
• The authority asks which roads require formal maintenance planning.

## Slide 7: Student task
• 1. Classify Road A, Road B and Road C.
• 2. Fill in the table: road type, expected vehicle access, maintenance level, main risk.
• 3. Assign materials to layers: compacted soil, laterite gravel, natural gravel, improved local fill.
• 4. Recommend one low-cost improvement for each road.

## Slide 8: Data / materials
• Classification options: natural trail; dirt road; elaborate unpaved road.
• Material options: treated/untreated local soil; laterite gravel; natural gravel; stabilised sand.
• Assumed constraints: no asphalt, limited budget, one grader available twice per year.
• Climate: long wet season with intense rainfall and erosion risk.

## Slide 9: Work organisation
• Group work: 35 min — classification and table.
• Internal peer check: 20 min — another group reviews the table.
• Discussion: 25 min — compare maintenance implications.
• Reporting: 10 min — one recommendation per group.

## Slide 10: Expected answer / solution
• Road A: dirt road — seasonal use, seasonal maintenance, drainage and passability risk.
• Road B: elaborate unpaved road — daily ordinary vehicle access, routine and periodic maintenance.
• Road C: natural trail — no formal surface, very low control of travel time and viability.
• Laterite/natural gravel can serve as wearing or base material; compacted local soil/improved fill supports the foundation/platform.
• Improvements should focus first on drainage, shaping, crowning and local material stabilisation.

## Slide 11: Teacher notes
• Observe whether students understand “unpaved” is not one uniform category.
• Typical mistake: proposing asphalt without considering budget or maintenance capacity.
• Key discussion point: viability of the road is a management concept, not only a construction detail.
• Extension: ask how classification changes if traffic volume doubles.