## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Laboratory 01. Asphalt distress identification
• Exercise type: Individual exercise + group verification
• Estimated duration: 90 minutes
• Course topic: asphalt pavement distress recognition

## Slide 5: Learning objectives
• Recognise common asphalt pavement distresses.
• Distinguish load-associated and non-load-associated cracking.
• Link visible damage with likely technical causes.
• Select the first diagnostic question for each distress.

## Slide 6: Background / case study
• An urban road in Goma serves a hospital, motorcycle taxis and delivery vehicles.
• After heavy rainfall, several defects are reported by residents.
• The road authority has photos but limited measurement equipment.
• Students act as a first-level inspection team.

## Slide 7: Student task
• 1. Classify each described defect.
• 2. State whether it is mainly cracking, distortion, disintegration or skid-related.
• 3. Identify two likely causes.
• 4. Propose one additional field observation needed before choosing maintenance.

## Slide 8: Data / materials
• Assumed defect descriptions:
• A: interconnected cracks in the wheel path, later developing potholes.
• B: transverse cracks at regular intervals across the lane.
• C: shiny asphalt surface with low friction during rain.
• D: loss of aggregate particles from the surface.
• E: longitudinal depressions in wheel paths near a bus stop.

## Slide 9: Work organisation
• Individual work: 30 min — classify A-E.
• Pair work: 20 min — compare classifications.
• Group work: 30 min — agree on likely causes.
• Class discussion: 10 min — teacher reviews model answers.

## Slide 10: Expected answer / solution
• A: fatigue/alligator cracking — repeated heavy loads, inadequate support, poor drainage.
• B: thermal cracking — stiff binder, temperature susceptibility, ageing.
• C: bleeding/flushing or polished aggregate — reduced skid resistance, poor macro/microtexture.
• D: raveling — low in-place density, lack of fines, aged binder.
• E: rutting — weak subgrade/base, excessive binder, heavy braking/standing traffic.

## Slide 11: Teacher notes
• Observe if students use distress evidence, not guesses.
• Typical mistake: calling every crack “fatigue cracking”.
• Key discussion point: drainage can contribute to several different distress types.
• Extension: introduce severity levels and ask which defects require urgent action.