## Slide 2: Road Transportation Systems Engineering Development in the Sub-Saharan Africa – Modern EU Master Programme & Capacity Building

## Slide 4: Project 05. Inspection report and recommendation
• Exercise type: Mixed capstone exercise
• Estimated duration: 45 minutes
• Course topic: pavement inspection and maintenance reporting

## Slide 5: Learning objectives
• Summarise road-condition observations in an engineering format.
• Assess damage frequency, size, severity and likely causes.
• Translate inspection results into maintenance needs.
• Present recommendations clearly to a non-specialist decision-maker.

## Slide 6: Background / case study
• Each student group has inspected or is given a hypothetical road section.
• The road authority asks for a short presentation before deciding the annual maintenance plan.
• The report must be practical, evidence-based and understandable.
• Students should use photographs, tables or sketches if available.

## Slide 7: Student task
• 1. Prepare a summary table for one road section.
• 2. Identify dominant defects and likely causes.
• 3. Assign a simplified condition class and level.
• 4. Recommend maintenance actions: immediate, short-term, medium-term.
• 5. Prepare a 3-minute oral briefing.

## Slide 8: Data / materials
• Assumed reporting template:
• Road ID; location; length; surface type; function; traffic users.
• Observed defects: type, frequency, size/severity, likely cause, photo ID.
• Condition class: A good, B satisfactory, C unsatisfactory, D bad.
• Condition level: desired, warning, critical.
• Recommendation: treatment, urgency, required resources, expected risk if postponed.

## Slide 9: Work organisation
• Individual work: 10 min — draft own observations.
• Group work: 20 min — complete report table.
• Presentation: 10 min — selected groups give a 3-minute briefing.
• Teacher feedback: 5 min — clarity and decision usefulness.

## Slide 10: Expected answer / solution
• A strong report contains: location, evidence, classification, cause hypothesis and actionable recommendation.
• Dominant problem should be linked to maintenance decision, e.g. drainage failure before surface repair.
• Immediate actions address safety and access; short-term actions restore function; medium-term actions prevent recurrence.
• The presentation should avoid excessive terminology and explain consequences of postponement.

## Slide 11: Teacher notes
• Observe whether each student contributes a defined part.
• Typical mistake: describing defects without recommending a decision.
• Key discussion point: a maintenance report is a management tool, not only a technical inventory.
• Extension: ask students to add cost estimates and a monitoring indicator.