## Slide 1: Transport Research and Analysis
Module 3: Transport Modeling and Simulation
Lecture 12: Traffic Flow Theory and Simulation

## Slide 3
Section 1: Overview and Objectives ……………………..………………………………………………. 4
1.1 Overview …..…….………………………………….…………….…………………………….………. 5
Section 2: Fundamentals of Travel Demand ……..………..…………………………………………... 6
2.1 What is Traffic Flow Theory? …..…………………………….…………………………….………. 7
2.2 Importance of Traffic Flow Theory in Transport Planning? …….…………………………….. 8
2.3 Real-World Applications ………………..………………………………………………………….... 9
Section 3: Fundamental Concepts of Traffic Flow ……………………..…..………………………… 10
3.1 Core Variables: Flow, Speed, Density ….………………………….….…………………………. 11
3.2 Traffic States ….……………………………………………...………….….…………………………. 13
Section 4: Microscopic traffic flow ……………………...........................….………………………….. 14
4.1 What is Microscopic Modeling ……………………………………….……….……………………. 15
4.2 Key Characteristics …………………………………………………...….…………………………... 16
4.3 Car-Following Models …………………………………………..…….….…………………………... 17
4.4 Lane Changing Models …………………………………………..…..….…………………………... 19
4.5 Microscopic Traffic Simulation ………………………………..…….…………………………... 21
Section 5: Macroscopic Traffic Flow Theory …………………………….….………………………….. 22
5.1 What is Macroscopic Modeling? ……………………………………..……….……………………. 23
Traffic Flow Theory and Simulation
Table of Contents
Notes: # English
First of all, let’s take a look at what’s included in this lab.
We begin with Section 1: Lab Overview and Required Tools, where we’ll talk about the lab objectives, the overall content, and the tools will be using.
Then in Section 2: Data Preprocessing Techniques, we’ll explore the key steps used to clean and prepare raw datasets.
After that, in Section 3: Data Format Standardizing, we’ll learn how to make the data consistent—such as aligning time formats, currencies, and measurement units across different sources.
# French
Tout d'abord, examinons le contenu de ce laboratoire.
Nous commençons par la section 1 : Présentation du laboratoire et outils requis, où nous aborderons les objectifs du laboratoire, le contenu général et les outils utilisés. Ensuite, dans la section 2 : Techniques de prétraitement des données, nous explorerons les étapes clés du nettoyage et de la préparation des jeux de données brutes.
Ensuite, dans la section 3 : Normalisation des formats de données, nous apprendrons à assurer la cohérence des données, notamment en alignant les formats d'heure, les devises et les unités de mesure entre différentes sources.

## Slide 4
5.2 Fundamental Traffic Models ………………………….…………..…….…………………………... 26
5.3 Applications of Macroscopic Models ……………….…………..…….…………………………... 29
Section 6: Mesoscopic Traffic Flow Theory ……..………...…………………………………………... 30
6.1 What is Mesoscopic Modeling? …..………………………….…………………………….………. 31
6.2 Common Mesoscopic Models (Gas-kinetic, METANET) …………………………………….... 33
6.3 Advantages and Limitations of Mesoscopic Models ………………………………………….... 34
6.4 Applications of Mesoscopic Models ……………………………….…………………………….... 35
Section 7: Comparison of Traffic Flow Models ………………………..………………………………. 36
7.1 Microscopic vs Macroscopic vs Mesoscopic …………………………………………….………. 37
7.2 When to Use Each Model? ………………………………………………………………….………. 39
Section 8: Mathematical Models in Traffic Flow ……………................……………………………... 40
8.1 Microscopic Traffic Flow Models (Mathematical Form) …..……………….………….………. 41
8.2 Macroscopic Traffic Flow Models (Mathematical Form) ………...…………………………….. 43
8.3 Mesoscopic Traffic Flow Models (Mathematical Form) …………………..………………….... 44
Section 9: Quiz ………………………………………………………………..….………………………….. 47
9.1 MCQ Questions (x10) ………………………………………….………….…………………………. 48
Table of Contents
Traffic Flow Theory and Simulation
Notes: # English
First of all, let’s take a look at what’s included in this lab.
We begin with Section 1: Lab Overview and Required Tools, where we’ll talk about the lab objectives, the overall content, and the tools will be using.
Then in Section 2: Data Preprocessing Techniques, we’ll explore the key steps used to clean and prepare raw datasets.
After that, in Section 3: Data Format Standardizing, we’ll learn how to make the data consistent—such as aligning time formats, currencies, and measurement units across different sources.
# French
Tout d'abord, examinons le contenu de ce laboratoire.
Nous commençons par la section 1 : Présentation du laboratoire et outils requis, où nous aborderons les objectifs du laboratoire, le contenu général et les outils utilisés. Ensuite, dans la section 2 : Techniques de prétraitement des données, nous explorerons les étapes clés du nettoyage et de la préparation des jeux de données brutes.
Ensuite, dans la section 3 : Normalisation des formats de données, nous apprendrons à assurer la cohérence des données, notamment en alignant les formats d'heure, les devises et les unités de mesure entre différentes sources.

## Slide 5
Section 01:
Overview and Objectives
Notes: # English
Now we are in Section 1: Overview and Tools.
Let’s quickly see what this lab is about and what tools we’ll use.
# French
Nous voici maintenant à la section 1 : Présentation et outils.
Voyons rapidement en quoi consiste cet atelier et quels outils nous utiliserons.

## Slide 6: 1. Overview and Objectives
1.1 Overview: Traffic Flow Theory and Simulation
Traffic Flow Theory helps us understand how vehicles move on roads, how congestion forms, and how traffic conditions can be predicted. This lecture introduces the key scientific principles behind traffic movement and demonstrates how simulation tools use these principles to model real-world road networks.
Understand the basic concepts of traffic flow: speed, flow, and density.
Explain microscopic, macroscopic, and mesoscopic traffic flow models.
Interpret the fundamental diagram of traffic flow.
Compare different traffic modelling approaches.
Understand how simulation tools use traffic flow theory.
Learning Objectives:

## Slide 7
Section 02:
Introduction to Traffic Flow Theory
Notes: # English
Now we are in Section 1: Overview and Tools.
Let’s quickly see what this lab is about and what tools we’ll use.
# French
Nous voici maintenant à la section 1 : Présentation et outils.
Voyons rapidement en quoi consiste cet atelier et quels outils nous utiliserons.

## Slide 8: 2. Introduction to Traffic Flow Theory
2.1 What is Traffic Flow Theory?
Traffic Flow Theory is the study of how vehicles behave on road networks.
It uses mathematical and analytical models to describe traffic movement, helping planners and engineers understand congestion, delays, and safety.
Why is It Important?
Traffic flow theory is essential because it:
Understand the fundamental concepts of traffic flow
Differentiate between microscopic, macroscopic, and mesoscopic traffic
Explore the role of traffic simulations in urban planning and congestion management
Analyze mathematical models used for traffic analysis

## Slide 9: 1. Introduction
2.2 Importance of Traffic Flow Theory in Transport Planning
Traffic flow theory is critical for designing efficient and safe transportation systems. Without it, roadways would be chaotic, leading to congestion, increased travel time, and safety hazards.
Optimizes road network efficiency: Helps in designing road networks to maximize capacity and minimize delays.
Improves traffic safety: Understanding vehicle interactions can help reduce accidents.
Reduces congestion and travel time: Traffic models can predict and mitigate congestion hotspots.
Supports sustainable transportation planning: Helps in designing eco-friendly transport policies and reducing emissions.
Guides policy decisions: Used by governments and city planners to implement traffic regulations and improve infrastructure.
Why is traffic flow theory important?

## Slide 10: 1. Introduction to Traffic Flow Theory
2.3 Real-World Applications
Traffic flow theory is directly used in everyday transport operations and long-term planning. It helps engineers understand how traffic behaves under different conditions and supports decisions that improve safety, reduce congestion, and optimize road performance. These concepts are applied across many real-world scenarios, from traffic control to infrastructure design.
Traffic flow theory is used in:
Traffic signal timing design
Highway capacity analysis
Planning for large events or peak hours
Autonomous vehicle behavior modelling
Smart mobility systems

## Slide 11
Section 03:
Fundamental Concepts of Traffic Flow
Notes: # English
Now we are in Section 1: Overview and Tools.
Let’s quickly see what this lab is about and what tools we’ll use.
# French
Nous voici maintenant à la section 1 : Présentation et outils.
Voyons rapidement en quoi consiste cet atelier et quels outils nous utiliserons.

## Slide 12: 3. Fundamental Concepts of Traffic Flow
3.1 Core Variables: Flow, Speed, Density
Traffic flow refers to the movement of vehicles along a roadway, influenced by roadway design, traffic control measures, and driver behavior.
Traffic flow is characterized by three fundamental parameters:
Key Elements of Traffic Flow
✅ Represents the number of vehicles passing a fixed point per unit of time.
✅ Measured in vehicles per hour (veh/hr).
✅ Example: If 600 cars pass a highway checkpoint in one hour, the flow rate is 600 veh/hr.
1. Flow (Q)
2. Density (K)
✅ Represents the number of vehicles occupying a given road length at an instant.
✅ Measured in vehicles per kilometer (veh/km).
✅ Example: If 30 vehicles are on a 1 km section of a highway, the density is 30 veh/km.
3. Speed (V)
✅ The average velocity of vehicles in a traffic stream.
✅ Measured in kilometers per hour (km/h).
✅ Example: If the average speed of cars on a freeway is 80 km/h, this affects overall traffic flow.

## Slide 13: 3. Fundamental Concepts of Traffic Flow
Flow vs Density vs Speed:
The three parameters are connected by the fundamental traffic flow equation:
✅ If vehicle speed increases, density decreases (fewer cars per unit length).
✅ If density increases too much, speed drops, leading to congestion.
Q = K . V
Q – Flow
K – Density
V – Speed
V
V0
V
V0
qm

## Slide 14: 3. Fundamental Concepts of Traffic Flow
3.2 Traffic States
  Understanding traffic states helps in traffic management decisions.
  ✅ Free Flow: vehicles move freely with no interaction.
  ✅ Capacity Flow: road is fully used, highest throughput.
  ✅ Congested Flow: slow movement, unstable traffic.
  ✅ Emergency evacuation planning.
Real-World Applications
  Traffic flow theory is directly used in everyday transport operations and long-term planning. It helps engineers understand how traffic behaves under different conditions and supports decisions that improve safety, reduce congestion, and optimize road performance.
  ✅ Predicting congestion on highways.
  ✅ Designing lane additions or ramps.
  ✅ Setting speed limits.
  ✅ Emergency evacuation planning.

## Slide 15
Section 04:
Microscopic traffic flow
Notes: # English
Now we are in Section 1: Overview and Tools.
Let’s quickly see what this lab is about and what tools we’ll use.
# French
Nous voici maintenant à la section 1 : Présentation et outils.
Voyons rapidement en quoi consiste cet atelier et quels outils nous utiliserons.

## Slide 16: 4. Microscopic traffic flow
4.1 What is Microscopic Modeling?
Microscopic traffic modeling represents traffic at the level of individual vehicles. It examines how each driver accelerates, decelerates, changes lanes, and reacts to the surrounding environment. This detailed perspective helps us understand how small behaviors can lead to larger traffic patterns such as congestion, stop-and-go waves, or bottlenecks.
Microscopic models simulate vehicle movement one-by-one, considering:
  ✅ Driver behavior: acceleration, deceleration, lane-changing decisions
  ✅ Vehicle interactions: following distance, response to braking, overtaking
  ✅ Traffic rules: signals, stop signs, speed limits
Unlike macroscopic models that treat traffic as a continuous flow, microscopic models focus on individual decision-making and vehicle-level dynamics, making them ideal for detailed simulation and intelligent transportation systems (ITS).
Definition and Scope

## Slide 17: 4. Microscopic traffic flow
4.2 Key Characteristics
Microscopic traffic flow models capture how individual drivers behave on the road. These models focus on the detailed movement of each vehicle and its direct interaction with surrounding vehicles. This level of detail helps researchers and engineers understand how small behavioral changes—such as delayed reactions or aggressive braking—can create larger traffic patterns like shockwaves or congestion.
Individual Vehicle Representation: Each vehicle is modeled separately with its own position, speed, and acceleration.
Driver-Specific Behavior: Models include reaction time, desired speed, aggressiveness, and decision-making.
Car-Following Dynamics: Vehicles adjust their speed based on the distance and speed of the car ahead.
Lane-Changing Decisions: Decisions to change lanes depend on safety, incentive, and surrounding traffic conditions.
High Temporal and Spatial Resolution: Vehicle behavior is updated continuously (often every 0.1–1 second).
Detailed Interaction with Traffic Controls: Models capture how individual vehicles respond to signals, stop signs, yield rules, and speed limits.

## Slide 18: 4. Microscopic traffic flow
4.3 Car-Following Models
Car-following models describe how a driver controls their vehicle in response to the vehicle ahead.
These models determine acceleration, deceleration, following distance, and reaction to changing traffic conditions. They are essential for simulating realistic driver behavior, analyzing congestion, and modeling autonomous vehicle movement.
Key Concepts of Car-Following Models:
Describe how a vehicle adjusts speed based on the distance (gap) and speed difference to the car in front.
Capture driver reaction time, desired speed, and safety margins.
Influence how stop-and-go waves, shockwaves, and congestion form.
Used in many simulation tools such as VISSIM, SUMO, and AIMSUN.

## Slide 19: 4. Microscopic traffic flow
Common Car-Following Models:
1. GHR Model (Gazis–Herman–Rothery)
Adjusts speed based on gap, relative speed and sensitivity parameters.
Represents human reaction to the leader vehicle.
Useful for studying basic driver behavior and stability of traffic flow.
2. IDM – Intelligent Driver Model
One of the most widely used car-following models today.
Provides smooth and realistic acceleration/deceleration.
Includes desired speed, safe time headway, maximum acceleration, and comfortable braking.
Used in microscopic simulation and autonomous vehicle research.
3. ACC/AV Car-Following Models
Designed for Adaptive Cruise Control (ACC) and Autonomous Vehicles (AVs).
Vehicles adjust speed automatically using sensors (radar/LiDAR).
Provide consistent, low-variance behavior ideal for AV platooning and cooperative driving simulations.

## Slide 20: 4. Microscopic traffic flow
4.4 Lane Changing Models
Lane-changing models describe how and why drivers decide to switch lanes. These decisions depend on safety, available space, traffic rules, and the driver’s intention (e.g., overtaking, preparing for a turn). Accurate lane-changing modeling is essential for realistic traffic simulations, especially on multi-lane highways and at complex intersections.
Types of Lane-Changing Models:
1. Rule-Based Models
Use a set of clear rules to decide when a vehicle changes lanes.
MOBIL model evaluates:
Safety (is it safe to move?)
Advantage (will it improve my speed?)
Impact on others (does it cause danger or heavy braking?)
Widely used due to simplicity and realistic behavior.

## Slide 21: 4. Microscopic traffic flow
2. Gap Acceptance Models
Vehicle changes lanes only if a sufficient gap is available in the target lane.
Based on driver judgment of safety and comfort.
Used for simulating merging, weaving sections, and roundabouts.
Key factors:
Minimum acceptable gap
Relative speed to cars in the target lane
Driver aggressiveness

## Slide 22: 4. Microscopic traffic flow
4.5 Microscopic Traffic Simulation
Microscopic traffic simulation tools model individual vehicle behavior using car-following and lane-changing rules. They allow planners and researchers to visualize how traffic operates in detailed environments such as intersections, roundabouts, urban corridors, and AV test scenarios
Popular Microscopic Simulation Tools:
1. VISSIM
Industry-standard microscopic simulation software.
Highly detailed models for signals, priority rules, pedestrians, bicycles, and AV behavior.
Often used for intersection design, signal control evaluation, and public transport priority studies.
2. SUMO (Simulation of Urban Mobility)
Open-source, highly flexible microscopic simulator.
Supports large-scale networks, route assignment, and connected/automated vehicles.
Popular in academic research and AV communication studies.
3. AIMSUN
Offers microscopic, mesoscopic, and hybrid simulations.
Strong in real-time operations, predictive traffic management, and urban network modelling.
Supports dynamic traffic assignment and complex scenario testing.

## Slide 23
Section 05:
Macroscopic Traffic Flow Theory
Notes: # English
Now we are in Section 1: Overview and Tools.
Let’s quickly see what this lab is about and what tools we’ll use.
# French
Nous voici maintenant à la section 1 : Présentation et outils.
Voyons rapidement en quoi consiste cet atelier et quels outils nous utiliserons.

## Slide 24: 5. Macroscopic Traffic Flow Theory
5.1 What is Macroscopic Modeling?
Macroscopic traffic modeling studies traffic flow at an aggregated level rather than focusing on individual vehicles. Instead of modeling each driver separately, it describes traffic using collective variables such as flow, speed, and density. This approach is useful for understanding large-scale traffic behavior on corridors, highways, or entire networks.
Macroscopic models:
Treat traffic as a continuous flow, similar to fluid dynamics.
Use aggregate measures such as average speed, total flow, and vehicle density.
Focus on overall patterns, not individual driver decisions.
Are ideal for analyzing large-scale traffic conditions, congestion patterns and the relationship between speed, flow, and density.
Support strategic planning, highway design and traffic control policies.
Definition and Scope:

## Slide 25: 5. Macroscopic Traffic Flow Theory
Key Variables (aggregated flow-density-speed relations):
Macroscopic traffic flow describes how traffic behaves at a large scale using three aggregate variables: flow, density, and speed. These variables help us understand how crowded a road is, how fast vehicles are moving, and how many vehicles can be served by the road system.
Primary Macroscopic Variables:
1. Traffic Flow (Q)
Number of vehicles passing a specific point per unit time.
Measured in vehicles per hour (veh/hr).
Represents how much traffic the road is carrying.
2. Traffic Density (K)
Number of vehicles per unit length of roadway.
Measured in vehicles per kilometer (veh/km).
Indicates how closely vehicles are spaced.
3. Traffic Speed (V)
The average speed of vehicles in a given road segment.
Measured in km/h or mph.
Helps describe traffic conditions (free flow vs congestion).

## Slide 26: 5. Macroscopic Traffic Flow Theory
Relationship Between the Variables:
These variables are connected through the fundamental traffic flow equation:
✅ Higher density with moderate speed → flow increases
✅ Density beyond a critical level → speed drops → flow decreases
Example:
Free-flowing highway: Low density → High speed → Moderate flow.
Traffic jam: High density → Very low speed → Low flow
Q = K . V

## Slide 27: 5. Macroscopic Traffic Flow Theory
5.2 Fundamental Traffic Models
Macroscopic traffic flow models describe how speed, flow, and density are related. These models help planners predict how traffic behaves as roads fill up, identify congestion points, and estimate roadway capacity. The three classical models below are widely used in transportation engineering.
1. Greenshields Model (Linear Model)
  ✅ Assumes a linear relationship between speed and density.
  ✅ Speed decreases steadily as density increases.
  ✅ At jam density, speed becomes zero.
  ✅ Simple and widely used for teaching and basic analysis.
  ✅ Equation:
Use Cases:
Quick estimations
Understanding basic flow–density characteristics
Where:
𝑉𝑓​ = free-flow speed
𝐾𝑗​ = jam density

## Slide 28: 5. Macroscopic Traffic Flow Theory
2. Greenberg Model (Logarithmic Model)
  ✅ Uses a logarithmic relationship between speed and density.
  ✅ Better suited for high-density traffic, such as urban congestion.
  ✅ Implies speed approaches infinity at low density (theoretical).
  ✅ Equation:
Use Cases:
Dense urban traffic
Congestion modelling
Analytical studies
Where:
c = model constant

## Slide 29: 5. Macroscopic Traffic Flow Theory
3. Underwood Model (Exponential Model)
  ✅ Uses an exponential relationship between speed and density.
  ✅ Assumes smoother speed reduction as density rises.
  ✅ Provides more realistic behavior at medium densities.
  ✅ Equation:
Use Cases:
Highway analysis
Medium-density flow
Simulation calibration
Where:
𝐾0​ = model shape parameter

## Slide 30: 5. Macroscopic Traffic Flow Theory
5.3 Applications of Macroscopic Models
Macroscopic traffic models are widely used in transportation planning because they provide a high-level understanding of how traffic behaves on large sections of a road network. By analyzing how speed, flow, and density change together, planners can make informed decisions about roadway design, congestion management, and network performance.
Highway Capacity Analysis
Congestion Prediction and Management
Roadway Design and Planning
Speed–Flow–Density Evaluation
Policy and Operational Analysis
Integration with Simulation Tools

## Slide 31
Section 06:
Mesoscopic Traffic Flow Theory
Notes: # English
Now we are in Section 1: Overview and Tools.
Let’s quickly see what this lab is about and what tools we’ll use.
# French
Nous voici maintenant à la section 1 : Présentation et outils.
Voyons rapidement en quoi consiste cet atelier et quels outils nous utiliserons.

## Slide 32: 6. Mesoscopic Traffic Flow Theory
6.1 What is Mesoscopic Modeling?
Mesoscopic traffic modeling represents a middle ground between microscopic and macroscopic approaches.
Instead of modeling every vehicle individually or treating traffic as a continuous flow, mesoscopic models simulate vehicles in groups or packets. This allows for realistic behavior while keeping computation efficient, making them ideal for city-wide or regional simulations.
  ✅ Combine features of micro and macro models
  Individual vehicles may be represented
  But their behavior is simplified or averaged
  ✅ Emphasize traffic dynamics (queues, propagation, speeds) rather than detailed driver behavior
  ✅ Use aggregated rules for movement and interaction
  ✅ Provide realistic traffic patterns without high computational cost
  ✅ Suitable for large network analysis, dynamic traffic assignment, and real-time applications
Mesoscopic models:

## Slide 33: 6. Mesoscopic Traffic Flow Theory
Key Concepts (packet-based, hybrid behavior):
Mesoscopic traffic flow models simplify driver behavior while still capturing dynamic traffic conditions such as congestion buildup, queue formation, and travel-time variations.
They balance realism and computational efficiency, making them suitable for modelling large network scenarios where a fully microscopic approach would be too slow or complex.
Vehicle Packets or Groups
Simplified Driver Behavior
Speed and Travel Time Based on Density
Dynamic Traffic Propagation
Lower Computational Demand
Supports Dynamic Traffic Assignment (DTA)

## Slide 34: 6. Mesoscopic Traffic Flow Theory
6.2 Common Mesoscopic Models (Gas-kinetic, METANET)
Mesoscopic models use simplified rules and aggregated behavior to simulate traffic dynamics. They are widely used for large-scale transport planning and dynamic traffic assignment because they balance realism with computational efficiency.
1. Gas-Kinetic Models
Based on principles similar to gas particle movement.
Vehicle groups behave like particles in a flow.
Captures traffic shockwaves and congestion formation well.
2. METANET Model
One of the most widely used mesoscopic models.
Describes flow, density, and speed using differential equations.
Supports simulation of entire freeway networks.
Often used for real-time traffic management applications.
3. Cell Transmission Model (CTM)
Divides roads into cells (segments).
Vehicles move cell-to-cell based on capacity and density.
Simple, efficient, and widely used for large networks.

## Slide 35: 6. Mesoscopic Traffic Flow Theory
6.4 Advantages and Limitations of Mesoscopic Models
Mesoscopic models offer a practical compromise between accuracy and computational speed. They are useful for large-scale simulations but have trade-offs in detail and behavioral realism.
✅ Advantages
  ✔ Efficient for large networks: Faster than microscopic models.
  ✔ Captures dynamic congestion: Realistic queue buildup and dissipation.
  ✔ Good balance between detail and computation: More realistic than macroscopic models.
  ✔ Ideal for scenario testing: Tolling, rerouting, incident management.
  ✔ Supports DTA: Used for evaluating network-wide travel behavior.
❌ Limitations
  ✘ Less behavioral detail: No individual driver actions.
  ✘ Simplified lane-changing: Not suitable for detailed intersection analysis.
  ✘ Less precise than microscopic simulation: Not ideal for AV or Safety studies.
  ✘ Assumptions vary by model: Calibration can be challenging.

## Slide 36: 6. Mesoscopic Traffic Flow Theory
6.5 Applications of Mesoscopic Models
Mesoscopic models are particularly valuable for analyzing mobility at a regional or city-wide scale. Their speed and flexibility make them ideal for testing multiple scenarios and operational strategies.
✅ City-wide traffic simulation
Evaluate congestion patterns across entire urban areas.
✅ Dynamic Traffic Assignment (DTA)
Study how drivers change routes based on real-time conditions.
✅ Policy testing and evaluation
Congestion pricing, tolling, low-emission zones.
✅ Incident and event management
Evaluate effects of crashes, road works, or large events.
✅ Large-scale transport planning
Future network design and long-term mobility strategies.

## Slide 37
Section 07:
Comparison of Traffic Flow Models
Notes: # English
Now we are in Section 1: Overview and Tools.
Let’s quickly see what this lab is about and what tools we’ll use.
# French
Nous voici maintenant à la section 1 : Présentation et outils.
Voyons rapidement en quoi consiste cet atelier et quels outils nous utiliserons.

## Slide 38: 7. Comparison of Traffic Flow Models
7.1 Microscopic vs Macroscopic vs Mesoscopic
Traffic flow models are generally categorized into microscopic, macroscopic, and mesoscopic models. These categories differ in how they represent vehicle behavior, the level of detail they provide, and the computational effort required.
Microscopic Models:
  ✅ Represent individual vehicles and driver behavior.
  ✅ Very detailed, high accuracy.
  ✅ Best for intersections, AV studies, and safety analysis.
Macroscopic Models:
  ✅ Treat traffic as continuous flow.
  ✅ Focus on aggregate variables (flow, speed, density).
  ✅ Best for highways and corridor-level analysis.
Mesoscopic Models:
  ✅ Hybrid approach: vehicles grouped into packets.
  ✅ Good balance of realism and computational efficiency.
  ✅ Best for city-wide and regional simulations.

## Slide 39: 7. Comparison of Traffic Flow Models
# | Feature | Microscopic Model | Macroscopic Model | Mesoscopic Model
1 | Focus | Individual vehicles and drivers | Aggregate traffic flow | Vehicle groups (platoons)
2 | Key Variables | Speed, acceleration, lane changes | Flow, density, average speed | Statistical vehicle behavior
3 | Data Requirement | High (detailed vehicle and driver behavior data) | Low (aggregated traffic data) | Medium (some individual vehicle data)
4 | Computational Complexity | High (simulates every vehicle) | Low (solves aggregate equations) | Medium (simplifies vehicle interactions)
5 | Best Use Case | Intersection modeling, signal optimization | Highway capacity analysis, congestion estimation | Dynamic traffic assignment, urban traffic flow
6 | Example Models | Car-following models (Gipps, IDM), Lane-changing models (MOBIL) | LWR (Lighthill-Whitham-Richards) model, Greenshields model | Cell Transmission Model (CTM), Hybrid models
7 | Application Areas | Autonomous vehicle testing, driver behavior analysis | Large-scale traffic simulation, transport planning | Intelligent Transport Systems (ITS), toll pricing, evacuation planning
Comparison Table:

## Slide 40: 7. Comparison of Traffic Flow Models
7.2 When to Use Each Model?
Each type of model is suited to different problems. Choosing the right model depends on the study area, required detail, and available computation resources.
✅ Microscopic Models:
  ✔ Best for local traffic behavior analysis.
  ✔ Used in driver behavior research, lane management, and intersection design.
✅ Macroscopic Models:
  ✔ Best for large-scale traffic flow analysis.
  ✔ Used for predicting highway congestion and regional transport planning.
✅ Mesoscopic Models:
  ✔ Best for dynamic simulations with moderate detail.
  ✔ Used in real-time traffic management, dynamic pricing, and urban simulations.
Example:
  ✅ If analyzing an autonomous vehicle's movement, use microscopic models.
  ✅ If estimating city-wide congestion trends, use macroscopic models.
  ✅ If simulating urban networks with medium detail, use mesoscopic models.

## Slide 41
Section 08:
Mathematical Models in Traffic Flow
Notes: # English
Now we are in Section 1: Overview and Tools.
Let’s quickly see what this lab is about and what tools we’ll use.
# French
Nous voici maintenant à la section 1 : Présentation et outils.
Voyons rapidement en quoi consiste cet atelier et quels outils nous utiliserons.

## Slide 42: 8. Mathematical Models in Traffic Flow
8.1 Microscopic Traffic Flow Models (Mathematical Form)
Microscopic models describe the behavior of individual vehicles using mathematical rules for acceleration, braking, and following distances. These equations help simulate realistic driver reactions and vehicle interactions in dynamic environments.
1. GHR Model (Gazis–Herman–Rothery)
Describes acceleration based on the distance gap and relative speed to the leader.
Where:
𝑣𝑛​ = speed of following vehicle
𝑣𝑛−1​ = speed of leader
𝑥𝑛−1−𝑥𝑛​ = spacing (gap)
𝛼,𝛽 = sensitivity parameters

## Slide 43: 8. Mathematical Models in Traffic Flow
2. IDM (Intelligent Driver Model)
One of the most widely used car-following models.
Key Features:
Smooth acceleration
Safety distance control
Used extensively in AV and CAV simulation
3. ACC/AV Control Models
Use radar/LiDAR inputs for automatic speed control
Often based on variants of IDM or PID control
Provide stable and cooperative car-following behavior
Desired gap:

## Slide 44: 8. Mathematical Models in Traffic Flow
8.2 Macroscopic Traffic Flow Models (Mathematical Form)
Macroscopic models treat traffic as a continuous flow and use equations similar to fluid dynamics. These models describe the relationship between flow, speed, and density at a large scale.
1. Fundamental Flow Equation
Characteristics:
Captures stop-and-go waves
Widely used in highway traffic modeling
2. Greenshields Model (Linear Speed–Density)
3. LWR Model (Lighthill–Whitham–Richards)
Describes shockwave propagation and traffic states.

## Slide 45: 8. Mathematical Models in Traffic Flow
8.3 Mesoscopic Traffic Flow Models (Mathematical Form)
Mesoscopic models combine micro-level dynamics with macro-level aggregation. Their equations describe how groups of vehicles move, react to congestion, and propagate through the network.
1. Gas-Kinetic Model (Example)
Describes acceleration based on the distance gap and relative speed to the leader.
Where 𝑃 is “traffic pressure” from dense traffic.

## Slide 46: 8. Mathematical Models in Traffic Flow
2. METANET Model (Common Mesoscopic Model)
Speed update equation:
Flow equation:
3. Cell Transmission Model (CTM)
Flow between cells:
Density update:
Why it’s used:
Realistic dynamics
Suitable for freeway networks
Supports real-time control applications
CTM is widely used for:
Large-scale simulations
Signal coordination
Congestion pattern prediction

## Slide 47: 8. Mathematical Models in Traffic Flow
Summary Table of all Mathematical Approaches:
Choosing the right traffic flow model depends on the level of detail required and computational constraints. Microscopic models provide precision but require heavy computing, while macroscopic models simplify flow dynamics for large-scale planning. Mesoscopic models balance these approaches for urban simulations and dynamic traffic assignments.
# | Feature | Microscopic Models | Macroscopic Models | Mesoscopic Models
1 | Focus | Individual vehicles | Aggregated traffic flow | Groups of vehicles
2 | Mathematical Complexity | High | Moderate | Medium
3 | Key Models | Car-following, Lane-changing | Flow-density-speed relationships | Cell Transmission Model, Gas-Kinetic
4 | Typical Equations | ODEs (ex: IDM, MOBIL) | PDEs (ex: LWR model, Greenshields) | Hybrid (Discrete-time flow models)
5 | Computational Cost | High | Low | Medium
6 | Use Cases | Driver behavior analysis, ITS | Highway flow prediction | Urban transport planning, Toll pricing

## Slide 48
Section 09:
Quiz
Notes: # English
Now we are in Section 1: Overview and Tools.
Let’s quickly see what this lab is about and what tools we’ll use.
# French
Nous voici maintenant à la section 1 : Présentation et outils.
Voyons rapidement en quoi consiste cet atelier et quels outils nous utiliserons.

## Slide 49: 9. Quiz
1. What is the key characteristic of microscopic traffic flow models?
                They consider the collective behavior of traffic flow.
                They analyze the movement of individual vehicles.
                They focus only on road infrastructure.
                They ignore driver behavior.
2. What equation represents the fundamental relationship in macroscopic traffic flow models?
                Q = K.V
                F = m⋅a
                E = mc2
                P = V⋅IP
3. Which of the following is an example of a mesoscopic traffic flow model?
                Lighthill-Whitham-Richards (LWR) model
                Cell Transmission Model (CTM)
                Intelligent Driver Model (IDM)
                Newton’s Law of Motion

## Slide 50: 9. Quiz
4. What is the main limitation of macroscopic traffic flow models?
                They require extensive computational power.
                They do not consider individual vehicle behavior.
                They cannot model speed variations.
                They only work on highways.
5. Which of the following models is commonly used for microscopic traffic simulation?
                Greenshields Model
                LWR Model
                Gipps Car-Following Model
                Cell Transmission Model
6. What does the Lighthill-Whitham-Richards (LWR) model primarily describe?
                The movement of individual vehicles
                The distribution of traffic signals
                The propagation of traffic density waves
                The relationship between lane width and vehicle speed

## Slide 51: 9. Quiz
7. Which traffic flow model best balances computational efficiency and realism?
51
                Macroscopic Models
                Microscopic Models
                Mesoscopic Models
                Random Walk Models
8. According to the Greenshields model, what happens to vehicle speed as density increases?
                Speed remains constant.
                Speed increases linearly.
                Speed decreases linearly.
                Speed becomes unpredictable.
9. What is a common application of mesoscopic traffic models?
                Individual vehicle behavior prediction
                Large-scale highway congestion analysis
                City-wide traffic simulations and dynamic traffic assignment
                Only pedestrian movement modeling

## Slide 52: 9. Quiz
10. In which scenario would a microscopic traffic model be the best choice?
                Simulating traffic at an entire city level
                Designing an individual vehicle’s autonomous driving system
                Estimating daily congestion patterns for a state
                Evaluating fuel consumption trends on highways

## Slide 53: Thank you for your attention!
Notes: # English
Thanks for following along See you in the next session!