## Slide 1: Transport Research and Analysis
Module 4: Sustainable Transport and Policy Analysis
Lab 9: Introduction to Environmental Impact Assessment

## Slide 3: Table of Contents
i
Lab 9: Introduction to Environmental Impact Assessment
Importance of Data Visualization in Transport Research
0. Objective | 1
0.1 Learning Objectives | 2
1. Goals and Relevance of Environmental Impact Assessment (EIA) | 3
1.1 Definition and Purpose of EIA | 4
1.2 Importance of EIA in Infrastructure and Transport Projects | 5
1.3 Regulatory Frameworks and International Standards | 6
1.4 Role of EIA in Sustainable Development | 7
2. Key Environmental Indicators in Transport Projects | 8
2.1 Overview of Environmental Indicators | 9
2.2 Emissions (CO₂, NOₓ, PM2.5, etc.) | 10
2.3 Noise Pollution and Vibrations | 11
2.4 Land Use and Biodiversity Impacts | 12
2.5 Water and Soil Quality | 13
2.6 Visual and Community Impact Assessment | 14
3. Case Studies and Real-World Examples | 15
3.1 Metro Line Expansion in Urban Area – EIA Highlights | 16
3.2 Highway Construction in Protected Areas – Challenges and Outcomes | 18
3.3 Airport Development – Stakeholder Conflict and Resolution in EIAs | 20
3.4 Creating Scatter Plots in Excel | 21
4. Challenges in Conducting EIAs for Transport Projects | 22
4.1 Data Collection and Quality Issues | 23
4.2 Forecasting Future Impacts Accurately | 24
4.3 Balancing Economic and Environmental Objectives | 25
4.4 Stakeholder Engagement and Public Consultation | 26

## Slide 4: Table of Contents
ii
Lab 9: Introduction to Environmental Impact Assessment
Importance of Data Visualization in Transport Research
5. Practical Component – Excel for Emissions | 27
5.1 Introduction to Emission Factor Calculations | 28
5.2 Excel Formula Walkthrough | 29
5.3 Sample Dataset Activity | 30
5.4 Interpretation of Results in the Context of Transport EIAs | 31
5.5 Home Assignment | 32
6. References | 33
6.1 Reference Textbooks & Tutorials | 34

## Slide 5
1
Section 0:
Objective
Sustainable Transport and Policy Analysis

## Slide 6: 0.1 Learning Objectives
2
Section No | Activity | Activity Type | Tools | Activity Done by | Allocated Time (min)
1 | Understand the purpose of Environmental Impact Assessment (EIA) and its role in sustainable transport planning. | Presentation | Slides | Teacher | 20
1 | Identify and evaluate key environmental indicators such as emissions, noise, and land use. | Presentation | Slides | Teacher | 20
2 | Familiarize with major EIA frameworks, laws, and international standards. | Presentation | Slides | Teacher | 15
2 | Analyze real-world case studies to explore EIA challenges and mitigation strategies. | Presentation | Slides | Teacher | 30
2 | Apply Excel tools for emission calculations and derive policy-relevant insights. | Presentation | Excel | Teacher | 45
5 | Home Assignment | Homework | Excel | Students | 120
 | TOTAL |  |  |  | 265
Sustainable Transport and Policy Analysis

## Slide 7
3
Section 01:
Goals and Relevance of Environmental Impact Assessment (EIA)
Sustainable Transport and Policy Analysis

## Slide 8
4
EIA is a structured process to identify, predict, and evaluate the environmental effects of proposed projects before decisions are made.
It helps decision-makers understand potential environmental consequences and integrate mitigation strategies.
Focuses on:
i. Preventing environmental harm
ii. Improving project design
iii. Involving stakeholders early
Sustainable Transport and Policy Analysis
1.1 Definition and Purpose of EIA
1. Goals and Relevance of Environmental Impact Assessment (EIA

## Slide 9: 1. Goals and Relevance of Environmental Impact Assessment (EIA
5
      Transport projects often affect air quality, land use, water resources, and human settlements.
      EIAs help:
      i. Identify direct, indirect, cumulative impacts
      ii. Avoid costly design errors through early analysis
      iii. Secure legal and community approvals
      Promotes efficient use of resources and minimizes delays due to environmental non-compliance.
      Real-World Examples:
      i. EIA prevented a highway from being built through a protected forest in Sri Lanka.
      ii. Metro system in India adjusted tunneling methods due to groundwater impact identified in the EIA.
Sustainable Transport and Policy Analysis
1.2 Importance of EIA in Infrastructure and Transport Projects

## Slide 10
6
      EIAs are mandatory for large projects under many national laws and international agreements.
      Key frameworks:
      i. EU EIA Directive (Directive 2014/52/EU)
      ii. US NEPA (National Environmental Policy Act)
      iii. World Bank & ADB Environmental Safeguards
      EIAs must include:
      i. Baseline studies
      ii. Predicted impacts
      iii. Alternatives analysis
      iv .Public consultations
Transport Research and Analysis
1.3 Regulatory Frameworks and International Standards
1. Goals and Relevance of Environmental Impact Assessment (EIA

## Slide 11
7
      EIA aligns with the UN Sustainable Development Goals (SDGs):
      i. SDG 11 (Sustainable Cities)
      ii. SDG 13 (Climate Action)
      iii. SDG 15 (Life on Land)
      Ensures that growth:
      i. Does not come at the cost of the environment
      ii. Respects social equity and long-term ecological balance
      Encourages use of:
      i. Clean technologies
      ii. Alternative transport modes (public transit, cycling)
      iii. Carbon footprint reduction strategies
Transport Research and Analysis
1.4 Role of EIA in Sustainable Development
1. Goals and Relevance of Environmental Impact Assessment (EIA

## Slide 12
8
Section 02:
Key Environmental Indicators in Transport Projects
Transport Research and Analysis

## Slide 13: 2. Key Environmental Indicators in Transport Projects
9
Indicator Type | Example | Measurement Tool
Air Quality | CO₂, NOₓ | Emission models (e.g., COPERT)
Noise | dB Levels | Sound meters, monitoring stations
Biodiversity | Habitat disruption | GIS & ecological surveys
      Environmental indicators are measurable variables used to assess the impact of a transport project.
Transport Research and Analysis
2.1 Overview of Environmental Indicators

## Slide 14
10
Key Emissions:
i. CO₂ – Climate change (global warming)
ii. NOₓ – Respiratory health, smog formation
iii. PM₂.₅/PM₁₀ – Penetrate lungs, cardiovascular issues
iv. HC & CO – Toxic gases from incomplete combustion
Sources:
i. Vehicle exhaust
ii. Fuel evaporation
iii. Road dust
Transport Research and Analysis
2.2 Emissions
2. Key Environmental Indicators in Transport Projects

## Slide 15
11
Sources:
i. Engine noise, tire-road interaction, horns, railway tracks
Impacts:
i. Stress, sleep disturbance, hearing loss
ii. Disturbance to wildlife
Metrics:
i. Measured in decibels (dB(A))
ii. Time-weighted averages (e.g., Ldn, Leq)
Examples:
i. Noise barriers in highways
ii. Speed limits to reduce engine noise
Transport Research and Analysis
2.3 Noise Pollution and Vibrations
2. Key Environmental Indicators in Transport Projects

## Slide 16
12
Impacts:
i. Land clearing for roads/rails
ii. Fragmentation of habitats and wildlife corridors
iii. Encroachment on protected zones
Indicators:
i. Hectares of forest removed
ii. Number of affected species (IUCN Red List)
Transport Research and Analysis
2.4 Land Use and Biodiversity Impacts
2. Key Environmental Indicators in Transport Projects

## Slide 17
13
Sources:
i. Oil, fuel spills, heavy metals from tires and brakes
ii. Construction sediment
Impacts:
i. Water pollution in rivers/lakes
ii. Soil degradation affecting agriculture
Monitoring
i. Water: BOD, COD, heavy metal concentrations
ii. Soil: pH, lead content, organic matter
Transport Research and Analysis
2.5 Water and Soil Quality
2. Key Environmental Indicators in Transport Projects

## Slide 18
14
Visual Impact:
i. Change in scenic quality (e.g., flyovers in historic cities)
Community Disruption:
i. Relocation, traffic congestion, cultural site disturbance
Tools:
i. Visual simulations
ii. Social surveys
Transport Research and Analysis
2.6 Visual and Community Impact Assessment
2. Key Environmental Indicators in Transport Projects

## Slide 19
15
Section 03:
Case Studies and Real-World Examples
Transport Research and Analysis

## Slide 20: 3. Case Studies and Real-World Examples
16
Urban Metro Line Expansion - Delhi Metro, India (also applicable: Vienna U-Bahn or London Crossrail)
Project Description:
i. Multi-phase underground/overground metro system in a dense urban environment
Key Concerns:
i. Noise and vibration during tunneling
ii. Displacement of informal settlements
iii. Groundwater level disruptions
Mitigation Measures:
i. Vibration-dampening tunnel boring machines
ii. Rehabilitation for displaced communities
iii. Rainwater harvesting and aquifer recharge
Transport Research and Analysis
3.1 Metro Line Expansion in Urban Area – EIA Highlights

## Slide 21: 3. Case Studies and Real-World Examples
17
London Crossrail Project
Focus: Sustainability strategy, reuse of excavated material, emissions reduction and long-term environmental benefits
Transport Research and Analysis
3.1 Metro Line Expansion in Urban Area – EIA Highlights
https://youtu.be/OBfTvWTzl68

## Slide 22
18
Highway Through Ecologically Sensitive Area (Example: Southern Expressway, Sri Lanka or A303 Tunnel near Stonehenge, UK)
Project Description:
i. Highway project designed to improve regional connectivity but cuts through wetlands/forests
EIA Challenges:
i. Deforestation and wildlife corridor interruption and Wetland degradation
ii. Opposition from environmental groups
Outcomes:
i. Changes in Alignment to minimize impact
ii. Wildlife crossings (overpasses and underpasses)
iii. Ongoing environmental monitoring post-construction
Transport Research and Analysis
3.2 Highway Construction in Protected Areas – Challenges and Outcomes
3. Case Studies and Real-World Examples

## Slide 23: 3. Case Studies and Real-World Examples
19
A303 Tunnel near Stonehenge, UK
Focus: Shows how traffic would be diverted underground, reducing intrusion into the heritage landscape. Perfect for highlighting visual and ecological mitigation.
Transport Research and Analysis
3.2 Highway Construction in Protected Areas – Challenges and Outcomes
https://youtu.be/Vexogpfnm9Q

## Slide 24
20
Airport Megaproject and Stakeholder Engagement (Example: Istanbul Airport, Turkey or Heathrow Third Runway, UK)
Project Description:
i. Major international airport project to boost tourism and logistics
Conflict Points:
i. Large-scale deforestation (Istanbul: 6600 hectares), Bird migration path disruption
ii. Community displacement and land acquisition disputes
EIA Process:
i. Multiple revisions due to strong public opposition
ii. Legal action from environmental NGOs
iii. Additional studies and public hearings mandated
Transport Research and Analysis
3.3 Airport Development – Stakeholder Conflict and Resolution in EIAs
3. Case Studies and Real-World Examples

## Slide 25: 3. Case Studies and Real-World Examples
21
Heathrow Third Runway, UK
Focus: Animated visuals of proposed infrastructure paired with public and political dispute coverage, especially regarding environmental implications and community concerns around wildlife, noise, and emissions
Transport Research and Analysis
3.3 Airport Development – Stakeholder Conflict and Resolution in EIAs
https://youtu.be/BPrJxRcMJ9A

## Slide 26
22
Section 04:
Challenges in Conducting EIAs for Transport Projects
Transport Research and Analysis

## Slide 27: 4. Challenges in Conducting EIAs for Transport Projects
23
Problems:
i. Missing or outdated baseline data (air, biodiversity, etc.)
ii. Limited access to accurate traffic/environmental data
iii. Inconsistent formats across sources
Solutions:
i. Use remote sensing, open data, citizen science
ii. Standardize data collection and formats
Transport Research and Analysis
4.1 Data Collection and Quality Issues

## Slide 28
24
Challenges:
i. Long project timelines increase uncertainty
ii. Changing fuel types, regulations, traffic patterns
Risks:
i. Inaccurate predictions → weak mitigation
Solutions:
i. Scenario-based modeling (best/worst case)
ii. Sensitivity analysis in emissions and land-use models
Transport Research and Analysis
4.2 Forecasting Future Impacts Accurately
4. Challenges in Conducting EIAs for Transport Projects

## Slide 29
25
Conflict:
i. Faster, cheaper construction vs. environmental protection
Examples:
i. Route through forests vs. longer detour
ii. Minimal EIA vs. comprehensive review
Approach:
i. Include environmental costs in cost-benefit analysis
ii. Invest in green infrastructure (e.g., EV support, sound barriers with vegetation)
Transport Research and Analysis
4.3 Balancing Economic and Environmental Objectives
4. Challenges in Conducting EIAs for Transport Projects

## Slide 30
26
Issues:
i. Limited participation
ii. Community mistrust
iii. Project delays due to legal or public opposition
Solutions:
i. Engage early with affected groups
ii. Use maps/simulations to explain impacts
iii. Communicate in local languages, accessible formats
Transport Research and Analysis
4.4 Stakeholder Engagement and Public Consultation
4. Challenges in Conducting EIAs for Transport Projects

## Slide 31
27
Section 05:
Practical Component – Excel for Emissions
Transport Research and Analysis

## Slide 32: 5. Practical Component – Excel for Emissions
28
An Emission Factor (EF) is a coefficient that estimates the emissions from a specific activity (e.g., driving 1 km), expressed in grams per kilometer (g/km) or grams per liter (g/L).
Common Equation:
Alternative (Fuel-based) Equation:
Transport Research and Analysis
5.1 Introduction to Emission Factor Calculations

## Slide 33
29
Extra Excel Tips
  i. Use SUM() to find total emissions
ii. Use AVERAGE() to analyze efficiency across vehicle types
iii. Add conditional formatting to highlight high emitters
Vehicle ID | Fuel Consumed (L) | EF (g/L) | Emissions (kg)
F001 | 30 | 2392 | =B2*C2/1000
F002 | 85 | 2640 | =B3*C3/1000
Transport Research and Analysis
5.2 Excel Formula Walkthrough
5. Practical Component – Excel for Emissions

## Slide 34
30
Use the provided dataset (emissions_dataset.csv) to calculate CO₂ emissions from different vehicles based on fuel consumption and emission factors.
Calculate emissions for each vehicle:
  Formula → =D2*E2/1000
Visualize total emissions per vehicle type:
Insert → Pivot Table
Rows: Vehicle Type
Values: Sum of Emissions (kg)
Insert → Pie or Bar Chart
Compare diesel vs petrol emissions using filters or: =SUMIF(C:C, "Diesel", F:F)
Transport Research and Analysis
5.3 Sample Dataset Activity
5. Practical Component – Excel for Emissions

## Slide 35
31
Discussion Questions
i. Which vehicle types contribute the highest CO₂ emissions?
ii. Do diesel engines emit significantly more than petrol?
iii. How much impact do buses or trucks have relative to smaller vehicles?
iv. What happens if these are replaced with electric or hybrid options?
Policy Implications
i. Identify priority areas for emission reduction (e.g., switch bus fleets to electric)
ii. Results can feed into EIA reports to recommend mitigation measures
iii. Supports cost-benefit decisions for adopting cleaner technologies
Extended Activity Ideas
i. Modify the dataset to simulate switching all diesel vehicles to electric
ii. Measure percentage change in total emissions
iii. Prepare a short policy memo or visual dashboard in Excel
Transport Research and Analysis
5.4 Interpretation of Results in the Context of Transport EIAs
5. Practical Component – Excel for Emissions

## Slide 36
32
Define a realistic transport infrastructure scenario
Map five key environmental indicators (e.g., CO₂, noise, biodiversity)
Perform Excel-based emissions analysis with visualizations (transport_emissions_dataset.csv)
Write a professional policy memo with actionable recommendations
Reflect on practical EIA challenges and stakeholder dynamics
Deliverables:
        i. Structured PDF report
        ii. Annotated Excel workbook
        iii. Clear formatting and evidence of critical thinking
Transport Research and Analysis
5.5 Home Assignment
5. Practical Component – Excel for Emissions

## Slide 37
33
Section 06:
References
Transport Research and Analysis

## Slide 38
34
European Union. (2014). Directive 2014/52/EU on the assessment of the effects of certain public and private projects on the environment. Official Journal of the European Union.
https://youtu.be/OBfTvWTzl68
https://youtu.be/Vexogpfnm9Q
https://youtu.be/Vexogpfnm9Q
Transport Research and Analysis
6.1 Reference Textbooks & Tutorials
6. References

## Slide 39: Thank You for Your Attention