## Slide 1: Fundamentals of Transportation
Lecture: Transport and Environment

## Slide 3: Learning objectives
Understand basic definitions and parameters related to transport & environment
Examine traffic emissions, immission, air quality, and climate impacts
Analyze policy frameworks including the European Green Deal and modal shift
Identify mitigation strategies and monitoring indicators for transport emissions

## Slide 4: Lecture outline
Key definitions & parameters
Traffic & environment: emissions, air quality, GHGs
Policy frameworks: EU Green Deal, modal shift, e-mobility
Regional focus: Africa — DRC & Cameroon case studies
Methods, indicators, and recommendations

## Slide 5: Traffic & Environment:
Emission
  any release of pollutants or energy from a source into the environment
According to the Federal Immission Control Act of Germany (BImSchG): "the air pollution, noise, vibrations, light, heat, radiation and similar phenomena emanating from an installation" [§3, Art. 3].
      Measured at the point of release (tailpipe, chimney, fuel evaporation).
      Typically quantified as mass per unit time or mass per kilometer, e.g., g/km, g/s, tons/year
      Used for inventory, modeling, and regulation of polluting sources.

## Slide 6
Immission
  refers to the concentration of emissions on the environment where people, ecosystems, or materials are exposed.
  According to BImSchG: "air pollution, noise, vibrations, light, heat, radiation and similar phenomena affecting humans, animals and plants, the soil, water, the atmosphere and cultural and other material assets" [§3, Art. 2].
      Represent ambient air pollution after emissions disperse, react, or accumulate.
      Measured at receptor points—where humans or ecosystems experience the pollution.
      Expressed as concentration: e.g., µg/m³, ppm
Image source: Federal Office for the Environment, Forests and Landscape 1996
Traffic & Environment:

## Slide 7: Traffic & Environment:
Greenhouse gases and air pollutants
Greenhouse gases
Gases that affect the climate: Retain heat radiation from the earth's surface back into space and thus contribute to the greenhouse effect
Of natural or anthropogenic origin
These include for example carbon dioxide (CO2), methane (CH4) and nitrous oxide (N2O)
Air pollutants
"any substance present in the air that has a harmful effect on human health". health or the environment as whole" (39th BImSchV)
Changes in the natural composition of the air
These include nitrogen oxides (N2O), particulate matter, ozone and carbon monoxide (CO)
Transport emits both greenhouse gases and air pollutants

## Slide 8: Traffic & Environment:
Air quality
Air quality in cities is a global problem
' Air pollutants are identified as highly hazardous to health
The main causes of health problems are particulate matter and nitrogen oxides
(Legally binding) limit values are often exceeded
' This is also the case in many cities in Germany
The right to clean air is enforceable
' Conviction of the Federal Republic of Germany by the ECJ for exceeding the limit values for nitrogen oxide too frequently

## Slide 9: Traffic & Environment:
Air quality: legal basis
Legal framework
EC Air Quality Framework Directive and daughter directives
EC Environmental Noise Directive
Federal Immission Control Act and Ordinance (BImSchG, BImSchV)
Objective
Compliance with immission limits (municipal obligation)
Reduction of greenhouse gas emissions
Realization
Development and implementation of effective action plans
Increased use of traffic management to reduce traffic-related emissions
Integrative view of traffic and environmental management

## Slide 10: Traffic & Environment:
Air Quality Metrics
Describe pollutants in the air that affect human health and local air quality.
typically measured as ambient concentrations (µg/m³ or ppm) at ground level.
    PM₂.₅ (Fine Particulate Matter ≤ 2.5 µm) : Tiny inhalable particles from combustion (vehicles, industry, biomass).
PM₁₀ (Coarse Particulate Matter ≤ 10 µm) :Larger particles from road dust, construction, brake/tire wear.
NOₓ (Nitrogen Oxides: NO + NO₂): Produced by high-temperature combustion in vehicle engines. Strong roadside pollutant, especially in congested urban corridors.
    SO₂ (Sulfur Dioxide), CO (Carbon Monoxide), O₃ (Ground-Level Ozone), and Black Carbon (BC)

## Slide 11: Traffic & Environment:
Climate impact Greenhouse gas emission
measure long-lived greenhouse gases that drive global climate change..
CO₂ (Carbon Dioxide): Primary greenhouse gas from fossil fuel combustion (vehicles, industry) with long atmospheric lifetime (hundreds of years).
CH₄ (Methane) : Strong short-lived greenhouse gas (lifetime ~12 years). It has about 28 times the warming effect of CO₂ over 100 years.
N₂O (Nitrous Oxide) : Very potent, long-lived greenhouse gas (lifetime ~120 years). Emitted from agriculture and some vehicle catalytic converters. It has ~273 times the warming effect of CO₂ over 100 years.
CO₂-eq (GWP100) : “Carbon dioxide equivalent,” calculated using Global Warming Potential over 100 years (GWP100). It converts different GHGs into a common metric.

## Slide 12
Traffic & Environment
Political framework conditions: The European Green Deal
Goal: Sustainable transformation of the EU-wide economy
By 2030: Reduction of net greenhouse gas emissions by at least 55% compared to 1990
By 2050: Reduction of net greenhouse gas emissions to zero
Mobilization of at least one trillion euros to implement the agreement

## Slide 13
Fields of action:
Traffic & Environment
Political framework conditions: The European Green Deal
+ from 2026: Road transport part of the emissions trading system

## Slide 14
Traffic & Environment
Political framework conditions: The European Green Deal
Political framework conditions: Federal Climate Protection Act (KSG)
The amended Climate Protection Act 2021 stipulates a reduction in emissions in the transport sector by by 48% in 2030 compared to 1990.
The German government's Climate Action Program 2030 structures the measures to achieve this goal in six fields of action:
Passenger transport: strengthening the environmental network
Freight transport: shifting transportation to rail and inland waterways
Alternative fuels: biofuels and e-fuels in air, ship and heavy goods transport
Passenger cars: increasing the proportion of electric cars
Commercial vehicles: Trucks with climate-friendly drives
Digital networking: e.g. linking different modes of transport via digital mobility platforms

## Slide 15
Traffic & Environment
Transportation/Traffic Shift
Traffic Shift
= the process towards a sustainable transport system
All three aspects of sustainability must be taken into account:
Ecological sustainability
Social sustainability
Economic sustainability

## Slide 16
Traffic & Environment
Transportation/Traffic Shift
Traffic turnaround
Based on two pillars:
🡪 Avoiding & relocating traffic
Reduction of MIV
Expansion of public transport
Promotion of cycling and walking
Mobility Shift
+
Drive Shift
🡪 Improvement of Drive technologies
Replacing fossil fuels with alternative, climate-neutral fuels, Drive types
Reduction of emissions during
of the driving operation
Own representation; see Agora Verkehrswende and VCD 2021