## Slide 1: Traffic Engineering
Lecture 5.1: Level of Service (LOS) Analysis -Concepts

## Slide 2: Learning objectives
At the end of this lecture, students should be able to:
Define uninterrupted flow facilities and describe their characteristics
Explain the concept of highway capacity and factors affecting it
Define Level of Service (LOS) and interpret LOS grades A–F
Identify the measures of effectiveness (MOEs) for different facilities
Discuss the limitations of LOS as a performance indicator

## Slide 3: Lecture outline
Introduction
Highway Capacity Concept
Level of Service (LOS) Concept
Measures of Effectiveness for LOS
Limitations and Problems of LOS
Basic reference:
Roger P. Roess; Elena S. Prassas; William R. McShane, Traffic Engineering, 5th edition, Pearson, 2019 (Chapter 13, pp 275-284)

## Slide 4: Introduction
Why Study LOS and Capacity?
  Traffic engineers must understand:
  How much traffic a facility can accommodate
  Under what operating conditions can traffic be served
  When congestion begins and how it grows
  Since opportunities to redesign roads occur rarely, engineers must use LOS and capacity tools effectively during design and planning stages.

## Slide 5: Introduction
Uninterrupted Flow Facilities
  Uninterrupted flow exists when traffic is not affected by external controls such as:
    Traffic signals
    STOP signs
    YIELD signs
    At-grade intersections
  Freeways represent uninterrupted flow in its purest form because access is only through ramps.

## Slide 6: Introduction
What Makes Flow “Uninterrupted”?
In uninterrupted flow:
    Vehicles interact mainly with each other
    Congestion is caused by internal vehicle interactions
    No fixed interruptions exist from traffic control devices
    However, congestion can still occur, especially in urban peak hours.
Three facility types operate under uninterrupted flow
    Freeways
    Multilane highways with more than 2 miles or more
    Rural two-lane highways with more than 2 miles or more

## Slide 7: Highway Capacity Concept
The Highway Capacity Manual (HCM)
The U.S. standard for LOS and capacity analysis is the Highway Capacity Manual (HCM).
The German Highway Capacity Manual (HBS)

## Slide 8: Highway Capacity Concept
Definition of Capacity (HCM2000)
    “Capacity is the maximum hourly rate at which persons or vehicles can reasonably be expected to traverse a point or uniform segment under prevailing roadway, traffic, and control conditions.”

## Slide 9: Highway Capacity Concept
The definition contains important concepts:
    Capacity is a maximum hourly rate
    Usually based on the peak 15 minutes of the peak hour
    Capacity may be measured in persons or vehicles
    Capacity depends on prevailing conditions
    Capacity is defined for a point or uniform segment
    Capacity is based on “reasonable expectancy,” not extreme cases

## Slide 10: Highway Capacity Concept
Capacity changes if any of the following changes:
Roadway conditions:
    Number of lanes
    Lane width
    Shoulder width
    Free-flow speed
Traffic conditions:
    Cars vs heavy vehicles
    Buses and recreational vehicles
Control conditions:
    Signal timing (mainly interrupted flow facilities)

## Slide 11: Highway Capacity Concept
Ideal capacity values for uninterrupted flow facilities: (HCM2010)
Examples:
    Freeways: about 2,250–2,400 pc/h/ln
    Multilane highways: about 1,900–2,200 pc/h/ln
    Two-lane highways: about 3,200 pc/h total (both directions)
  These values represent ideal conditions and must be adjusted for real conditions.
Source: Traffic Engineering, 5th edition , (pp: 278)

## Slide 12: Highway Capacity Concept
Free-Flow Speed and Capacity Relationship
For freeways and multilane highways:
    Capacity depends on free-flow speed (FFS)
    Lower FFS → lower capacity
Free-flow speed decreases due to:
    Narrow lanes
    Restricted lateral clearance
    Ramp density (freeways)
    Roadside access density (multilane highways)
    This is why design features strongly affect LOS.

## Slide 13: Level of Service (LOS) Concept
Why Capacity Alone is Not Enough?
A road segment operating at capacity produces poor conditions because:
    No usable gaps in traffic
    Lane changing becomes difficult
    Entering vehicles creates chain reactions
    Traffic disturbances propagate upstream
    Breakdown may occur quickly

## Slide 14: Level of Service (LOS) Concept
What is Level of Service (LOS)?
LOS was introduced in the HCM (1965) as a convenient way to describe the general quality of operation.
LOS uses a letter-grade system:
    A, B, C, D, E, and F
LOS is mainly a communication tool for:
    Engineers
    Decision makers
    General public

## Slide 15: Level of Service (LOS) Concept
What is Level of Service (LOS)?
LOS as a quality measure describing operational conditions in a traffic stream.
LOS is based on service measures such as:
    Speed and travel time
    Freedom to maneuver
    Traffic interruptions
    Comfort and convenience

## Slide 16: Level of Service (LOS) Concept
LOS Grades (A to F)
LOS categories are:
    LOS A: Excellent conditions, free flow
    LOS B: Stable flow with slight restrictions
    LOS C: Stable flow but noticeable interaction
    LOS D: High density, limited maneuvering
    LOS E: Operation at or near capacity
    LOS F: Breakdown flow and unstable operation

## Slide 17: Level of Service (LOS) Concept
LOS A represents:
    Free-flow traffic conditions,
    Very low volumes,
    Vehicles unaffected by the presence of others,
    High freedom to select desired speeds,
    High freedom of maneuver,
    Excellent level of driver comfort and convenience

## Slide 18: Level of Service (LOS) Concept
LOS B represents:
    Speed at or near free-flow speed
    Noticeable presence of other users,
    High freedom to select desired speeds,
    Slight decline in the freedom to maneuver,

## Slide 19: Level of Service (LOS) Concept
LOS C represents:
    Speed at or near free-flow speed
    Freedom to maneuver noticeably restricted,
    The general level of comfort and convenience declines significantly
    Disruption in the traffic stream can result in significant queue and delay,

## Slide 20: Level of Service (LOS) Concept
LOS D represents:
    Speeds begin to decline with increasing flow,
    freedom to maneuver is more restricted
    Drivers experience reductions in physical and psychological comfort.
    Incidents can generate lengthy queues,

## Slide 21: Level of Service (LOS) Concept
LOS E represents:
    Operating at or near the capacity
    Even a minor disruption to the traffic stream can cause a delay
    Maneuverability extremely limited,
    Drivers experience considerable physical and psychological discomfort

## Slide 22: Level of Service (LOS) Concept
LOS E represents:
    Breakdown in vehicle flow
    Queues form quickly behind points if demand exceeds capacity
    Low speeds or even stop-and-go conditions
    The cyclic formations and dissipation of queues are the key characterization of LOS F.

## Slide 23: Measures of Effectiveness for LOS
Measures of Effectiveness Used in HCM2000:
For interrupted flow facilities:
    Signalized intersections: control delay
    STOP-controlled intersections: control delay
    Urban streets: average travel speed
This shows interrupted flow facilities focus on delay-based performance.

## Slide 24: Measures of Effectiveness for LOS
Measures of Effectiveness Used in HCM2000:
For uninterrupted flow facilities:
    Two-lane highways: % time spent following
    Multilane highways: density
    Basic freeway segments: density
    Weaving areas: density
    Ramp junctions: density
Density is the most important indicator for freeway-related LOS.

## Slide 25: Measures of Effectiveness for LOS
Why is density used for Freeways?
Density is a strong indicator for freeways because it reflects:
    Vehicle spacing
    Driver comfort and maneuvering freedom
    Traffic stream stability
As density increases:
    Lane changing becomes difficult
    Drivers feel stress
    Breakdown risk increases
Thus, LOS for freeways is based on density rather than delay.

## Slide 26: Limitations and Problems of LOS
Problems in LOS Interpretation:
    LOS is a step-function scale applied to continuous variables
    The letter grade oversimplifies complex conditions
    LOS may hide important details such as speed, density, and delay values
    LOS comparability varies by location (urban vs rural expectations)
    LOS is not perceived equally everywhere. For example:
          High freeway density may be normal in some big Cities
          The same density may be unacceptable in smaller cities

## Slide 27: Discussion questions?
What subjective LOS do you estimate for the following traffic flows? WHY?
Figure -1
Figure -2
Figure -3

## Slide 28: Additional references
Transportation Research Board (TRB). Highway Capacity Manual, Washington, DC: The National Academies Press, 2010.
https://www.youtube.com/watch?v=V3bEdLs_8pE&t=385s
https://www.sciencedirect.com/science/article/pii/S2352146516305324