## Slide 1: Traffic Engineering
Lecture 5.4: Capacity and Level of Service (LOS) Analysis –3

## Slide 2: Learning objectives
At the end of this lecture, students should be able to:
Identify freeway and multilane highway facility types
Compute LOS using density criteria
Estimate free-flow speed (FFS) for freeway and multilane segments
Adjust flow rates using PHF and heavy vehicle factors
Conduct capacity and LOS analysis using HCM methodology

## Slide 3: Lecture outline
Uninterrupted flow facilities
Freeways
Multilane Highways
Base Speed–Flow Curves
LOS Criteria
Service flow rates and capacity
Determining Free-Flow Speed
Basic reference:
Roger P. Roess; Elena S. Prassas; William R. McShane, Traffic Engineering, 5th edition, Pearson, 2019 (Chapter 13, pp 275-284)

## Slide 4: Determining Free-Flow Speed
Choosing the Correct FFS Curve
Do not interpolate curves.
Use the nearest curve as shown in the table.
  Example: In the previous examples, the free-flow speeds were estimated as 63.8 mi/h for the freeways (example 1) and 43.6 mi/h for the multilane highway (example 2). Determine the correct FFS curves.
  For free-flow speed 63.8 mi/h => FFS curve is 65 mi/h
  For free-flow speed 43.6 mi/h => FFS curve is 45 mi/h

## Slide 5: Calculate Analysis Flow Rate
This step includes the following tasks
  Adjust for PHF
  Adjust for vehicle mix
  Adjust for driver population

## Slide 6: Calculate Analysis Flow Rate
Peak Hour Factor (PHF)
Heavy vehicle adjustment factor (fHV):

## Slide 7: Calculate Analysis Flow Rate
Passenger Car Equivalency (PCE) factor
    Two vehicle classes
      Trucks and Buses (T)
      Recreational vehicles (RVs)
    Passenger equivalence values
      1 Trucks = 2.5 passenger car
      1 RV = 2.0 passenger car
    However, for different terrains, the PCE values will be
      Level terrain: ET = 1.5, ER = 1.2
      Rolling terrain: ET = 2.5, ER = 2.0
      Mountainous terrain: ET = 4.5, ER = 4.0
    Detailed values of PCE are also available for different grades

## Slide 8: Example-3
Consider the following situation: A volume of 2,500 veh/h traverses a section of freeway and contains 15% trucks and 5% RVs. The section in question is a 5% upgrade, 0.75 miles long. What is the equivalent volume in passenger-car equivalents?
Solution:
first determine ET =2.5 and ER = 3.0 from the tables for 5% grade and a 0.75-mile length
The heavy-vehicle adjustment factor is computed as:

## Slide 9: Example-3
Solution:
Hence, the passenger-car equivalent volume is estimated as:
Alternative Method (Direct Application of PCEs)
    The solution can also be found by applying passenger-car equivalents directly:
    Truck PCE: 2500 X 0.15 X2.5 = 938
    RVs PCE : 2500 X 0.05 X 3.0 = 375
    Passenger cars: 2500 X 0.80 X 1.0 = 2000
    Hence, Total PCE = 2000+ 375+ 938= 3,313

## Slide 10: Calculate Analysis Flow Rate
Driver Population Factor (fp)
    The value for fp ranges from 1.0 to 0.85.
    Consider 1.0 for commuter traffic (i.e., familiar road users)
    Unless there is sufficient evidence available, a value of 1.0 is generally used.
    Where future situations are analyzed, and recreational users dominate, a value of 0.85 is suggested.

## Slide 11: Calculate Density and LOS
Density

## Slide 12: Calculate Density and LOS
LOS

## Slide 13: Example-4
A six-lane urban freeway (three lanes in each direction) is on rolling terrain with 11-ft lanes, with obstructions 2 ft from the right edge of the traveled pavement, and 9 ramps within 3 miles upstream and 3 miles downstream of the midpoint of the analysis segment. The traffic stream consists primarily of commuters. A directional weekday peak-hour volume of 2300 veh/h is observed, with 700 vehicles arriving in the most congested 15-minute period. If the traffic stream has 15% large trucks and buses and no recreational vehicles, determine the level of service (LOS).

## Slide 14: Example-4
Given:
    Lane width = 11 ft
    Right-shoulder lateral clearance=2 ft
    Heavy vehicle percentage = 15%
    No. of ramps within 3-mi upstream and downstream =9
    Terrain type = rolling
    Driver population = frequent commuters or familiar users

## Slide 15: Example-4
Solution:
Step 1 — Estimate free-flow speed (FFS)
    For freeway FFS model:
      = 1.9 mi/h ( Lane adjustment for 11-ft)
      = 1.6 mi/h ( Adjustment for Lateral clearance of 2-ft)
      Compute total ramp density (TRD)
          There are 9 ramps within a total length of 3+3=6 miles.
          Hence,
    Accordingly, the appropriate FFS curve is the 65 mi/h curve

## Slide 16: Example-4
Solution:
Step 2 — Determine the flow rate ( )
  Compute Peak Hour Factor (PHF)
  Heavy-vehicle adjustment factor ( )
  use equation

## Slide 17: Example-4
Solution:
Step 2 — Determine the flow rate ( )
  Heavy-vehicle adjustment factor ( )
      However, PT= 0.15, PRV = 0
      For rolling terrain basic freeway segment, ET = 2.5
      Hence,
    Driver population factor for commuters:
  Therefore, Passenger-car equivalent flow rate per lane will be:

## Slide 18: Example-4
Solution:
Step 3 — Determine the Density and LOS
    For a basic freeway segment, LOS is determined primarily by density:
    At this moderate flow, the average speed is close to the free-flow speed; use S=65 mi/h
    Since D=17.6, the facility operates at: LOS =B
    Level of Service (LOS) = B (stable flow with slight restrictions; speeds near free-flow and moderate density).

## Slide 19: Exercise
Example:
Define the following freeway sections as basic, off-ramp (diverging), on-ramp (merging), or weaving.

## Slide 20: Additional references
Transportation Research Board (TRB). Highway Capacity Manual, Washington, DC: The National Academies Press, 2010.
https://www.youtube.com/watch?v=V3bEdLs_8pE&t=385s
https://www.sciencedirect.com/science/article/pii/S2352146516305324